## Slide 1: Piscivore: studying our ocean’s top predators
2023 Abstract Proposal
Jared Figurski
Kelly Benoit-Bird
Brett Hobson
Jared Figurski, Kelly Benoit-Bird, Brett Hobson
George Stern, Aaron Schnittger, Brent Roman, Dennis Klimov
Lonny Lundsten and Brian Schlining

## Slide 2: Predators
Wolves in Yellowstone
(Ripley et al. 2014)
Sea Otters
(Estes et al. 1998)
Ecologically and Economically Important
Notes: The importance of predators and the disproportionate role they play in structuring ecosystems has been well established. Take for example the wolves to Yellowstone and even our local sea otter. They exert strong top down pressure, driving trophic cascades that fundamentally alter the entire ecosystem.

## Slide 3: Question
How can we find rare, diffuse, highly mobile and evasive species in a vast ocean and still sample at a fine enough resolution to understand the factors that underpin their ecology?

## Slide 4: Approach
Piscivore
  LRAUV with cameras
  Lure to attract predators
  Environmental sensors
Survey for predators and prey
Characterizing the habitat
Notes: We proposed Piscivore as the solution. It is an
Piscivore allows as to survey for predators and prey while simultaneously characterizing the habitat.

## Slide 5: Example Piscivore Sampling
Monitoring
  Regular surveys to track changes in species composition
Complementary Tool
  Piscivore targets species that are not sampled easily
  Bio-acoustics, trawl surveys, and eDNA
  Ground-truthing
Exploratory
  Look for rare species
Targeted
  Studies on a targeted species (e.g., habitat assessment)

## Slide 6
Current Machine Learning Applications
Post-processing
  VARS ingestion
  Lonny reviews ROIs within a couple days
  Posts results to Slack
  Data products
Gen 3 camera
  Next week
  Oclea™ CV25 System on Module
  Improved image and low light capability
  Enable edge computing

## Slide 7: Proposed Machine Learning Applications
Onboard (Edge) Detection
  Real-time or near-real-time detection of target species
  Enables communication via wave glider (e.g., acoustic modem or surfacing relay)
Adaptive Sampling
  Vehicle behavior adjusts in response to detections (e.g., initiate habitat characterization)
  Enables targeted eDNA sampling via paired systems (e.g., ESP or Sipper vehicles)
  Accelerate attractor development
eDNA Integration
  Triggered eDNA sampling increases value of genetic data
  Higher chance of obtaining long-stranded DNA (e.g., for stock ID in whales or fish)
Power and Memory Optimization
  Use low-power, low-res scanning mode for routine operation
  Switch to high-res (e.g., 4K) recording only when target species are detected
  Reduces unnecessary high-res footage of empty ocean

## Slide 8: Challenges and Technical Considerations
Quantification Limitations
  Current ML model sub-samples video (e.g., 1 Hz), preventing object tracking
  Hard to tell if detections (ROIs) are the same individual across frames
Potential Solutions
  Use ML to flag sequences where detailed tracking is valuable
  Apply more intensive tracking only to segments with target species (e.g., tuna, salmon)
  Avoid running full tracking on abundant, non-target taxa (e.g., pyrosomes)
  If needed, just run full model on shore