## Slide 1: Deep Ocean Seafloor Mapping at Scales of Meters to Centimeters Using ROVs and AUVs David W. Caress Monterey Bay Aquarium Research Institute
Presentation to US Navy Special Warfare Visitors – 5 August 2015

## Slide 2: MBARI Mapping AUV
200 kHz or 400 kHz Reson 7125 Multibeam Sonar
1-6 or 2-16 kHz Edgetech Chirp Subbottom Profiler
110/410 kHz Edgetech Chirp Sidescan

## Slide 3: MBARI Mapping AUV Capabilities
Sensors
  multibeam
  chirp sidescan
  chirp subbottom profiler
Aided inertial navigation good to 0.05% of distance traveled.
Duration 17.5 hours
Speed 1.5 m/s
  = 5.4 km/hr = 3 knots
50 m altitude  1 m resolution bathymetry
Mission track 70 to 95 km
Rated to 6000 m depth

## Slide 4: Modular Mapping AUV Design
Tail
  Vehicle propulsion and control
  Main vehicle computer
  Communications
  Navigation
Nose
  Batteries & CTD
Midbody
  Mapping Sonar Payload

## Slide 5: Processing Issues Particular to Swath Data Collected Using Underwater Platforms
Vehicle navigation is low precision relative to the lateral resolution of the seafloor mapping data
Vehicle depth derives from pressure measurements
  Deep pressure sensors are less precise vertically than sonars
Tides matter in
every survey
and if the vehicle doesn’t
come back, there are no
data to process….

## Slide 6: Open Source Software for Seafloor Mapping Data Processing
Academic use requires customizable tools and permanent data archiving
Supports dozens of sonars & swath data formats
Funded by NSF (since 1993) & Packard Foundation (since 1998)
Collaboration w/ Dale Chayes (L-DEO), Christian Ferreira (MARUM) and others
Widely used
  2012: Used by at least 41 US and 68 foreign academic institutions, 11 US and 40 foreign government agencies, and 37 companies
  2015: Email forum has 316 active users
  Underlies US/NOAA, US/NSF and German national seafloor mapping data archives

## Slide 8: Patch Test / Bias Parameters: MBeditviz

## Slide 9: Navigation Adjustment: MBnavadjust
Identifies crossing and overlap points
Correlate features in overlapping swaths
Solve for optimal navigation model

## Slide 10: Navigation Adjustment - MBnavadjust
Raw navigation in black
Adjusted navigation in red
<1m precision in AUV navigation relative to itself
Also adjusted to fit to EM300 bathymetry – fixed to GPS frame to ~20 m precision

## Slide 11
200 Successful MBARI Mapping AUV Survey Missions Since 2006…..
  Submarine Canyons: 54
  Seamounts: 13
  Hydrates/Seeps: 20
  Spreading Centers: 54
  Lau Basin: 3
  Offshore fault zones: 29
  Fan systems: 14
  Slumps: 4
  Shipwrecks: 3
  Cable routes: 3
  Dumpsites: 1

## Slide 12
2009 Surveys of
Hydrate Deposits
Offshore British Columbia:
Bullseye Vent

## Slide 13: Bullseye Vent – Cascadia Margin
A
B
C
100 m
D
A
B
C
Material appears to be
missing from depression?
up-turned sides
20 m
blanking - gas?

## Slide 14: MBARI Mapping AUV Fluid explusion on the Beaufort Sea margin, Arctic Ocean Multibeam bathymetry

## Slide 15: Fluid explusion on the Beaufort Sea margin, Arctic Ocean: 110 kHz chirp sidescan mosaic
1-m resolution sidescan laid out on 1-m resolution bathymetry
Amplitude corrections made using 3D grazing angle corrections

## Slide 16
’
Axial
Seamount

## Slide 17
’

## Slide 18
’
Axial
Seamount

## Slide 19: Ocean Imaging Project
Low (2-3 meter) altitude surveys
Topography
  Multibeam sonar: 5-cm lateral-resolution
  Lidar: 1-cm lateral-resolution
Photographic Imagery
  2-mm resolution
Operated on ROV Doc Ricketts or ROV Ventana
Intended for operation from a hover-capable AUV
Lidar
Multibeam Sonar
Cameras
INS
Strobe

## Slide 20: MBARI Low Altitude Survey Tests
Repeated surveys at three sites in Monterey Canyon around 2850 m depth starting in 2012

## Slide 21: MBARI Low Altitude Survey Tests
80-m by 80-m surveys at 2-3 m altitude from ROV Ricketts
5-cm lateral-resolution multibeam bathymetry
1-cm lateral-resolution LIDAR bathymetry
2.5-mm resolution photomosaics

## Slide 22: Ocean Imaging Site 2: Bedforms 5-cm resolution multibeam bathymetry 2-mm resolution photography
50 meters
50 meters
50 cm
50 cm

## Slide 23
ROV Ventana Stereo Camera and Multibeam Sonar Survey:
Ashes Hydrothermal Vent Field, Axial Seamount
5 mm Photomosaic
5 cm Topography Grid
20 meters
20 meters
1 meter
1 meter
1 meter

## Slide 24
Ocean Imaging Survey:
Planned BIN Site at 1850-m Bend in Monterey Canyon
(11 May 2014)
5 meters
5 meters
500 meters
Poorly sorted sediments, no scouring
Scouring around boulders
Fine sediments deposited and reworked into small ripples
Seafloor smooth at 1-cm scale
Photomosaic – 2-mm resolution
Lidar Bathymetry 1-cm resolution
Mapping AUV Bathymetry 1-m resolution

## Slide 25
Example Lidar Bathymetry from Ocean Imaging Site 0: Chemosynthetic Clam Community at 2850 m Depth

## Slide 26
Example Lidar Bathymetry from Ocean Imaging Site 0: Chemosynthetic Clam Community at 2850 m Depth

## Slide 27: Towards a Low-Altitude Survey AUV
Currently defining functional requirements based on use cases
  Platform requirements most driven by difficult terrain
    Carbonate platforms (e.g. Campeche Escarpment)
    Hydrothermal Vent Fields (e.g. Alarcon Rise)
Working with 3DatDepth to develop a wide swath lidar (>=80° FOV)
Proposing to proceed to a Concept Design Review in 2016

## Slide 28
The end…

## Slide 29: Low-Altitude Survey AUV Requirements
~1-cm lateral resolution topography
~2-mm resolution color photography
Surveys repeatable to map change
Cover at least 100-m by 100-m area per day
Operate in complex topography
Orient sensor package normal to seafloor
Depth rated >= 4000 m
Collect lower resolution bathymetry from 20-50 m altitude
Real-time terrain aiding and vision aiding of navigation
Capable of mid-water acoustic and optical imaging missions
Such an AUV is feasible with following characteristics:
  Hover Capable (heave/surge/sway/yaw)
  Lidar + stereo cameras + lights + multibeam + INS + 2 DVL
  Large (larger than Mapping AUV, smaller than ROV Ricketts)