Xeos Systems
www.xeostech.com
support@xeostech.com
( 902 ) 444 – 7650 Voice	Reference:
( 902 ) 444 – 7651 FAX	Apollo_User_Manual.pdf
# Electrical Connections

MCIL6M

1	Apollo GPS TXD	RS232	9600 Baud	8-N-1
2	Apollo Ctrl TXD	RS232	57.6 k Baud	8-N-1
3	Apollo Ctrl RXD	RS232	57.6k Baud	8-N-1
4	GPS	1pps	RS232 levels
5	+V power	12V Nom
6	Ground

# Electrical Specs

( page 46 of the Xeos manual )

Supply Voltage	7 – 30 VDC
Max Current Draw	1.5 Amps – Iridium peak current
Idle Current	4.0 mAmp – Diag & NMEA
  1. mAmp – Diag @ 12 Volts
30 microAmp – Underwater
25 mAmp – GPS
30 mAmp – 30 sec average Iridium current
5.8 mAmp – Bluetooth with Diag @ 12 Volts

# Physical Location for GPS and Iridium

( The following text is verbatim from Apollo User Manual Version 3.2: )

When installing the Apollo there are several factors that can influence performance.

The Apollo’s head should be pointing toward the sky.

Iridium and especially GPS performance may suffer if large angles of the horizon are blocked, such as if the
Apollo is next to a wall.

Do not use conductive material at the top of the Apollo around the glass lens; this will cause the water sensor to fail.
# IMEI Numbers, Serial Numbers and Unlock Codes

300434064407370	226	75120
300434064917380	224	63557
300434064122480	225	40319

# Local RS232 Connection to the Apollo Relay

Connect up a laptop to the Apollo Ctrl TXD, RXD and Ground
Set comms for 57.6 kBaud 8-N-1
Power up the Apollo Relay
To verify if comms are working,
Type:
$ver < cr >
( < cr > = “ Enter “ or “ Return “
A response should come back from the Apollo Relay detailing firmware and hardware versions.
To see a listing of the Apollo Relay configuration:
Type:
$settings < cr >
The “ unlock code “ is listed in the section “ General: “
These codes persist until a restart after a firmware update
( or you can set the unlock code yourself if desired

# Sending and Receiving Iridium Messages

## subscribe to MBARI listserver:

auvsbd@listserver.mbari.org

## Send text from Apollo Relay to MBARI email:

( Xeos manual pg 40 )

( All lines terminated with carriage return, line feed, or both. )

Type:

$sendSBD < cr >
Text which you want to send<cr>
$finished<cr>

Check email to see if the message came through. It may take a few minutes due to satellite coverage.

## Send a file from Apollo Relay to MBARI email:

Create a “ pure “ text file with the contents:

( All lines terminated with carriage return, line feed, or both. )

$sendSBD <cr>
text line one<cr>
text line two<cr>
etc<cr>
$finished<cr>

Use the communication software “send file” option

## Send email to Apollo Relay serial port:

Create a “ pure “ text file with .sbd extension

$unlock < code >	Unlock code of the Apollo Relay
$outPort 1
< file contents goes here >

Send email to:

data@sbd.iridium.com
Subject:	< IMEI Number >	IMEI Number of the Apollo Relay
Attachment:	< filename.sbd >	The .sbd file you created
Body:	empty	Nothing goes in the body of the email

# Strobe Settings
( page 27 of the Xeos manual )

Strobe can flash a maximum of 4 flashes of 50 millisecond duration each.
The period is a maximum of 60 seconds.

Example setting:
$strobe 2 10	Two flashes at 10 second intervals
$strobe 3 5	Three flashes at 5 second intervals

Enabling / Disabling the strobe:
$switch B 1	Enables the strobe
$switch B 0	Disables the strobe

Light Sensor
$switch L 0	Treats environment as always dark
$switch L 1	Turns off strobe in daylight

Flashing underwater:
$StrFlshUw 1	Flashes while underwater
$StrFlshUw 0	No underwater flashing
# Timer Settings
( page 25 of the Xeos manual )
( also check out the “ flow chart “ on page 22 of the Xeos manual )

Timer 0 is normal mode
Timer 1 is start up mode
Timer 2 is alarm mode
Timer 3 is underwater mode
Timer 4 is low battery mode

Examples:

$timer GPS 0 15m	Timer 0 GPS interval 15m
$timer GPS 1 15m	Timer 1 GPS interval 15m
$timer GPS 2 15m	Timer 2 GPS interval 15m
$timer GPS 3 15m	Timer 3 GPS interval 15m
$timer GPS 4 1h	Timer 4 GPS interval 1 h
$timer SBD 0 15m	Timer 0 SBD interval 15m
$timer SBD 1 15m	Timer 1 SBD interval 15m
$timer SBD 2 15m	Timer 2 SBD interval 15m
$timer SBD 3 15m	Timer 3 SBD interval 15m
$timer SBD 4 1h	Timer 4 SBD interval 1 h
# Message Enable Settings

( page 32 of the Xeos manual )

Examples:

$msgenable 0 0	1 message, Timer 0 Short GPS plain text
$msgenable 1 0	1 message, Timer 1 Short GPS plain text
$msgenable 2 0	1 message, Timer 2 Short GPS plain text
$msgenable 3 0	1 message, Timer 3 Short GPS plain text

$msgenable 0 0,1	2 messages, Short GPS plain text
and Long GPS plain text
# Tilt Sensing
( page 31 of the Xeos manual )

Tilt sensor turns off the strobe when the Apollo Relay is not upright. The Relay keeps transmitting while the unit is tilted.

$switch T 1	Turns on tilt sensing

# NMEA Sentences via Iridium

$gNMEA 1	Enables NMEA messages

# Exercises:

Serial port connection
Read settings
Change the strobe interval
Set up the timers
Set up the messages
Verify that MBARI email is receiving the correct messages at the times you set up
Send a text message from MBARI email to the Apollo Relay
Send a text message from the Apollo Relay to MBARI email
Send a file from MBARI email to the Apollo Relay
Send a file from the Apollo Relay to MBARI email