## Slide 1: MBARI-WEC Software And Simulator Andrew Hamilton and Michael Anderson MBARI

## Slide 2: Demo Days Outline
MBARI-WEC Project Overview (Andy)
On-Buoy Software Interactions
  Log-in and Command Line Interactions (Andy)
  ROS2 Features (Michael)
Simulator Interactions
  Installation Overview (Michael)
  Running the Simulator (Andy)
  Coding for the Simulator (Michael)
Summary, Wrap-Up, and Questions

## Slide 3: Persistent Presence
Technology needed:
Vehicles (Capability, Reliability)
Autonomy
Instrumentation
Energy
Communications
Energy Options:
Bring energy along (in batteries).
Collect energy from the environment.

## Slide 4
MBARI Wave-Energy Converter

## Slide 5
MBARI Mooring with
Wind and Solar Collection:
Weight Avg. Power
5000lbs 50W
Wave Power Buoy Prototype
Weight Avg. Power
5000lbs 200W-300W

## Slide 6
Oceanographic WEC
10’ diameter Buoy
200W Average
Regular Deployments

## Slide 7
2023 Deployment - 232 Days

## Slide 9
Some design features
Electro-Hydraulic PTO and Pneumatic Spring
Heave-Cone w/ Trefoil doors
4-Quadrant Power Electronics, 10kW motor/drive.
6kW-Hr On-board Battery
24V Power Supplies and Ethernet Network (instruments)
Linux Control Computer and Cell Connection

## Slide 10
Wave-Energy Conversion Technical Challenges
Reliability and Storm Survivability
  3-5 Million wave cycles per year
  1-2 Million meters of linear travel
  Designed to maximize forces - extreme events

## Slide 11
Simplest approach, PTO force proportional to velocity (RPM)
Control-System Approaches
Piston Extension
Piston Retraction

## Slide 12
Control Opportunity
Make device smaller
Stroke constraint
Increase robustness
Increased energy capture
Control-System Approaches
MPC Simulation Example

## Slide 13
Open Software Interface – Dept of Energy/Open Robotics
Goal: Make the MBARI WEC available to outside researchers
ROS 2
Publish/Subscribe message infrastructure.
Very popular in robotics
Python/C++ Bindings
One user process on Linux controls buoy
Approach: ROS 2 software on buoy Linux computer provides all
telemetry data to user process and allows control of WEC

## Slide 14: Compute and Control Architecture
Linux Computer
Micro-controllers

## Slide 15
Simulation Environment
Goal: Control software can not tell if its running on the real buoy or on the simulator

## Slide 16
Simulation
Gazebo: Open Robotics supported simulation environment.
Provides physics simulation (rigid body dynamics of joined bodies)
Plugin based, designed for new forcings to be added.
  Pneumatic Spring
  Electro-Hydraulic PTO
  Free-surface hydrodynamics
  Flexible tether
Lacked support for added-mass terms!
While running, the ROS interface provided to user software is exactly the same as the real buoy.
Plus, addition information only available in simulation…

## Slide 17
Simulation

## Slide 18: Outside Researchers
Simulation first, then on-buoy operations.
Researchers may be ROS2 beginners, so we’ve tried to make the system approachable. Simplest solutions possible.
Tutorials and examples
Easy access. GitHub Templates, Docker.
Discussion forum.

## Slide 19
Resources – Open Source
https://github.com/osrf/mbari_wec
Documentation

## Slide 20
Resources – Documentation Site
Tutorials
https://osrf.github.io/mbari_wec/

## Slide 21
Resources – Tutorials
hamilton@mbari.org

## Slide 22
MBARI-WEC Project Overview (Andy)
On-Buoy Software Interactions
  Log-in and Command Line Interactions (Andy)
  ROS2 Features (Michael)
Simulator Interactions
  Installation Overview (Michael)
  Running the Simulator (Andy)
  Coding for the Simulator (Michael)
Summary, Wrap-Up, and Questions
Demo Days Outline

## Slide 23: Demo Days Outline
MBARI-WEC Project Overview (Andy)
On-Buoy Software Interactions
  Log-in and Command Line Interactions (Andy)
  ROS2 Features (Michael)
Simulator Interactions
  Installation Overview (Michael)
  Running the Simulator (Andy)
  Coding for the Simulator (Michael)
Summary, Wrap-Up, and Questions

## Slide 24: Demo Days Outline
MBARI-WEC Project Overview (Andy)
On-Buoy Software Interactions
  Log-in and Command Line Interactions (Andy)
  ROS2 Features (Michael)
Simulator Interactions
  Installation Overview (Michael)
  Running the Simulator (Andy)
  Coding for the Simulator (Michael)
Summary, Wrap-Up, and Questions

## Slide 27
Resources – Forum
https://github.com/osrf/mbari_wec/discussions
hamilton@mbari.org
anderson@mbari.org