## Slide 1: Energy Harvesting for the Persistent Presence of Oceanographic Instrumentation Andrew Hamilton MBARI

## Slide 2: Monterey Bay Aquarium Research Institute

## Slide 3: Monterey Bay Aquarium Research Institute - Engineering

## Slide 4: Persistent Presence
Technology needed:
Vehicles (Capability, Reliability)
Autonomy
Instrumentation
Energy
Communications
Energy Options:
Bring energy along (in batteries).
Collect energy from the environment.

## Slide 5
MBARI Wave-Energy Converter

## Slide 6
MBARI Mooring with
Wind and Solar Collection:
Weight Avg. Power
5000lbs 50W
Wave Power Buoy Prototype
Weight Avg. Power
5000lbs 200W-300W

## Slide 7
Oceanographic WEC
10’ diameter Buoy
225W Average
Regular Deployments

## Slide 8
Some design features
Electro-Hydraulic PTO and Pneumatic Spring
Heave-Cone w/ Trefoil doors
4-Quadrant Power Electronics, 10kW motor/drive.
6kW-Hr On-board Battery
24V Power Supplies and Ethernet Network (instruments)
Linux Control Computer and Cell Connection
Regular Deployments

## Slide 9
225 Watts Continuous…
On buoy instrumentation
- Unusual that typical instrumentation requires hundres of watts
- Some exceptions: Imaging Flow CytoBot
Autonomous vehicle re-charge
- Requires docking capabilities
- Fleets of vehicles

## Slide 10: Imaging Flow Cytobot On Wave-Energy Buoy (2022)
Photo: McLane
Intake
Sampling freq: 20-30 mins
Sampling Vol: ~5 ml
Size Range: <10 μm to 150 μm
Image Resolution: ∼ 3.4 pixels/micron
1000s of images generated every hour
~ 190 Gb of images
Over 190 days of Operation
~ 45 Watts
Patrick Daniel (Kudela Lab / UCSC)

## Slide 11: Recent Samples
~ 839 images
General Rule: More smaller things
Too much to look at manually.

## Slide 12: Machine Classifier
51 class CNN (Xception)
100k + manually classified images
Work in progress…
Accuracy (f-1 score) = .93
Confusion Matrix:
True images vs Class Prediction

## Slide 13: Data in Action
Chaetoceros Bloom
Chaetoceros

## Slide 14: Eucampia sp. Bloom
May 2022
source: Kudela Lab
Eucampia zodiacus
Efficient at N-Uptake, can outcompete Nori in farms and cause bleaching

## Slide 15: Eucampia Bloom
Other species abundance == Doesn’t Change
Is Eucampia outcompeting other Diatoms?

## Slide 16
Eucampia Bloom
Santa Cruz Wharf
Power Buoy

## Slide 17: Margalefidinium (Cochlodinium)
Red tide forming - Toxin producing
Present in background since late summer year
Santa Cruz Wharf
Power Buoy

## Slide 19
Wave-Energy Conversion Technical Challenges
Reliability and Storm Survivability
  3-5 Million wave cycles per year
  1-2 Million meters of linear travel
  Designed to maximize forces - extreme events

## Slide 20
System natural period = 2-3 seconds
Simplest approach, PTO force proportional to velocity
Control Opportunity
Make device smaller
Stroke constraint
Increase robustness
Increased energy capture
Control-System Approaches

## Slide 21: Compute and Control Architecture
Linux Computer
Micro-controllers

## Slide 22
Open Software Interface
Goal: Make the MBARI WEC available to outside researchers
Approach: ROS2 software on buoy Linux computer provides all
telemetry data to user process and allows control of WEC
ROS2
Publish/Subscribe message infrastructure.
Very popular in robotics
Python/C++ Bindings
One user process on Linux controls buoy

## Slide 23
Simulation Environment
Goal: Control software can not tell if its running on the on real buoy or on the simulator

## Slide 24
Simulation
Gazebo: Open Robotics supported simulation environment.
Provides physics simulation (rigid body dynamics of joined bodies)
Plugin based, designed for new forcings to be added.
  Pneumatic Spring
  Electro-Hydraulic PTO
  Free-surface hydrodynamics
  Flexible tether
Lacked support for added-mass terms!
While running, the ROS interface provided to user software is exactly the same as the real buoy.
Plus, addition information only available in simulation…

## Slide 25
Simulation

## Slide 26: Outside Researchers
Engagement is perhaps the most challenging part of this project.
We have a few initial possible participants: Sandia National Labs, Oregon State University, JHU/APL. And other candidates…
Simulation first, then on-buoy operations.
These researchers may be ROS2 beginners, so we need to make the system approachable. Simplest solutions possible.
Good tutorials and examples
Easy access. Docker, Cloud based, etc.
Responsive forum.

## Slide 27
Resources – Open Source
https://github.com/osrf/buoy_entrypoint

## Slide 28
Resources – User Guide

## Slide 29
Resources – Tutorials
hamilton@mbari.org

## Slide 30
People:
- Francois Cazenave
- Scott Jensen
- Jon Erickson
- Rich Henthorn
- Eric Martin
- Denis Klimov
- Rob McEwen
- Jose Rosal
- John Ferrierra