## Slide 1
Power Buoy IFCB
Video: Brent Jones
Patrick Daniel
PhD Student
Kudela Lab
Department of Ocean Sciences
UCSC
Nov, 3 2022

## Slide 2: Thank you!
IFCB integration onto the Power Buoy has been an overwhelming success!
Most interesting and highest quality data of the dozen IFCBs in California!
Thanks to the Wave Energy Team!
MBARI IFCB Team:
Francisco
Tom
Denis
Henry (CeNCOOS)
Brent (Wire Walker!)
UCSC IFCB Team:
Raphe Kudela
Kendra Negrey
Jaime Walton (Berkeley)
Anna McGaraghan

## Slide 3: Power Buoy IFCB Quick Facts
Photo: McLane
Intake
Sampling freq: 20-30 mins
Sampling Vol: ~5 ml
Size Range: <10 μm to 150 μm
Image Resolution: ∼ 3.4 pixels/micron
1000s of images generated every hour
~190 Gb of images
Over 190 days of Operation!

## Slide 4: IFCB Theory in 1 minute
Source: McLane
Needle injects particles into sheath fluid, sorts and aligns particles into thin line
Cell passing through quartz Cuvette
Cell passing through a laser
Chl-a fluorescence is detected and
triggers a flash lamp
Image is taken with Camera
Cocholodinium sp.

## Slide 5: Sample from this Morning
~ 839 images
General Rule: More smaller things
Too much to look at manually.

## Slide 6: Classifier
51 class CNN (Xception)
100k + manually classified images
Work in progress…
Accuracy (f-1 score) = .93
Confusion Matrix:
True images vs Class Prediction

## Slide 7: Data in Action
Chaetoceros Bloom
Chaetoceros

## Slide 8: Eucampia sp. Bloom
May 2022
source: Kudela Lab
Eucampia zodiacus
Efficient at N-Uptake, can outcompete Nori in farms and cause bleaching

## Slide 9: Eucampia Bloom
Other species abundance == Doesn’t Change
Is Eucampia outcompeting other Diatoms?

## Slide 10
Eucampia Bloom
Santa Cruz Wharf
Power Buoy

## Slide 11: Margalefidinium (Cochlodinium)
Red tide forming
Toxin producing
Present in background since late summer year
Santa Cruz Wharf
Power Buoy

## Slide 12: A Physical View: Wire Walker
Co-located profiling CTD – Hourly Casts

## Slide 13
Internal Waves

## Slide 14: Density: PSD
At Depth: semi-diurnal variability is greatest
At Surface: Diurnal Variability is greatest

## Slide 15: Fluorescence – Chl-a
contour: 25.4 Isopycnal

## Slide 16: Zoomed Out
Mixed Layer
Low Biomass

## Slide 17
Low Biomass
The Wire Walker confirms what we see with IFCB

## Slide 19
Upwelling/Retention
Particle Tracking: HF Radar
Estimate origins of surface water mass.
Changes in Circulation  Shift in community structure + Biomass
Downwelling/Relaxation
Release Point
Backward Propagation Path

## Slide 20: Any questions?