## Slide 2
Core payload: Seabird CTD/DO/Chl (SeaOwl)/PAR, Up/Down DVL
Config 1, Open ocean science -
  Tall antenna, camera, 10 kHz modem/receive array, Soundscape, camera
  No sonar, no whisker box
Config 2, Open ocean, oil – Santa Barbara
  Tall antenna, camera, 10 kHz modem/receive array, Chelsea UV, camera
  Exchanges Chelsea for Soundscape
  No sonar
Config 3, Under-ice, minimum – Great Lakes and Barrow
  Whiskerbox, C-DUSBL, 10 kHz modem/receive array, 900 kHz, Avi Beacon, short antenna, camera
  Chelsea or soundscape, no sona
  Freshwater in Great Lakes requires removal of camera and addition of 100m foam packs
Config 4, Under-ice, full – Future under-ice mapping
  Whiskerbox, C-DUSBL, 10 kHz modem/receive array, 900 kHz, Avi Beacon, short antenna
  Upward looking Norbit WBMS, INS
  No Chelsea, Soundscape, camera,
Config 5, Seafloor mapping
  Downward looking Norbit WBMS, INS, 10 kHz modem/receive array, Tall antenna, Soundscape
  No Chelsea,, or camera