## Slide 1: 800139 - EyeRIS Remote Imaging System
We are developing a plenoptic (3D), deep-sea imaging methodology for ROVs and AUVs. It will enable quantitative measurement of in situ velocity-fields, deformable surfaces, and particle distributions at scales of millimeters to 10s of centimeters.
By deploying 3D snapshot imaging in the deep-sea, we can enable unprecedented studies of centimeter-scale bio-physical interactions at the core of the ocean food web and global carbon cycle.

## Slide 2: 800139 - EyeRIS Remote Imaging System
We are building a system that integrates state-of-the-art plenoptic (3D) cameras with deep-sea pressure housings, illumination, and real-time data processing. To achieve this we are leveraging MBARI’s unique access to ROVs, AUVs, and in-house expertise in underwater imaging.
In 2020, we plan to design and deploy an AUV-specific version of our plenoptic imaging system (camera, illumination, and computer) on the LRAUV.

## Slide 3: 800139 - EyeRIS Remote Imaging System
A 4000 m rated housing contains the plenoptic (3D) camera and lens, high-speed (24 Gb/s) data interface, and power supplies
Two LED spot lights with 660 nm (red) output illuminate the imaged volume
Mini ROV
EyeRIS camera system
660 nm (red) Illumination

## Slide 4: 800139 - EyeRIS Remote Imaging System
Solmissus swimming through a field of natural particles in the Monterey Bay at 200 m depth
The color in the video codes depth in the scene
We can visualize the motion and deformation of the bell and the acceleration imparted on the fluid in 3D
-70 cm
-75 cm
-65 cm
25 cm

## Slide 5: 800139 - EyeRIS Remote Imaging System
Dimensions
Folded OD : 42 cm
Expanded OD : 85 cm
Length: 89 cm
Weight in air (water): 25 kg (15 kg)
Unfolded
Folded