## Slide 1: A high resolution camera array with integrated edge computing for three-dimensional, sub-millimeter-resolution imaging and real-time processing on autonomous vehicles
Paul Roberts*, Eric Orenstein, Kevin Barnard, Jon Erickson, Denis Klimov, Rich Henthorn, Ben Raanan, Brian Kieft, Brett Hobson, Erik Trauschke, Joost Daniels, Alana Sherman, Henry Ruhl, Kakani Katija
Grant #: 7583
Notes: Shorten title: EyeRIS Remote Imaging System – Enabling 3D in situ
Moore foundation grant number
Thanks to Adam Jones

## Slide 2: Monitoring a Changing Ecosystem
Illustration: David Fierstein © MBARI 2019
Notes: Motivate this work by considering the tools and vehicles needed to monitor an ecosystem
Here’s an example from a recent field program at MBARI to study vertical migration of plankton in 2019
The main point here is that it takes an ensemble of approaches to study these processes in a synoptic way
Despite the great diversity of platforms, aside from ships, only a few can carry imaging systems
Of these approaches consider how many are now taking shape as autonomous vehicles
I've highlighted five unique kinds of vehicles here
  Dorado, fast short duration
  Long range AUV fast and powerful
  Spray glider longer endurance
  Wave Glider
  Sail drone
Key challenge is to design imaging systems that can integrate with these platforms without changing there capabilities.

## Slide 3: Benefits of Imaging Plankton
Who/what is there
How many
Projected size
Proximity to each other
Size and orientation
3D statistics
1 cm
Notes: To motivate the use of imaging on autonomous vehicles, lets start with an in situ image of plankton. Without knowing anything more about the image we can say:
Who/what is there
How many of them are there
If we add scale then we can define:
Projected size
But there is a lot more to this scene, if we add 3D location and scale we can define:
Proximity to other particles / animals
True size and orientation
3D statistics
Many more things!

## Slide 4: Plankton Imaging Tools
Flow cell, Free space, Telecentric, Light sheet, Holographic
Lombard et al. 2019
Camera array
Preserve 3D spatial relationships
In Situ
Camera Arrays

## Slide 5: AyeRIS = Autonomous EyeRIS (Remote Imaging System)
Camera array and strobes integrated in AUV payload
~ 2 liter imaged volume with 50 um resolution
MBARI’s Long-Range AUV
Quantitative
Compact
Large imaged volume
Real-time
Joost Daniels: PI02 Studying flow inside and around deep-sea animals in 2D and 3D using novel imaging techniques

## Slide 6: MBARI’s Tethys Long Range AUV
Mature system: 22,000 hours offshore across 12 vehicles
Long Range/Endurance (weeks)
Collaborative operations (inter-vehicle comms)
Lagrangian observation
Notes: For this work we focused on designing a system to integrate with MBARI’s long range AUV, here’s why

## Slide 7: Camera Array Approach
Enable multiview image processing
Flexible
Cameras and lenses are readily available
Leverage advances in drones and self-driving-cars

## Slide 8: Integration on LRAUV
31 in
12 in
Acrylic
View Port
10x 30,000 lumen
4000k LED strobes
7x Fujinon 23 MP Lenses
6x 16 mm, 1x 8 mm
7x Sony IMX183
20 MP imagers
2x Nvidia Jetson TX2
2x 48 Whr Li-Ion
Controller and strobe
ballast

## Slide 9: Tank Testing
Calibration
Confirm vehicle operations
Ballasting

## Slide 10: Deployment on LRAUV Galene
Over 60 hours in Monterey Bay
Vehicle behaviors
  Circular profiles
  Yoyo transect between waypoints
  Station keeping
  Drifting with the flow
Processing modes
  Local storage of up to 7 TB
  Real-time particle detection and publishing to shore
  Supervised autonomy: object detection and acoustic transmission during mission
Ivan Masmitja : OT05 A reinforcement learning approach for underwater target tracking optimization

## Slide 11: High Resolution Multiview Images
2 cm

## Slide 12: Realtime object detection and 3D Localization
{
bounding_box : [top, left, width, height],
timestamp: unixtime in microseconds, camera_id: 0-6 number of camera region_props: [eccentricity, angle, area]
}
Hexagonal geometry constrains
Epipolar search to equilateral triangles
{
bounding_box : [top, left, width, height],
3d_location: [x, y, z]
timestamp: unixtime in microseconds, camera_id: 0-6 number of camera region_props: [eccentricity, angle, area]
}
Enumerate and Distribute
LRAUV Data Slate
(Realtime)
Particle Logs (at surface)
LRAUV Image transfer (at surface)

## Slide 13: Example regions of interest from nighttime yoyo
0-5 m
50-70 m
110-120 m
10 cm

## Slide 14: Example Particle Distributions
5 m
50 m
110 m

## Slide 15: Future work
Grant #: 7583
Training robust object detection models
  Kakani Katija : IN05 FathomNet: An open-source image database to train artificial intelligence algorithms that help us understand our ocean and its inhabitants
Targeting biological features
  Eric Orenstein : OD13 Autonomous detection and sampling of biological features with the AyeRIS imaging system on an AUV
Real-time 3D particle statistics
  Sending summary statistics of 3D particle distributions to shore within minutes of vehicle surfacing during extended missions
Deeper water versions down to 6000 m