## Slide 2: In Situ 3D methods
Stereo Cameras
Time of Flight /
Lidar
Lightfield
Structured Light
WHOI / MBARI : Mesobot
Massot-Campos et. al 2014
Harbor Branch: Unobtrusive Multi-Static Lidar Imager (2020)
MBARI EyeRIS Remote Imaging System (2021)

## Slide 3: Room for One More?
Quantitative
Compact
Large imaged volume
Object Size
Instrument Size
Flow-through
Telecentric,
holographic
or free space
Camera arrays
Light sheet

## Slide 4: Many excellent tools for imaging plankton
Lombard et al. 2019

## Slide 5: AyeRIS Autonomous Instrument
Camera array and strobes mounted in AUV payload
~ 2 liter imaged volume
7, Sony IMX183, 20 megapixel sensors in hexagonal array,
10, 33,000 lumen strobes in a ring around the cameras
Real-time particle detection and size spectra estimation
Deployed on MBARI’s Long-Range AUV
300 m depth rating version completed and demonstrated
AyeRIS = Autonomous EyeRIS

## Slide 6: Realtime object detection and supervised autonomy
Run an on-board object detector
Collate counts from images
Update vehicle behavior
Human operator confirms behavior change
Enumerate and Distribute
LRAUV Data Slate
(Realtime)
Object Logs (at surface)
LRAUV Image transfer (at surface)
larvacean
larvacean
{
larvacean : 2,
copepod: 0, jelly: 0, aggregate: 0, }
if num_larv > threshold:
stop yoyo
signal partner LRAUV