## Slide 1
Plenoptic and multi-camera imaging on ROVs and AUVs
Paul Roberts, Joost Daniels, Eric Orenstein, Jon Erickson, Denis Klimov, Rich Henthorn, Alana Sherman, Henry Ruhl, Kakani Katija
EyeRIS - Remotely Operated Vehicles
4000 m lightfield camera with real-time 3D visualization
AyeRIS - Autonomous Underwater Vehicles
300 m autonomous camera array with real-time processing
Key Features:
4000 m depth rating
Real-time 3D visualization
Imaged volume: 60 ml to 2 l
Resolution:
  x/y: 20 um to 60 um
  z: 200 um to 600 um
Interface:
  Wide range AC/DC
  < 300 W (with lights)
  Single-mode fiber
Key Features:
300 m / 1500 m depth rating
Real-time object detection
Imaged volume: 2 l to 10 l
Resolution:
  x/y: 50 um
  z: 400 um
Interface:
  24 VDC
  < 25 W (at 1 FPS)
  Gigabit ethernet
Grant #: 7583
Enabling the quantitative study of time-resolved, small-scale (mm to cm) animal-fluid interactions, predator prey dynamics, particle distributions, and plankton abundance through the use of in situ 3D imaging
(left) Focused depth map of a pasiphaeid shrimp as it swims downwards. (Right) Displacement of the tip of one of its protopods during a cycle. This shrimp swam over 90 meters downwards during the recording.
(Left) Focused depth map of an octopus imaged at Octopus Garden on Davidson Seamount in August 2022. (Top) Sequential frames from video of an octopus moving. Video will be used to measure in situ gait dynamics of these deep-sea animals.
(Top) Zoomed in view showing particle trajectories meandering in the wake of the branch.
(Left) Pathline view of flow over an isidella coral branch at Sponge Ridge off Monterey. Lines show the bulk fluid motion and the downstream vortices to the left of the coral are clearly visualized.
An amphipod surfs in the wake of the coral branch
(Right) Map of Monterey Bay showing a transect line between waypoints in the Monterey Bay Time Series. ROIs and particle size data were recorded continuously during the transect and saved to local storage.
(Bottom) Visualization of particle size spectrum slope along the transect between (M2) to near-shore (C1). Size spectra are computed over 10 m depth bins and the slope is estimated for particle sizes in the range 0.8 mm to 8 mm. The plot shows a large patch of relatively flatter size spectrum that intrudes into the shallower water near-shore.
Longitude (deg)
Depth (km)
Size Spectrum Slope
-1.0
-2.0
-1.5
M2
C1
Examples of raw images from AyeRIS and estimated particle size spectrum averaged over 10 m depth depths at three distinct depths in one profile. An overall increase in particle abundance with depth and change in size spectrum slope can be seen.
Midwater Kinematics
Benthic Flow Studies
Benthic Biomechanics
Particle Size Estimation
EyeRIS on SOI SuBastian Aug 2021
Canon f2.8
70-200 zoom lens
3D printed zoom gear drive
Raytrix R26 lightfield camera
Phrontier CWDM CXP 1.0 extender
5-channel CWDM mux
Power Relays
Raspberry Pi Controller
Protopod Motion
Protopod Displacement (mm)
Time(ms)
Camera array
Strobe ballast
Internal batteries
Strobe firing in test tank
AyeRIS on MBARI’s
Long-Range AUV Nov 2021
Scan for Video
Scan for Video
Scan for Video
100
Histogram of Detected Particle Size
Number per Image
Equivalent Spherical Diameter (mm)
10-1
100
101
10-2
10-1
100
101
102
103
104
Histogram of Detected Particle Size
Number per Image
Equivalent Spherical Diameter (mm)
10-1
100
101
10-2
10-1
100
101
102
103
104
Histogram of Detected Particle Size
Number per Image
Equivalent Spherical Diameter (mm)
10-1
100
101
10-2
10-1
100
101
102
103
104