## Slide 1: Supervised autonomy
1st Autonomous Control Loop
?
?
When the vehicle is underwater, we do not know what is going on

## Slide 2: Supervised autonomy
Only when it reach the surface, it is able to send some information at shore
However, the vehicle can stay underwater for more than 24h. For example, conducting a Lagrangian movement to follow a thermal front

## Slide 3: Supervised autonomy
1st Autonomous Control Loop
2nd Supervised Control Loop
Multi-vehicle approach

## Slide 4: Supervised autonomy
1st Autonomous Control Loop
2nd Supervised Control Loop
1st Autonomous Control Loop:
  Fast response time
  Automatic mission change based on in situ measurements
2nd Supervised Control Loop (Human-in-the-loop):
  Real-time human interaction
  Validating (or invalidating) an output
  Fine tune hyperparameters
  Define new missions on the fly

## Slide 5: Supervised autonomy
To create this supervised autonomy system two aspects are key:
1- To have bidirectional communications between the LRAUV and the on shore server while the vehicle is underwater
Hotspot Acoustic Relay system:
Status: we are currently conducting laboratory tests and we expect to do some sea test during the next weeks.

## Slide 6: Supervised autonomy
To create this human-in-the-loop system two aspects are key:
2- To have a great localization/tracking system between vehicles
Studying Reinforcement Learning methods to train an agent to learn the best policy for both tracking and communication purposes:
Trained agent in action
Trained agent result
Tracking performance
Status: we have the first simulation results of a trained agent, which has a better performance than traditional methods (greater accuracy at the beginning of the tracking)