## Slide 1: LRAUV Camera Options
Camera | Lens | Raw FOV at 50 cm in water | 3D FOV at 50 cm in water | Maximum Effective Resolution | Depth of Field (cm) @ 125 um @ 20% | Data Rate (MB/s @ 1 Hz) | Real-time processing on AUV | Integration potential | Power (w TX1)
R42 | Fujinon 12 mm, 12 MP lens 2/3” | 22 x 17 | 22 x 17 | 125 um | 3 cm | 42 | no | Good (USB3), need to confirm global reset access | 9 W
6-camera array (G2 sensor) | Fujinon 12 mm, 12 MP lens 2/3” | 28 x 21 | Min: 16 x 14 Max: 16 x 17 | 31 um | 2D: 18 3D: 9 Min: 3 | Max: 252 Mid: 63 Min: 42 | yes | Poor: no access to global reset, brittle software interface, TX1 only | 17 W
6-camera array (IMX183 sensor) | Fujinon 16 mm, 23 MP lens 1” | 28 x 21 | Min: 16 x 14 Max: 16 x 17 | 51 um | 2D: 18 3D: 9 Min: 3 | Max: 120 Mid: 30 Min: 20 | yes | Great (USB3), best API and access to global reset | 20 W

## Slide 2: PIV Options
Raytrix R42
  Bin sensor 2x to get within USB3 bandwidth limit
  Best case, lightfield engine works as is and resolution is just reduced to ~250 um, this is TBD
  Can get 30 FPS within USB3 bus bandwidth
G2 sensor
  Run all six cameras in 4k at 24 Hz, resolution is ~62 um, vertical FOV 14 cm for 2D, 7 cm for 3D
  Run stereo pair in 4k at 56 Hz, resolution is ~ 62 um, vertical FOV 14 cm for 2D, 11 cm for 3D
IMX183 sensor
  Run cropped and binned 2k FOVs at 30 fps, maintain 3D overlap, ~ 100 um resolution
  Run stereo pair at