## Slide 1
Rover Battery Sphere Block Diagram
Li Batts
10A fuse
Shorting plug
Deck cable
10A fuse
+28V
+28V
TO E-Sphere
1 atm Battery Housing
Bench Power Supply

## Slide 2
Deck Cable 10A fuse has blown 3 times
No other fuse has blown
Li Batts
10A fuse
Shorting plug
Deck cable
10A fuse
+28V
+28V
TO E-Sphere
1 atm Battery Housing
Bench Power Supply

## Slide 3
First episode: on deck of Flyer
Rover still wet and just lifted with crane Li batts dead Shorting plug installed
Li Batts
10A fuse
Shorting plug
Deck cable
10A fuse
+28V
+28V
TO E-Sphere
1 atm Battery Housing
Bench Power Supply

## Slide 4
Second episode: during tank tests
Rover still wet and just lifted with crane Li batts had plenty of capacity Shorting plug installed
Power supply current limited to 4A
Li Batts
10A fuse
Shorting plug
Deck cable
10A fuse
+28V
+28V
TO E-Sphere
1 atm Battery Housing
Bench Power Supply

## Slide 5
Third episode: during tank tests
Rover still wet and just lifted with crane Li batts had plenty of capacity Shorting plug installed
E-sphere disconnected
Li Batts
10A fuse
Shorting plug
Deck cable
10A fuse
+28V
+28V
TO E-Sphere
1 atm Battery Housing
Bench Power Supply

## Slide 6: Other information
Deck cable used with no blown fuse many times in high bay and cold room (for years)
Fuse blew with two different power supplies
When current limit raised to 20A on supply, fuse did not blow when we tried to repeat failure- may be circumstantial
No diode on the deck cable input means current could potentially flow either direction
No shorts were reproducible in deck cable