## Slide 1: Rover Transfer Discussion
Dec 10, 2024

## Slide 2: Export Control Warning
“WARNING - This document contains information whose export is restricted by the Arms Export Control Act (Title 22, U.S.C., Sec 2751, et seq.) [or the Export Administration Act of 1979 (Title 50, U.S.C., App. 2401 et seq.), as amended]. Violations of these export laws are subject to severe civil and/or criminal penalties.”

## Slide 3: Outline
Rover overview
Deployment
  Previous issues
Electrical Overview
Mechanical Overview
Software Overview
Maintenance costs
Data
Other issues

## Slide 4: Rover details
Weights: 3,185 lbs in air, 130 lbs in water (with 250 lb drop weight)
Size: 2.6m long, 1.7 m wide, 1.5 m high
Depth rating : 4000 m
Materials: plastic and Ti
Energy consumed in 1 year of operation- 20 kWhrs (Li primary)

## Slide 5: Benthic Rover Configuration
Respirometer
Chamber
Current Meter
Acoustic
Modem
Video Cameras
Chamber
Rack

## Slide 6: Benthic Rover Configuration
Prop Motors
Argos
Brushes
Battery
Sphere

## Slide 7: Respirometers
Ti Knife edge
Valves
Touch
Pad
Stirrer
Cleaning
Pump

## Slide 8: Benthic Rover Typical Mission
Operational Profile
Transit up current to measurement site
Image measurement area
Insert B-R chambers
Measure O2 for 48hrs
Raise chambers
MBARI

## Slide 9
Raise Chambers – 10 min
Rover Task Cycle
Transit – 5 to 10 min
Current meter cycle – 1 Hr
Dust settle period – 1 to 4 Hrs
Lower Respirometer Chambers – 5 min
Transit camera & Strobe
Stir motors- 10 sec on/ 10 sec off
Read optode-
every 15 min for 1 min
Main Controller On
Main controller wakes up every 15 min, Stir motor controller on continuously
Time
Rover Tasks
Respirometry - 1 to 3 days
Fluorometry camera - 1 min
Chamber cameras and video server - 1 min
Chamber cameras and video server

## Slide 10: Rover Deployment

## Slide 11: Deployment Movies

## Slide 12: Electrical System Overview

## Slide 13: Open System Diagram PDF

## Slide 14: CPU Stack
“Wakey”
PC104 stack
  Real-time clk
  Serial expansion card, 12 port isolated
  TS7200 ARM 9
  Ethernet switch
Separate stirrer controller boards – PIC microprocessors

## Slide 15: Rack Junction boxes
Provide power/comms directly for:
  Rack motor
  Stir motor
  2 optodes (Aanderaa RS232)
  1 pump

## Slide 16: Instruments on Rover
Current Meter- FSI 2DACM
Acoustic Modems – Benthos LF and MF stand alone systems
4 Aanderaa optodes
2 Insight Nova video cameras (“chamber cameras”)
2 prosilica machine vision cameras (“transit” and “fluoro” cameras)
2 seabird pumps
1 aquaflash strobe

## Slide 17: Batteries
Custom packs from Electrochem:
  Li primary
  CSC93DD cells
  4 packs per sphere, each pack 15 V
  10 kWHrs per pack
  Cost for 2 spheres of batteries approx. $20k

## Slide 18
Chart: 
Chart: Percentage of Total Average Power (%)
| Propulsion Motors | Rack Motors | Stir Motors | PC-104 Stack, optode sampling | PC-104 Stack, other activities | Relay Board | Video Server | Chamber Camera | Transit Camera and Strobe | Fluor Camera and Light | Optode | Valve Pump | Current Meter
Avg Pwr (%) | 0.029578 | 0.027066 | 0.26283 | 0.29224 | 0.03004 | 0.031171 | 0.00086567 | 0.0010512 | 0.016451 | 0.014113 | 0.28856 | 0.0042389 | 0.0020186
Total energy available ~20 kWHrs
Lasts about 13 months

## Slide 19: Mechanical System Highlights

## Slide 20: Drive System
Two Separate Drive motors
  BLDC Maxon EC60 400W
  80 N-M torque; 6-8 RPM; 58% eff.
  Oil-filled, Independent compensators
  Gates 1 ¼ sync. Drive belt, 1:1 ratio
  Independent servo controller/amplifier mounted in 1-Atm housing near motor
Tracks
  Endless 18” wide ¼” thick conveyor belt
  Bonded transverse and inside longitudinal lugs
  Low contact pres. (0.1 psi) = low disturbance
    ~150lbs vehicle weight / 1600 sq-in
  Spring energized pre-load
    Two Ti Springs,~ 650N each
  Pressure plate fitted with rock guards
  Drive and idler track wheels built with (6) 1.5” wide wheels to minimize rock capture

## Slide 21: Respirometer and Racks
30cm (12”) dia, 20 cm (8”) high chambers
Mechanism to raise and lower chamber
Foot pad to stop rack
Optodes to measure O2
Stirrer to equalize O2 levels
Three vent valves
Sprayer to clean ID of chamber

## Slide 22: Rack Drive
Servo Controller/amp
In Ti housing
High pressure feed-thru
Into oil comp’d chamber
120 W Maxon Brushless
15:1 Planetary
Carbon/Teflon Seal
3/8-8 Acme
316 SST now
Ti later
Glass ball
Delrin seat
Thrust washers
Floating Nut
-Axial load only
Clear acrylic
Housing with
Oil vent on top
“Torpedo” lock
1.5 cm/sec max speed
1000N max force

## Slide 23: Chambers
Touchdown Switch
- 2” ball end-effecter
- Hall-effect limit switch
Centrifugal Pump
- Pumps into chamber
Through check valve
- Sprayer nozzle manifold
To clean ID of chamber
Aanderra Optodes
1/chamber + 1 ref
6-Port J-box
- Re-enter-able potting
¼” thick Acrylic walls
¾ “ thick top with
Sculpted “drains”
Rack Cart
-Rollers support
overhung load
Teflon-coated Ti knife edge
(3) 7cm dia Vent Valves

## Slide 24: Software

## Slide 25: Control System Overview
Reused basic ESP computer system
Technologic Systems ARM PC-104 stack
Linux 2.4-based kernel
Ruby is primary programming language
  Some utilities written in C, invoked within Ruby scripts
Simple script used for subsystem testing 2006-2008 - inadequate for actual deployments
2G system used since 2009
  Tested and evolved on MARS Aug-Oct 2009
  Improvements made in 2010 for Nov deployment

## Slide 26: 2G Control System
Supervisor - developed first
  Loads mission deployment file and translates into sequence of tasks (behaviors)
  Run behaviors one-at-a-time in separate thread
  ‘Acceptance’ tested 2009-2010
  Listens for messages from the…
Executive - introduced in 2010
  Starts a deployment by invoking the supervisor
  Listens for remote control requests via acoustic modem (status, abort, etc.)
  Automatically run during system startup

## Slide 27: 2G Control System
(1)Executive
(2) Supervisor
messages
(2)invokes
RC messages
plan
file
.
.
.
devices
drivers
behaviors
(3)load
(5)execute
(6)save
Saved
state
(4)load
Executive started at boot time
Executive runs Supervisor, establishes comm channels
Supervisor loads previous state
Supervisor loads plan file, creates behavior sequence
Supervisor runs behaviors one-at-a-time
Supervisor saves state before hibernation
Supervisor requests hibernation from OS

## Slide 28: 2G Control System
Why behaviors?
  Partition the mission process into logical blocks to create tailored mission plans
  Familiar concept (but not layered control)
Other benefits
  Rarely does a change in one behavior have an effect on other behaviors
  Unit-test the heck out of individual behaviors

## Slide 29: Previous Mission Critical Faults
Deployment Date | Ship |  | Problem
January-07 | WF | SE | rack stuck in down position
September-07 | PL | SE | external mission watchdog killing missions
November-07 | PL | SE | motor control comm error caused system abort
January-07 | WF | SE | software problem, uninitialized variable, program did not run
September-07 | WF | EE | stbd motor shut down
September-07 | WF | ME | valve not opening/closing
October-09 | MARS | ME | water in port rack controller housing
November-10 | WF | EE | Stbd Chamber Optode did not communicate
November-10 | WF | ? | Could not communicate with modem

## Slide 30: Cost of Maintenance and deployment
Cost of annual deployment:
  $20k for batteries +
  Ship time +
  Calibrating optodes
Maintenance
  Cost of replacing a mating pair of Ti connectors ~$4k
  Cost of replacing any instrument > $5k