## Slide 1: Capturing Episodic Events in the Deep-Sea Community using a Continuously Monitoring Instrument Suite
Alana Sherman1, Rich Henthorn1, Paul McGill1, Brett Hobson1, Henry Ruhl2, Jacob Ellena1, Ken Smith1
1Monterey Bay Aquarium Research Institute
2National Oceanography Center, University of Southampton

## Slide 2: Capturing Episodic Events
Be in right place at right time
  …or be there all the time
Have adequate sensors to capture event

## Slide 3: Station M: Deep Sea Study Site 23 Years of Time-Series Data
Only 1-2 Visits with a ship each year
Notes: 120 miles off shore, 4000 m water depth, and we are limited to visiting only 1-2 a year so need instruments to monitor the seafloor

## Slide 4: Deep Sea Observatory

## Slide 5: Deep Sea Observatory: Sediment Traps
Sediment Traps:
Each sample bottle is collecting for 10 days
POC Flux (mg C m-2day-1)

## Slide 6: Deep Sea Observatory: Time-Lapse Camera
One image per hour
Images 20 m2 area of sea floor
Particle and Organism Counts

## Slide 7: Pulse Event at St.M

## Slide 8: Benthic Rover
Notes: good temporal resolution always measuring at a undisturbed site

## Slide 9: Benthic Rover
Respirometer Chambers:
  Measures Sediment
  Community Oxygen
  Consumption (SCOC)
  Can Calculate Carbon demand
Transit Camera:
  Takes high-resolution image every
  meter during 10 m transit between
  sites
  Particle count per square meter

## Slide 10: ROV Video Transects
HD Video collected during ROV transect is analyzed using VARS for population counts
Notes: Only conducted when at St.M with ship so one-two datasets per year.

## Slide 11: Salp Event: Spring 2012
3 salps/m2 in 06/2012, 0 salps/m2 in 11/2011
Notes: Carbon export system, salps filter particulate and then deliver it to sea floor.

## Slide 12: Why do we care about a Salp bloom?
Carbon Transport Mechanism
Significant impact on benthic food supply

## Slide 13: Salp Event Measured by Other Instruments

## Slide 14: Sediment Trap Data
600 mab Trap Data
Notes: why use 600m trap?

## Slide 15: Sediment Trap Data
600 mab Trap Data

## Slide 16: Camera Tripod Data
Counts of Salps, Larvaceans, and Siphonophores

## Slide 17: Rover Transit Images

## Slide 18: Rover Oxygen Consumption Rates
Port
Stbd
87 Sites visited by
the Rover between 11/11- 6/12

## Slide 19: Rover Oxygen Consumption Rates
Port
Stbd

## Slide 20: Rover Data: Carbon Demand

## Slide 21: Sediment Trap, Time-Lapse Camera, and Rover Data
Rover
Trap
Camera

## Slide 22: Comparing to Surface Export Flux
Rover Slope (umol O2 l-1 hr -1)
Export flux data provided by Mati Kahru, Scripps Institution of Oceanography
Notes: export flux: sea surface temperature, ocean color, chlorophyll

## Slide 23: Conclusions
Continuously monitoring can capture episodic events
A variety of data forms is required to see a more complete picture of event
Time-series data from the benthos matches well with surface water events
Improving duration and resolution of instruments remains a priority

## Slide 24: Newest St.M Instrument: Sedimentation Event Sensor
Images and measures fluorescence of accumulated sediment every 12 hours
Photo: C. Buchner
Ken Smith and Paul McGill

## Slide 25: Newest Instrument: Sedimentation Event Sensor
Fluorescence (PM Counts)

## Slide 26: Acknowledgements
Team Rover: Ken Smith, Rich Henthorn, Paul McGill, Brett Hobson, Johnny Ferreira, Tom Marion
Mati Kahru, Henry Ruhl, Jake Ellena, Crew and ROV pilots on the R/V Western Flyer, the National Science Foundation, and the Packard Foundation