## Slide 1
Building xFOCE: Open Source Technology
for In Situ Ocean Acidification Research
Plymouth Marine Laboratory
W. Kirkwood
Sr. R&D Engr.

## Slide 2
The Monterey Bay Aquarium Research Institute
http://www.mbari.org
David Packard
Established in 1987
Funded by the
David and Lucile Packard Foundation
Annual budget approx. $37 M
210 Staff
Mission: Science and Engineering
working together to advance ocean science
Not to be confused with MBA – The Monterey Bay Aquarium
MBARI

## Slide 3: Points that explain what’s different
MBARI’s strategic plan requires that we address social relevance, particularly policy and education
MBARI projects are all pre-planned with an end date (a very industrial approach)
A project that reaches the end date has a few options:
1. External funding (very rare - we have a limit)
2. Spin out as a “Center” (also has an end date), requires full external funding
(rare but if you get selected you have total control)
3. Spin out as a company (tough road but encouraged)
4. Give it away to some other place (open source)
5. Ends with no lasting impact (not very graceful – worst case)
MBARI

## Slide 4
Free Air CO2 Enrichment
The question: Why no FACE in the ocean?
The Free Air CO2 Enrichment (FACE) experiments which eventually consisted of some 65 sites around the globe
FACE

## Slide 5: pCO2 & pH Predictions 2100:
1) PreIndustrial:
280 µatm, ~pH=8.2
2) Present Day:
380 µatm, pH= 8.1
3) B2 Scenario:
600 µatm, pH=7.9
4) A1F1 Scenario
950 µatm, pH=7.75
2000 2020 2040 2060 2080 2100
Year
From IPCC 2007
Free Ocean CO2 Enrichment
IPCC

## Slide 6: The Future Ocean
Assessing the Impacts of Ocean Acidification

## Slide 7: OA is a direct result of CO2 emissions
CO2(aq)
H2CO3
HCO3– + H+
CO32– + H+
Carbonic
acid
Bicarbonate
Carbonate
Dissolved
carbon dioxide
Atmospheric
carbon dioxide
CO2
(CO2 + H2O)
CO2(aq)
HCO3-
CO32-
pH
Figure Courtesy of Joannie Kleypas
Chemistry
Notes: Here is the basic process – and this is the only slide with chemistry!
Ocean acidification occurs because each year, about 25% of the CO2 we put into our atmosphere is taken up by the ocean.
Adding CO2 to water forms carbonic acid, which then breaks down into bicarbonate, and can further break down into carbonate
Without going into the chemistry, the end result is that both the CO2 concentration and the bicarbonate concentration INCREASE, while the carbonate and the pH both DECREASE.
So ocean acidification can be thought of as a SUITE of chemical changes

## Slide 8
Early Experiments
MBARI scientists have performed a number of CO2 experiments looking at a number of questions in chemistry, biology, and resource management policy
In Situ CO2

## Slide 9
The pH results from a 3,000m deep CO2 sensing experiments – the inevitability of the tidal cycle. This profoundly affected our design thinking
Not the model for 2100
In Situ CO2

## Slide 10
Beyond Climate
Closed loop pH control in the ocean concept
FACE
Experiments
Concept first published
June 2006
An in situ deep sea cabled observatory experiment looking at the impacts of anthropogenic CO2 and lower pH in the deep ocean

## Slide 11: Supporting Work
Examples of Brewer et. al. lab and in situ work in CO2 studies since 1996
CO2 Sequestration
CO2 Sequestration
and habitat
CO2 Instrumentation
CO2 Equilibrium
CO2 Clahrates
CO2 Mixing
CO2 Development

## Slide 12
1m
2m
0.5m
1m
2m
Control Volume
Emitter Ring
Slide courtesy of Rachel Dunk
Free Ocean CO2 Enrichment Prototype
protoFOCE
Notes: Surrounding this is a 2m diameter ring of 40 vertical emitters

## Slide 13
Acid Reservoir
Acid
H2O
Pumps
Emitter Ring: 40 emitters
5 emitters/section
8 sections
d a function of current regime and chemistry
FOCE Prototype : HCl System
protoFOCE
Notes: A mixture of acid and seawater is pumped from this level through the centre of an 8 port valve and out to the emitter ring.
The section of the ring that the acidified seawater is pumped to is controlled by the valve-vane assembly…..

## Slide 14: The FOCE Prototype
Acid Reservoir
Acid
H2O
Elevator for easy L & R
Eleven pH probes to record field
CTD and ADCP measurements
protoFOCE
Notes: And finally, here is how the schematic relates to the FOCE system prototype. Taking you through the FOCE system from top to bottom…..

## Slide 15: FOCE Prototype: Controls Concept
pH
Time
Ambient seawater pH
Step function input of desired value
Heavily damped system to set pt.
Desired
performance
pH 1
pH 2
pH 3
6<pH<8
Ave pH
Automated quality check or manual over-ride to exclude pH probe(s)
Manual over-ride to set total pump rate
Boxcar Filter
Current Velocity
Data
protoFOCE
Notes: Now for some more detail on the control program.
The 3 pH probes log data every second. To remove noise from the data we applied a box-car filter, that averages the 30 most recent measurements. The smoothed pH values are then passed through a quality filter & average, where if any probe records a pH less than 6 or greater than 8 it is excluded.
In simple terms, the difference between the measured average pH, and the set-point target, then controls the ratio of acid to water.
The current speed input controls the total volume pumped.
The control algorithm used yields a heavily damped, but exponentially responsive system. This was to provide for quick adjustments in current, while minimising bounce under constant current regimes.
As a fail-safe, and because prior to our first trials we quite simply didn’t know how the system would respond, we also had manual over-ride on both control parameters.

## Slide 16: Field Trial: Controls Interface
protoFOCE

## Slide 17: Field Trial: On the Seafloor
First In Situ Full Scale Operational pH FOCE – April 2007
These tests were at about 240 meters and conducted on a single day basis
protoFOCE
Notes: The following pictures were taken using the camera mounted on Ventana.
At the seafloor, the visibility was very poor, and we had a few nerve wracking moments until looming out of the gloom we saw the FOCE frame.
To the RHS of the frame you can see the underwater mateable connector, which is acquired using the manipulator arm on the ROV, and plugged into the front of the ROV.
& finally here’s a nice shot of a ling-cod sitting immediately between two acid emitters.
On the first day of field trials, the current speeds were very low, ranging from no flow to ~ 8cm/s, well below our design remit, and the system did not perform particularly well. However on the 2nd day we were fortunate and had current velocities of 10-20 cm/s, and the system performed very well indeed…..

## Slide 18: Field Trial: Data & pH Control
Problem to be solved
protoFOCE
Notes: In an attempt to minimize the impact of this phenomenon on the feedback control, we re-ran the experiment using only pH probe 1 to control the feedback loop. This is a 10 minute segment of that data, where with the exception of a small negative spike which quickly recovered, the pH was regulated extremely well, within +/- 0.04 units from the set-point.
So what lessons did we learn from these trials, and what are our plans for the next FOCE deployments…..

## Slide 19: HCl - CO2 Hydration Kinetics
HCO3- + H+
H2CO3
CO2(aq)+H2O
H2CO3
HCO3-
CO32- + H+
fast
fast
slow
fast
fast
fast
Reaction Time
Reaction pH
DpH
Formation of an intense cloud of CO2
Mixing and hydration of the excess CO2 to form HCO3-
Initial rapid decrease in pH at injection point
Ambient pH
protoFOCE
Notes: At the point of acid injection, we essentially drive the carbonate system equilibria to the left, and form aqueous CO2. These reactions are all fast. The CO2 enriched parcel of seawater then mixes with ambient seawater – it is now out of equilibrium

## Slide 20: Zeebe & Wolf-Gladrow Model (2001)
Linear differential equation:
d
(
C
O
)
d
2
d
t
=
-
d
C
O
2
1
t
F Appendix C.7:
C
O
+
H
O
2
2
k
+
1
k
-
1
H
C
O
+
H
3
+
-
C
O
+
O
H
2
k
+
4
k
-
4
H
C
O
3
-
-
Note: reaction kinetics are a function of both CO2 and pH.
While, the effect of pressure on the equilibrium constants can be calculated (see Z&W-G appendix A.11), the effect on the reaction kinetics is largely unknown.
e-Folding time
FOCE

## Slide 21
The model yields a highly non-linear curve with very strong pH dependency. The reaction is quasi-autocatalytic in that as pH drops the reaction goes faster. Normal sea water is near the peak and in a very steeply sloping region.
Specific example of the time required for CO2 hydration to occur: the figure illustrates the time for a 0.3 pH offset for deep-sea water at various temperatures and pressures. The result for the e-folding time ranges from about 15 seconds at 25ºC and the surface to 97 seconds at 900m and 4ºC.
Implementing the kinetic model – T and pH dependent
FOCE

## Slide 22
The path to Deep FOCE
A series of small scale experiments
and developments took place…
dpFOCE
Smallest In Situ FOCE to date
Approx. 8”x 8”x 8”
Control Volume

## Slide 23: Analog pH Sensor
Electrical interaction with other instruments and thruster motor.
Too noisy to observe background pH or for precise CO2 control.
pH sensor would go to the ‘rail’ at times
pH sensor
Notes: The new design was able to discern the tidally driven pH signal.
The MARS observatory connection enables ‘real time’ data analysis and experiment control.
In-situ calibration by offset adjustment could be made at the peak of the pH tidal cycle
Note: Vertical bars are in-situ calibration points
Data is intentional offset by 0.25

## Slide 24: Digital pH sensor corrected
pH sensor
Calibration using WOCE Buoys
Notes: The new design was able to discern the tidally driven pH signal.
The MARS observatory connection enables ‘real time’ data analysis and experiment control.
In-situ calibration by offset adjustment could be made at the peak of the pH tidal cycle
Note: Vertical bars are in-situ calibration points
Data is intentional offset by 0.25

## Slide 25: pH sensor
Uncorrected Digital pH plotted against WOCE data
Digital pH sensor from installation showing the KCl buffer normalization as the sensor settles and approaches being asymptotic with the known background
Notes: The new design was able to discern the tidally driven pH signal.
The MARS observatory connection enables ‘real time’ data analysis and experiment control.
In-situ calibration by offset adjustment could be made at the peak of the pH tidal cycle
Note: Vertical bars are in-situ calibration points
Data is intentional offset by 0.25

## Slide 26: Predicted vs In-Situ Corrected
New isolation and digitization demonstrating improved performance
pH sensor

## Slide 27
Performed extensive testing in the tank – 30 days
Simplified Control Algorithm
Ran 24 hour operations
Demonstrated reliable remote operations
Data management system
dpFOCE

## Slide 28
Flotation
Time Delay
Path
pH
pH
pH
pH
CTD
CTD
pCO2
Fans
Fans
pH
Hatch
Time Delay
Path
9 Meters
1m
1m
JBox
JBox
Main CPU
Camera
To MARS
Node
dpFOCE

## Slide 29
Long arms to allow time for CO2 hydration to occur, slow flow rates through the system, sensing of external pH variations and feedback control to set a constant ΔpH offset, and control by a GUI via an ethernet link enabling at-home monitoring and adjustments. Video imaging in real time of the central experiment chamber.
dpFOCE
Our experience with the deep FOCE system at 850m

## Slide 30
The figure below shows a month long offset in pH with compensation for variable flow all by feedback control.
dpFOCE

## Slide 31
Time lapse video used to observe urchin motions and feeding behaviors in elevated CO2 compared with a control section located 20 meters away
First long duration deep biology experiments just completed
– 10/23/2011 using sea urchins
dpFOCE

## Slide 32
Deployed for long term science – 1.4 years
In Situ CO2 upgrades, new biologic inserts, first bio experiment
dpFOCE

## Slide 33
Deep Free Ocean CO2 Enrichment
Solved numerous technical challenges useful for all FOCE units
Operated on a cabled observatory at 900m depth sharing resources
Developed and demonstrated digital pH sensors
Demonstrated long term tele-operation
Demonstrated in situ OA treatment with refillable liquid CO2 system
Open source data management and data analysis tools
Inspiration for next development - xFOCE
dpFOCE

## Slide 34
Why xFOCE?
The problem: A few scientists are misinterpreting our publications and what is required to make a FOCE system work properly. This is the first scientist to call us after he tried to build a FOCE system on his own.
MBARI was contacted and we gave feedback about how to modify the existing hardware and reconfigure it to become a functional FOCE and perform the chemistry correctly.
The scientist did some of it but still didn’t grasp what FOCE is an how to properly set up a system to get meaningful science results as a FOCE system. He refused to manage the chemistry but still called his system FOCE.
It became apparent a resource clearly outlining FOCE would be useful.

## Slide 35
The Real Problem
The chemistry in the ocean is very different than that on land. However the early prototype images and name gave the impression to non-chemists that it could be operated in the same manner and have scientific validity.
The reality is – it could be done but the amount of CO2 required is 1) cost prohibitive, 2) unfriendly to the environment and 3) is prone to the same weaknesses of FACE. So, the choice is to be “mostly” free with just enough structure to perform science for a given researchers work.

## Slide 36: A variety of FOCE units are funded
European FOCE (eFOCE) is currently under engineering testing. This system uses a cable but the CO2 is delivered in bottles to a surface expression. Science begins in early 2013.
Deep FOCE (dpFOCE) is the original FOCE built for multi-science users on a cabled observatory. Science continues.
Coral Prototype FOCE (cpFOCE) is the first tech transfer of FOCE built for multi-science users on the Great Barrier Reef. Solar and wind powered except for the creation of the enriched CO2 water.
Antarctic FOCE (antFOCE) proposal submitted and partially funded. Dr. Donna Roberts and her team successfully obtained the a second grant. Congrats!!

## Slide 37
Basic FOCE technology for OA Science
Chapter 8 focuses on best practices and uses the FOCE as a technology example of how to form a well executed experiment for specific types of studies.
FOCE and EPOCA

## Slide 38
The numbers (barriers) for FOCE
The barriers to entry:
Instrument costs – Dominate!
Access to technical people
The eFOCE team ½ funded and I realize we’ve got a problem for the long haul
eFOCE et al

## Slide 39
Learned some lessons along the way helping others
I’m still not good at getting the Zeebe Wolf-Gladrow model across
It is highly likely each scientist will want to modify the basic FOCE for their own science needs – need some expansion built in for future
Getting in the water early at a reasonable budget will help a lot of future proposal writers
Every FOCE has some core elements that make it a FOCE, without those the science maybe fine but it is not closed loop control of pH
Flexibility is key to success… after the proposal is won the real issues arise that force modifications usually related to the selected site.
MOST IMPORTANT: It is possible to transfer the technology out of MBARI and have an external researcher operate on their own (almost)
Open Source can help xFOCE

## Slide 40: xFOCE Concept of Ops- Cabled
Science interface on shore
CO2 and Enriching process on shore
Air / sea interface managed using buried cable
Capable of supporting 6 to 8 xFOCE units
(4 active pH chg and 4 control)
Depth rating
min - ??
max – 40m ??
Anchored to bottom

## Slide 41: xFOCE Concept of Ops - Non cabled
Science interface on shore
CO2 and Enriching process off shore
Air / sea interface managed using surface expression
Capable of supporting 2 xFOCE units minimum
1 active pH chg and 1 control, 3 active and 3 control desired
Depth rating
max – 40m
Anchored to bottom
Comms by telemetry
Buoy or Platform

## Slide 42: xFOCE Functional Interfaces
CO2
SW Pump
ESW
ESW Distributor
Data Archive
Data Acquisition
Data
Distribution
Console
Instruments
ESW injector(s)
Flow effector(s)
Camera(s)
Control System
Generation
Storage
Distribution/Protection
GUI
Configuration & Control
Monitoring/
Health/Status
Comms
ESW injector(s)
Flow effector(s)
Mixer
Subsea Electronics
Surface
Subsea
Power
Science / Control System
Internet
xFOCE Control
Enriched
Seawater
System
Not to worry… we pre-do this but make it available for those who want to modify the system
House Power
OR

## Slide 43
xFOCE Concept of Controls
What is the minimum that comprises a FOCE system?

## Slide 44
FOCE Unit Instrumentation:
pH Sensor
Thruster
CTDO Sensor
Camera and Light
Flow Meter
FOCE Controller
Power and Comm
Cabling
Ducting
Animal
Restrictor
Anchors
CO2 Enriched Water

## Slide 45
xFOCE Topside System Options Remote Ops
CO2 Mix Electronics
System Control Electronics
Diesel Fuel
Heater
Exhaust used for CO2
Particle Scrubber

## Slide 46
swFOCE
After cpFOCE, eFOCE, and antFOCE being funded we started a new FOCE in Monterey for shallow water - swFOCE. However, it was eFOCE and antFOCE that got me started on the path to xFOCE… swFOCE should be the demonstration of that technology “ belief ”.
Shallow Water FOCE

## Slide 47: Minimum FOCE??

## Slide 48
Potential xFOCE Components
Single or
Multiple Helix
Installation of
Anchor Pins
Epoxied Anchor Pins in Coral
Deadweight Block
Helix Anchor
Trolling Motor
Submersible Bilge Pump
With a basic chamber size of .5 x .5 x 1 m long – what works well enough?
Proven in the field – now part of xFOCE
Trolling motor in testing looks to be a winner currently

## Slide 49: Fabrication Methods
Fastening Angles for Stiffness
Inner Angle
Outer Angle
Use of appropriate materials will maximize light
transmission into the test chamber.
-1/4” Clear Acrylic Panels
-3/16” x 1.5” x 1.5” clear PVC angle used as outside support structure.
-3/16” x1.25” x1.25” clear PVC used inside.
-8-32 x 5/8” screws tapped into inner PVC pieces, 6” Center to Center.
Outer Angle
Wall
Wall
Inner Angle
Clearance
Threaded
xFOCE Reference Material
FABRICATION Note: Drilling holes in plastics, polycarbonate and especially acrylic can be difficult because the drill tends to grab and “dig” into the material. Modify the cutting edge of the drill’s flutes by filing or sanding the cutting edge to a more vertical “scraping” edge (i.e. perpendicular to the surface being cut). Keep it sharp and a very nice hole without breakout on the back surface will result.

## Slide 50
PVC |  | 
Nominal Pipe Size (inches) | Schedule 40 | Schedule 80
1/2 | 358 | 509
3/4 | 289 | 413
1 | 270 | 378
1 1/4 | 221 | 312
1 1/2 | 198 | 282
2 | 166 | 243
2 1/2 | 182 | 255
3 | 158 | 225
4 | 133 | 194
5 | 117 | 173
6 | 106 | 167
8 | 93 | 148
10 | 84 | 140
12 | 79 | 137
Operating Temp (°F) | De-Rating Factor
73 | 1.00
80 | 0.88
90 | 0.75
100 | 0.62
110 | 0.51
120 | 0.40
130 | 0.31
140 | 0.22
PVC - Polyvinyl Chloride
strong and rigid
resistant to a variety of acids and bases
maximum usable temperature 140oF (60oC)
Operating Depth = 40 Meters (~131 ft.)
Maximum Pressure = .444 x Depth (ft.) +14.7 psi  73 psi
Factor of Safety = 2 Therefore 2 x 73 psi = ~146 psi
Low Cost Shallow Water Pressure Housing Case Fabrication
XFOCE Reference Material

## Slide 51: xFOCE Engineering Trades
Color Frequency Wavelength
violet 668–789 THz 380–450 nm
blue 631–668 THz 450–475 nm
cyan 606–630 THz 476–495 nm
green 526–606 THz 495–570 nm
yellow 508–526 THz 570–590 nm
orange 484–508 THz 590–620 nm
red 400–484 THz 620–750 nm
infrared longer than 750 nm
Since these wavelengths penetrate water easier but most plastic materials respond poorly to high freq light the materials selections will focus on this end of the spectrum
The selection of materials will likely transmit this end of the spectrum fairly well but in selection, if required, we would trade attenuation here to maximize shorter frequencies.
Acrylic (vs Polycarbonate) has less attenuation overall and carries much further into the ultraviolet when comparing the blue lines.

## Slide 52: xFOCE Data Reqs.
Health and Status: Ability to query system status from web page (data dependent on sensors included)
Timing Accuracy: Network Time Protocol (NTP) protocol for synchronizing computers
Sample Rates: System will support 10 Hz standard operation
Basic Data Format: Comma delimited string, time stamped
swFOCE: Compatible with the current dpFOCE data streams and SSDS (Shore Side Data System*)
Near real time ground fault monitoring
*SSDS – Open source from MBARI

## Slide 53
Cheap, Reliable, Multi-function Connectors

## Slide 54
Flexible Duct
Sections
CO2 / Seawater Inlets
(Bi-directional)
Test Enclosure
w/Access Hatches
Duct Weighted
Support Blocks
Anchors
Conformable
Sealing Skirt
Support
Frame
Winter Test xFOCE / swFOCE
Critter
Prevention
Target – Develop a FOCE technology that a Biology Lab with 1 to 2 grad students and access to a decent technician could be up and running in 6 months. The dollar target is in trade studies now.
Bent Rebar
Open bottom – as close to natural as possible

## Slide 55
xFOCE / swFOCE Testing
We’ve tested a couple configurations to develop methods for control of erosion, minimizing burrowing animals, periods for maintenance and to minimize costs.
We’re on our third test set because we happen to have some time, but the latest protocol has shown to be very robust in very rough shallow waters (40 feet).

## Slide 56
Getting xFOCE into the hands of Science
First: Create a resource for the general public and researchers
Second: Create an identity that can be recognized – i.e. xFOCE.org

## Slide 57
Build a community, give them tools that are useful, offer a reference design for the new folks but more importantly
Getting xFOCE into the hands of Science

## Slide 58
Soft sediment
6 to 30 m
Support leg
ADCP
pH
ADV
pH
CTDO
Plymouth Marine Lab FOCE Concept
1m long x .5m wide
Exposed seabed experiment area
Timing baffles
(TBD)
Valve box and electrical interconnect
Access via side door
Planar optode option
Stephen Widdecombe visited MBARI to learn about FOCE and how it might be used for his OA research. We built a concept outline that could be the basis of pmlFOCE.
pmlFOCE

## Slide 59
pmlFOCE Surface Support Concept
Soft sediment
Pontoon Platform
Comms to and
from shore
Wind generator
Solar power
Electronics
and energy storage
CO2 enriched fluid sub-system
PML’s site had some new twists, remote site with fairly regular access but not daily… would like extended maintenance possible. Move most of the system topside.
pmlFOCE

## Slide 60
Questions? / Discussion
MBARI’s FOCE efforts are funded by the
David and Lucile Packard Foundation
Acknowledgements:

## Slide 61
Additional Topics of Potential Interest