## Slide 1
CANON LRAUV Water Sampler design options
Preliminary Science Requirements
4 liter samples rapidly acquired and filtered through modules
50 to 100 ml samples (treated with fixative) returned for analysis
Integrate with 3G ESP requirements
Method
Specification of the filter: physical size, material, um size?
Method of post-processing (lab)?
Maximum differential pressure for the type of the sample?
Constant Volume and Rate filtering presents a risk of overpressure and unknown reduction of filtered volume.
Adaptive filtering options:
  Constant Pressure with timeout, record filtered volume and time.
  Reach Pressure and Stop, record filtered volume
  Other?
LRAUV capabilities
Space, 6.5” diameter X 10.0” length at front of Long Nose Section
Buoyancy, package must be neutral (some room for dedicated foam pack)
Power, 14-15 nominal volts @ 2 amps

## Slide 2
CANON LRAUV Water Sampler design options
Preliminary Options
Collection
Gulper type piston and cylinder driven by electrical actuator
Collapsible (IV type) bag filled and emptied by pump
Direct Pump
Sampling
Gulper or pump pushes samples through filter manifold
Gulper or pump fills 50/100 ml syringes or bags manifold
Sample path flushed prior to sampling

## Slide 3
1.5 liter Gulper & Actuator
4.0 liter Gulper & Actuator