## Slide 1: Coordinated Canyon Experiment
BIN Deployment Planning
(DRAFT)
Rev. 2.0 4MAY15 mrc

## Slide 2: BIN Frame Specifications
Frame size 7.2 x 7.2 feet (diagonal 10.15)
Total Air weight is less than 2720 lbs.
Total estimated wet weight is 1000 lbs.

## Slide 3: WF Ship Facilities
Winch for deployment and recovery of the BIN frame – Dynacon CTD winch on 01 deck.
  Maximum static load (limited by deck bolt loading) 2720 lbs.*
    With new 12 bolt (4 at front and rear) mounting plate.
  Dynamic loading is accounted for in the 5x safety margin.
    Dynamic loads will be confirmed before review.
Lift line is 2090 meters of 2SPL 3/8" dia. Spectra 12 strand, tensile strength (new) 13,900 lbs.
  This line breaking strength is close to winch (13,600) and OK for A-Frame (37,589) maximum requirements.
  Weak link can be installed (13,000) if desired.
* From Glosten “Aft Winch Structure Review” Rev. B 26NOV2003

## Slide 4: Deployment Procedure
Attach beacon, release and weak link to the end of the lift line on the CTD winch.
Lift BIN frame from the well deck and lower until first bottom touch.
  Track position with SBL system.
Trigger release.
Recover lift line on CTD winch.
Dive and inspect BIN frame with ROV.
  Attach Aquadopp Profiler mount arm.

## Slide 5: Deployment Illustration

## Slide 6: Recovery Procedure
Deploy line spool with 2090 meters of 3/8” Spectra line.
Dive ROV and move line spool to BIN Frame location.
Attach end of lift line to BIN frame.
Release line spool.
Recover ROV.
Recover line spool and unspool remaining line.
Attach line to CTD winch.
Hoist BIN frame to WF well deck.

## Slide 7: Recovery Illustration

## Slide 8: Questions and Issues
Can we limit the total launch vertical height to fit through the A-Frame?
Can the Sonardyne beacon and Benthos release be co-located without interference?
Bridle recovery after release
  Let free ascend to surface? May lose hardware.
  Other options?
Total BIN Frame and launch hardware MUST be 2720 lbs. or less.
Need to examine strength and accessibility of corner lift points.
  Will Aquadopp mount interfere with recovery on board the WF?