## Slide 1
MBARI-developed mobile communication relay for Wave Glider ASV, with satellite, cell, 802.11 and acoustic links; connects subsea assets with shore
Utilized by multiple MBARI applications, including CCE.
Deployed for weeks at a time
All-weather operation, ~$100/day – replaces crewed ship for many applications
Located BEDs after events, retrieved data acoustically (through >1 meter of sediment)
Provided SIN user console for periodic status check/maintenance, troubleshooting
The Monterey Coordinated Canyon Experiment (CCE) deployed an array of sensors along the axis of Monterey Canyon to characterize the structure, dynamics and frequency of sediment density flows. During deployments spanning 1.5 years, array sensors captured data from sixteen flows in unprecedented detail. CCE utilized several novel technologies developed at MBARI, and we describe some of these in more detail here.
Coordinated Canyon Experiment
Seafloor Instrument Node (SIN): density flow structure, particle size distribution
T. O’Reilly, B. Kieft, M. Chaffey, M. Wolfson-Schwehr, R. Herlien, L. Bird, D. Klimov, C.K. Paull, R. Gwiazda, E. Lundsten, K. Anderson,
the Monterey Coordinated Canyon Experiment Team* (Contact: oreilly@mbari.org)
EP13C-1635: New Technological Developments Provide Deep-sea Sediment Density Flow Insights: Monterey Coordinated Canyon Experiment
Acknowledgements
Technology development generously supported by the David and Lucile Packard Foundation.
We thank the ship crews and ROV pilots of MBARI’s Department of Marine Operations for their technical support.
Wave Glider Hot Spot: low-cost acoustic-RF relay
ROV seafloor mapping: characterize morphological change
MBARI’s low-altitude survey system provides cm-scale topography combined with color photography from both ROV Doc Ricketts and ROV Ventana. This system is operated at 2-3 m altitude and includes a Reson 7125 SeaBat 400 kHz multibeam sonar, a 3DatDepth SL1 subsea lidar, two Prosilica 2.8 Mpixel color stereo cameras with xenon strobes, and a Kearfott SeaDevil INS. The system mapped a roughly 120 m by 100 m area around the 1850 m SIN site four times during CCE, bracketing the 3 sediment transport events that
Homer acoustic beacon
LF acoustic modem
Li batteries
Syntactic foam
Steel ballast
Argos antenna
Benthic Event Detectors (BEDs): sediment density flow frequency, motion dynamics
Accelerometer, gyro, pressure xdcr, CPU, clock, CF card, etc
802.11
Iridium
Cell
Benthos modem on Wave Glider skeg communicates with BED and SIN modems
Deployed at 1850 meters depth, included three ADCPs chirping at three different frequencies, CTD, OBS, transmissometer, current meter, oxygen optode, fluorometer/backscatter sensor, logged data at 10 second intervals or faster. Provided high­resolution measurements of three flow events during three successive deployments over 1.5 years.
*CCE Team MBARI: Charles K Paull, Roberto Gwiazda, Krystal Anderson, Eve Lundsten, Mark Chaffey, Dave Caress, Mike McCann, Larry Bird, Brian Kieft, Jim Barry, Chris Lovera, Johnny Ferrara, Hans Thomas, Monica Wolfson-Schwehr, Denis Klimov, Bob Herlien
NOC: Peter Talling, Esther Sumner, Matthieu Cartigny, Michael Clare, Maria Aspiroz, Will Symons, Jenny Gales Hull: Dan Parsons, Steve Simmons USGS: Katie Maier, Mary McGann, Kurt Rosenberger, Joanne Ferreira , Tom Lorenson OUC: Jingping Xu
Suspended particle size distribution and concentration can be estimated from multi-frequency data, as well as flow velocities
SIN CPU hosts Linux OS, running MBARI SIAM instrument drivers. All instrument data are time-stamped with single master clock and logged to flash card; system clock drift periodically logged for post-recovery correction
CTD/OBS/transmissometer sampled every 2 seconds, all other sensors every 10 seconds
64 KWh Li battery pack (8 spheres) for six months operation before replacement.
Acoustic modem communications to shore through Wave Glider Hot Spot relay enables periodic health and status checks, system maintenance.
Hardware/electrical system designed for high reliability, includes ground fault sensing, fault isolation, redundant power paths.
SIN can be deployed stand-alone or integrated with cabled observatory
Flow event on 1/15/2016 carried 1200 kg SIN 26 m down-canyon
Battery-powered sensor package deployed in sediment, moves down-canyon with density flows, records event onset, duration, acceleration, dynamics, depth
Accelerometer: 0.5 mg resol., ±16g range, @50Hz
Gyro: 0.06 deg/sec resol., 0-5.5 RPS range, @50Hz
Depth: 3 cm resol, 1 m accuracy, @1Hz
Four to six BEDs deployed along canyon axis between 250 and 400 m depth (most active canyon segment)
Engineering/science data retrieved by Wave Glider thru Benthos LF acoustic modem
Battery life depends mostly on acoustic modem use; typically ~100-365 days
Density trimmed (ρ ~2.1), coupled to sediment layer; ballast released after 10-12 months, BED floats to surface
Recorded 24 motion events in 1.5 years, longest transit ~5 km in 27 minutes (3.1 m/s)
11/24/2016: 6 BEDs spanning 4 km of canyon floor moved simultaneously for 3 minutes, including BED on 800 kg frame; suggests dense liquefied sediment layer
Wave Glider Hot Spot is launched and recovered from MBARI’s 32-foot RV Paragon
Galvanic ballast release
passed through the site. Representative data collected in May 2016 from 2.5-m altitude are shown below. During 2018, the system will survey deepwater sponge and coral communities on Sur Ridge, hydrothermal venting in the Pescadero Basin of the Gulf of California, and active faulting offshore of Southern California.
multibeam – 5 cm
lidar – 1 cm
photomosaic – 2 mm