## Slide 1: Technical background Sabertooth
Jan Siesjö
Chief Engineer
Saab Seaeye Ltd
jan.siesjo@saabgroup.com

## Slide 2
SUBROV
SABERTOOTH
COUGAR XTi
COMMERCIAL IN CONFIDENCE
LEOPARD
PANTHER XT PLUS
Merging the best of Defence & Commercial
SEA OWL XTi

## Slide 3: Seaeye Sabertooth New combination of existing technology
Double Eagle SAROV
Sabertooth
SUBROV
Seaeye WROV
The development of Seaeye Sabertooth has been distinguished by the use of existing reliable technology and components from the Seaeye range of commercial ROV’s and the use of defense technology to significantly increase the functionality of the system providing the Sabertooth with capabilities of an AUV and a ROV
SAROV 2005
SUBROV 2009
Sabertooth 2011

## Slide 4: Sabertooth Programme Design and benefits
The Sabertooth system is designed for:
  Remote inspection and intervention without the need for a supporting ship
  Operation as either an ROV or AUV
  Long term, subsea, deployment without the need for maintenance
  Autonomous surveys and transit between work sites
The main benefits of this are:
  Cost reductions - reduced ship time
  Access to installations that cannot be reached with ships due to ice or weather conditions
  Small footprint
  Faster response and mobilization time
  Compatible with conventional ROV tools and sensors
  Option to work as a battery powered ROV using a fiber optic umbilical giving it extremely long range (>20km)

## Slide 5: Specifications
Can operate in full 6 Degrees of Freedom
Depth rating 3,000 m
Length 3.7 m Height .45 m Width 1.2 m
Launch weight 1250 kg
Forward speed 4 knots
Thrust Forward 150 kgf Lateral 90 kgf Vertical 160 kgf
Battery capacity 20 kWh (30 kWh option)
Endurance 10-20 hours
Range 50 km
Payload 80 kg

## Slide 6: Launch and Recovery options

## Slide 7: LARS
Same as normal ROV launch and recovery
Docking performed usin optical coms (10-100 m range)
Guiding using acoustic coms
Positioning using INS/DVL and USBL/LBL
Options for heave comp snubber etc to high sea states

## Slide 8: Customized

## Slide 9: Launch and Retrieval Hook
Demonstrated
Uses towed line with float
Used on smaller ships and minehunters
Stabilisation cone can be added to crane

## Slide 10: Double Eagle MKIII Version

## Slide 11: Slide based launch and recovery
Proven, used for torpedo shaped AUVs
Requires suitable ship layout
More restrictions on sensor/tool integration
Better than crane, not as good as garage with respect to sea state

## Slide 12: Launch and recovery A-frame

## Slide 13: Launch and recovery latching
Inverted ”protection”
Same principle used for handling of Double Eagle systems and TPS
Enables hydrodynamic properties of ROV to be retained

## Slide 14: Positioning enhancement including USBL/LBL aiding

## Slide 15: Positioning Transponder/Communication
Kongsberg HiPAP, HPR
Nautronics
Trackpoint
LinkQuest
Etc… all better on paper
Shallow water challenging
Sonardyne
100-900 bps
4000 m range?
Sonar bells
Feature recognition

## Slide 16: Hull cleaning
LBL Navigation
MEMS AHRS
DVL
Navigation sonar
Visual tracking

## Slide 17
    Increasing Trajectory Accuracy
During missions the INS will be aided by the DVL (Doppler Velocity Log), Sparse LBL, and depth and altimeter sensors. Although these sensors minimize AUV drift, the resulting trajectory data is however not sufficient for the required pipeline inspection analyses, such as OOS-analyses.
Navigation in post will use all available sensor information to get optimal navigation accuracy. Navigation in post can iterate solution schemes and go backwards in time in order to improve the navigation accuracy. Navigation in post also has the advantage of not risking the operation if something goes wrong with the algorithm. Post processing will take advantage of:
  Recorded raw navigation sensor data in so-called forward/backward processing
  Landmarks data
The increased accurate trajectory will finally be used in the survey data analysis and reporting.
    Increasing Trajectory Accuracy
Landmark detection and database

## Slide 18: Communication/tether options including
Wifi
Acoustics
Optical
Satellite
Gateway buoy
Vehicle mission monitoring (including sensor data snippet transmission)

## Slide 19: Radio based communication
WiFi (Standard)
  Range ~300-400 m
  1-10 Mb bandwidth
  Surface only
Radio (Option)
  2-3 km range
  10-100 kb
Gateway bouy
  Radio or WiFi
  Acoustic coms
  Optical com (USV)
  Positioning
Sattelite
  Data packets

## Slide 20: Proposed Sabertooth/USV touchdown monitoring
Acoustic tracking system
Propelled Sabertooth garage with optical/acoustic communication
USV
Optical/acoustic communication pod
Sabertooth AUVs

## Slide 21: Sabertooth Communication options
Acoustic modem
Free space optics
Electromagnetic (RF)
Reusable 12 km 3 mm fibre tether
Disposable 20 km fibre tether
Power & fibre tether

## Slide 22: Operational system

## Slide 23: Power/Tether options
Battery can fill in for high power bursts
11 mm neutrally buoyant tether (2kV AC 800 Hz)
  ATC-FC winch
  Maximum length 1000-1200 m
  Maximum power 12 kW (15 peak). 8-9 with SeaOwl Xti transformer
17 mm slightly negative tether (~300-400 VDC)
  Std winch
  Maximum length 250 m?
  Maximum Power 10 kW

## Slide 24: Optical Communication
10-150 m range
10 m Daylight
High bandwidth 10 Mb
Not dependent on visual range
Clear water with particles is no problem

## Slide 25: Hammerfest trials
Link to ENI Norway produced video: http://vimeo.com/77780772

## Slide 30: Tooling and sensor integration

## Slide 31: Sabertooth Survey Demo
Edgetech 2200 combined SSS and SBP
  Simultaneous dual frequency SSS: 230/850 kHz
  2-16kHz chirp SBP
BlueView M900-2250 (dual frequency, 900kH and 2.25MHz), 130 degrees field of view imaging sonar
Tritech parametric sub bottom profiler
R2Sonic 2024 MBES with external SVP for SV compensation
Phins III INS with RDI DVL
AXIS industrial grade HD IP camera
QINSy data logging

## Slide 32: Manipulator skid
Very similar to other Seaeye ROVS
Sabertooth has similar thrust as Cougar Xti (New version of SM 7 thrusters)
Same interfaces
Increases drag
Manipulator_SabertoothDH.pdf

## Slide 33: Sabertooth Tooling examples
Rotating torque tool (class 1-4)
  Loads on the valve is limited by a number of design features:
    Small weight and size
    Neutrally buoyant
    Balancing thrust from the AUV
    Flexible joint
Tool skids
  On board power
  Same principles used for communication and power transfer as vehicle platform
  Tool skids can work independent of vehicle platform
  Docking stations provide:-
    Recharge
    Multi-unit stowage
    Protection
    In field distribution

## Slide 34: Endurance / Performance Increased capabilities

## Slide 35: CFD Analysis

## Slide 36: Sabertooth based high speed Survey
4 knots
700 m ROV depth
1.4 ton tow force
800 m offset
1500 m umbilical
Acoustic tracking system
Sabertooth X4

## Slide 37: Homing and tracking

## Slide 38: Data harvesting
Sonar
Sonar Bell
Sensor
Sabertooth DH
Inductive com.
Inductive power

## Slide 39: Data harvesting
Navigation, homing and docking: The Sabertooth will autonomously navigate to a known sensor location. At this point it will search for and relocate the sensor (marked by a Sonarbell). It will then home in and either do a flyby and retrieve data wirelessly or physically dock to the sensor platform and initiate data transfer as well as do a power transfer (recharge of the sensor).

## Slide 40: Data harvesting
Power transfer: A couple of different alternatives to inductive power transfer will be evaluated.
Inductive communication: Useful range and behavior of a WFS inductive communication system will be tested and evaluated on the Sabertooth. This will be done in both lake and real sea conditions.

## Slide 46: CAD/CAC

## Slide 47: Automatic route planning
Illustration of the route planning algorithm for MLO identification. The MLO result is grinded based on the MLO density. Based on the density grid an optimal route for Mine Identification is automatically generated.

## Slide 48: Commercial ROVs
Sea Owl Xti
Leopard Xti
Station keeping
Click navigation
DVL and MEMS based
USV Operation

## Slide 52: Road Map Presentation
Auto Target Recognition
Replanning and Adaptive Mission Control
Under Ice Applications
Long Term Resident Application

## Slide 53: CLEAN-SEA – Project Demonstration Test Phase II
CLEAN-SEA (Continuous Long-term Environmental and Asset integrity monitoring at SEA) is the concept of an innovative robotic system for environmental monitoring tasks around oil&gas installations by means of a commercial hovering AUV properly upgraded with key enabling technologies. The concept is based on a custom-designed mission payload arranged in modular and interchangeable pods to be loaded on the AUV
Environmental monitoring tasks, during all phases of the field development
General oil spill detection tasks (pre-planned paths, along flowlines, around SPS template and manifolds, verification of occurrence of situations for which mobilization of a ROV vessel is required)
Detection and localization of hydrocarbon leakages from flowlines
visual inspection tasks of SPS structures sauch as ROV panels on manifolds or similar

## Slide 54: Leakage detection mission Courtesy of Tecnomare
The mission is carried by a Sabertooth equipped with a chemical (Franatec) and acoustic (Customised AUV version of Colmar ALD) leakage sensors
Succsessively refined search patterns are executed by the Sabertooth
The location and pattern spacing is transmitted from the search algorithm in the leakage detection pod
In the final stage the precise location of the leak can be pinpointed

## Slide 55: Sabertooth Docking Station & Charging
Secure stowing place.
Power and communication interface
Non Galvanic charging, data up and download
Storage for new tools and payloads
Control module with the following functions:
  Power transformer/switching
  Ethernet switch
  Interface to the through water communication network

## Slide 56
Sabertooth garage

## Slide 57: Seaeye Sabertooth Docking Station
Non Galvanic charging, data up and download
Secure stowing place.
Allows for new tools and payloads
Power and communication interface
Control module with the following functions:
  Power transformer/switching
  Ethernet switch
  Interface to optical and acoustic communication antennas and network

## Slide 58: LARS/Resident
Installation
  Mudmat
  Structure
Docking aided by vehicle
Tool packs cradle on top
Tool skids
  On board power
  Same principles used for communication and power transfer as vehicle platform
  Tool skids can work independent of vehicle platform
  Docking stations provide:-
    Recharge
    Multi-unit stowage
    Protection
    In field distribution

## Slide 59
This is Ice Management
AUV
UAV
Ice Management.wmv

## Slide 60: Under ice operation

## Slide 61: Sabertooth and AUV 62
AUV systems perform remote
  Underwater survey
  2D/3D mapping of ice bergs/floes from below
  inspection
  intervention
  without the need for a supporting ship
Company Confidential

## Slide 63: Saab Test Site
Test platform with work space and hoist and lift facilities
Harbour
Test area:
8-15 m deep
Flat sand bottom
400 m
Docking and “work” site placed near platform

## Slide 64: Trials and verifications
2011 Basic AUV and ROV functionality (Waypoint navigation, obstacle avoidance etc)
2012 Basic sensor interaction, autonomous homing and docking (Environmental monitoring and data harvesting)
2013 Advanced sensor interaction, homing to structures, 3D navigation and optical communication

## Slide 65
Navigation
  IMU/DVL
  Passive nodes/landmarks for local navigation (Sonarbells)
  Obstacle avoidance
  Sonar/DVL for full 3D navigation relative to terrain or a structure
  Sonar homing to structures
Sabertooth Navigation tests

## Slide 66
Commercial ROV Range
50kg
GBP 100k
1,500kg
GBP +2,000k
Falcon
Tiger
Lynx
Cougar XT
Cougar XTi
Panther XT
Panther XT Plus
Jaguar
Observation & Inspection
Inspection & Light Work
Survey & Light Work
Survey and Medium Work
SeaOwl
Leopard