## Slide 1: Seafloor Mapping and Imaging Efforts Using Autonomous Underwater Vehicles
Eric J. Martin
Hans Thomas, David W. Caress, Brett W. Hobson
Monterey Bay Aquarium Research Institute
UUST 2013 August 14th, 2013

## Slide 2: Overview
Brief history of AUVs at MBARI
AUV Technical Capabilities
Mapping Configurations
Imaging Configurations
Mapping Efforts
Next Steps

## Slide 3: Brief History of the Dorado Class
2000: Design commenced of a 21” Diameter Vehicle.
2003: Science operations begin with a vehicle measuring water properties. Development of a mapping vehicle begins.
2006: The mapping vehicle begins survey operations, named the D. Allan B.
Since, the vehicle has completed over 165 successful survey missions.

## Slide 4: The D. Allan B. Mapping AUV

## Slide 5: General Vehicle Design
21” Cylindrical Body Varying 12’-20’ Length Based on Gertler 38 Body
Free flooded faired skin
Modular Section Design
17 Hours Typical Operation
  2x 5kW Li-Ion Battery Payload.
Depth Rated to 6,000 Meters in Seawater
    Operations as deep as 4,000m currently.

## Slide 6: Navigation Assets
Paroscientific Digiquartz Pressure Sensor
GPS Receiver
Sonardyne Tracking Wideband USBL Tracking Beacon
Kearfott SeaDeViL Inertial Navigation System
  Self contained ring laser gyro & Doppler velocity logger.
  Integrates previous sensors in aiding to perform with < 0.05% error over distance traveled.

## Slide 7: Control & Communication
Communication Assets:
  Iridium Satellite Short Burst Data
  Freewave® Wireless Data Radio Link
  Teledyne Benthos® LF Acoustic Modem
Control
  Main Vehicle Controller (MVC) Housing:
    Emergency Batteries and Electronics
    PC/104 Stack for Data Collection and Mission Controls
    Power Conditioning
  Propeller and Duct: Combined Propulsion and Control Surface.
PIC OF TAIL

## Slide 8: Mapping Sensors
EdgeTech FS-AU Combined System
  120/410kHz Sidescan Sonar
  1-6kHz or 2-16kHz Chirp Subbottom Sonar
Teledyne-Reson 7125
  200kHz or 400kHz Multi-beam Sonar
Typical Survey:
  50m Altitude
  1.5 m/s Speed.
  1 meter lateral resolution & 0.1 m vertical resolution.
Pic of Mapping payload

## Slide 9: Imaging Sensors
Nikon D3 w/ 24mm Lens
  74º Horizontal Field-of-View
Parallel Green Scale Projection Lasers
Ocean Imaging Systems Xenon Strobes
  200 Joules Combined Output
Typical Survey:
  0.5 Hz image acquisition
  3-5 meter altitude
  4 by 2.1 meter at 3m altitude

## Slide 10: Benthic Imaging
Mosaic of a 2.8m long Benthic Rover

## Slide 11: High Detail Results

## Slide 12: Repeat Mapping of Axial Volcano Lava Flows
Initial Surveys were conducted between 2006-2009
Detection of a New Flow in April 2011 led towards later re-mapping efforts.
Subtraction of the bathymetry led towards mapping of the extent of the new lava flow.
Notes: Add result title

## Slide 13
Repeat Maps

## Slide 14
Clague et al, Nature Geoscience, 2012

## Slide 15: New Hydrothermal Vent Discovery in the Gulf of California (2012)
Geological Mission to map active areas of the Alarcon Rise

## Slide 16
Original Survey (1-m Resolution)
Single Pass (3-D View)

## Slide 17: Vent Discovery
ROV Validation
Multiple Vents Found
  Including a 13-m Tall Vent

## Slide 18: Seep Exploration in Southern California
Surveys of Santa Monica and Santa Cruz Basins
Debris Mapping
Methane Seep Detection Coupled with ROV Validation
INSERT MAP of Dive Sites

## Slide 20: Debris Identification
ROV Frame Grab of a 55 Gallon Drum In Santa Cruz Basin

## Slide 21
Debris Identification

## Slide 22: Debris Identification
ROV Frame Grab of a Field of Cat Food Cans

## Slide 23: Seep Exploration
Santa Cruz Basin Including San Diego Trough Fault
Authigenic Carbonate Formation

## Slide 24
ROV Frame Grab of Carbonate Formations

## Slide 25: Future Efforts
Combine New Imaging Capabilities and Multibeam Payloads
  Targeting 1cm Lateral Resolution
  Addition of Stereo Imaging
  Evaluation of LIDAR Technologies
Test Interactively Using MBARI ROVs
Conduct Repeat Surveys
  Areas of Biological & Geological Interest Inside Monterey Bay

## Slide 26: ROV Imaging Test Platform
Notes: Pictured Here is Doc Ricketts, ROV
Custom Toolsled that gets bolted onto the bottom
Use Station Keeping software developed with Stanford to conduct au
Surveys
Near autonomous with real time results

## Slide 27
Area of Interest in the Monterey Canyon

## Slide 28
Shipboard Multibeam Data of Highlighted Area

## Slide 29
AUV Collected Data of the Previous Slide at 1m Resolution

## Slide 30
ROV Collected Multibeam at 1cm Resolution

## Slide 31
EM300 (50m)
AUV (1m)
Ocean Imaging (5cm)

## Slide 32: Conclusions
Seafloor mapping from AUVs continues to be a staple of exploration in areas where shipboard maps only provide hints to underlying areas of interest.
There is value in even finer scaling mapping.
Imaging provides potential for single mission survey target identification and verification.
These methods improve target identification and help aid more productive ROV dives.

## Slide 33: Questions?

## Slide 34: Acknowledgements
Hans Thomas, David Caress, Brett Hobson, MBARI
David Clague, Charles Paull
Steve Rock, Stanford University
For more information, please contact:
  emartin@mbari.org
  http://www.mbari.org