## Slide 1: MiniROV Smart Clump Preliminary Design Review

## Slide 2: PDR Agenda
Background
Review of design requirements
Operational considerations
Proposed design
  Mechanical
  Electrical
  Software

## Slide 3: Clump Weight System - Background
What’s the function and why does the MiniROV use one?
  Reduce umbilical drag
  Overcome limited power
Current clump weight design
  Scrap steel (150 lbs)
  USBL Transponder
Drawbacks
  Limited operating area
  2nd body to track

## Slide 4: Smart Clump
What is a Smart Clump
  Main function is still a depressor weight
  Access to power & real time data link to the surface
  Addition of cameras, sensors and Instrumentation
  Beneficial to the safe operation of the vehicle
  Enhances observational capabilities

## Slide 5: Functional Requirements
ROV operations not dependent on the Smart Clump
  Can be quickly removed and revert back to standard clump configuration
Camera(s) to provide bird’s eye view of the surrounding area
  Assist with navigation
Instrumentation to assist with the positioning of the clump in relation to the seafloor/ROV
Thrusters to assist with position/rotation of the clump
  Assist with transecting
  Assist with tether turns/monitoring
  Assist with camera orientation
Clone MiniROV technology/components to reduce risk

## Slide 6: Operational Considerations - Pros
Entanglement on canyon walls
  Altitude sensor and camera insures the clump is clear of the sea floor/wall
Manage umbilical turns
  Measure twists from cable torque with heading sensor
Overcome bad tracking
  Camera provides feedback of the ROV position to the pilot/captain
  Increased efficiency for transects
Better understanding of surrounding area (Bird’s eye view)

## Slide 7: Operational Considerations - Cons
Can’t remove Clump during launch & recovery
  Unable to spool flying tether section onto winch drum.
  Must deal with 50m of tether on deck.
Increase complexity of system – more things can break, more to maintain.
Impact on reliability?

## Slide 8: Proposed Design
Low design risk – its been done before
Use identical COTS hardware used on the MiniROV
  Same hardware/software architecture as the MiniROV
  No additional spares required
Reuse of software and instrument drivers
Smart clump frame

## Slide 9: Proposed Design - Instrumentation
Heading – Manage umbilical turns
Altimeter – Keep clump off of the canyon walls and bottom
Depth sensor – Maintain proper separation between ROV and clump
Camera(s) (HD & analog)– Provides birds eye view of the ROV and surrounding area
  Assist with tracking of the ROV and navigation of the ship
USBL transponder – Provide position of clump
Thrusters – Maintain camera orientation and prevent turns in umbilical
Sonar

## Slide 10
Proposed Design - Mechanical Layout

## Slide 11: Proposed Design – Mechanical (Continued)
Simple galvanized steel frame structure
Reuse tether termination/bullet assembly

## Slide 12: Proposed Design - Electrical
Overview of system
High voltage power routing through Smart Clump and MiniROV
Power budget and considerations

## Slide 14: Proposed Design – Smart Clump EPod
ALL components of Smart Clump Epod currently exist in MiniROV Epod
Focal fiber mux provides:
  3 channels video
  6 channels serial comms
  CWDM board adds one channel HD video and one channel HD video or GigE
Terminal blocks and fuse blocks distribute +24V, +5V, Frame Gnd, +375V
Wago modules provide Digital I/O, Analog I/O, can temp sensing
Two GFMs monitor low voltage GFs for +24 bus, +5V bus, +48V bus (thrusters)
GF monitoring of +375V done on topside

## Slide 15: Proposed Design – High Voltage Routing
Existing system

## Slide 16: Electrical – Power Considerations: Umbilical
Umbilical length = 1710 m
Total round trip resistance = 9.2 Ohms
Min Voltage for Vicors = 250 V
Max Voltage for Vicors = 425 V
Max current capacity of umbilical = 24 A
Topside power supply provides 500 Vmax, 10 kWatts
Maximum power delivery to bottom side calculated ~ 4.7 kWatts (254V at vehicle)

## Slide 17: Electrical – Smart Clump Power Budget
load | Man./Model | qnty | voltage (Volts) | current (Amps) | power per unit (Watts) | Total power (Watts)
+24V |  |  |  |  |  | 
HD Camera | DSP&L, HD Multi Seacam | 1 | 24 | 0.0833 | 1.9992 | 1.9992
Light | DSP&L, LED Sealite | 1 | 24 | 4.42 | 106.08 | 106.08
Altimeter/Depth | Valeport, VA500 | 1 | 24 | 0.0625 | 1.5 | 1.5
Aux Cam | DSP&L, Super Wide-i Seacam | 1 | 24 | 0.145 | 3.48 | 3.48
Sonar | Imagenex, 881A | 1 | 24 | 0.208 | 4.992 | 4.992
Tilt | MBARI | 1 | 24 | 2 | 48 | 48
Wago Stack | Wago | 1 | 24 | 0.5 | 12 | 12
Hotel load Epod | GFM, Relays, SSRs, Fan | 1 | 24 | 0.5 | 12 | 12
 |  |  |  |  | SUM | 190.0512
+5V |  |  |  |  |  | 
Fiber Mux | Focal 907-R/C | 1 | 5 | 2 | 10 | 10
Heading | PNI, Fieldforce TCM | 1 | 5 | 0.12 | 0.6 | 0.6
Hotel load | Rattler, humidity | 1 | 5 | 0.25 | 1.25 | 1.25
 |  |  |  |  | SUM | 11.85
+48V |  |  |  |  |  | 
Thrusters | MBARI | 2 | 48 | 9 | 432 | 864
 |  |  |  |  | SUM | 864.00
Total Power |  |  |  |  |  | 1065.90
Total Power- PreConverter |  |  |  |  | At 85% eff | 1225.79

## Slide 18: Proposed Design – Power Considerations
Total combined power for vehicle (all components consuming maximum power draw) is calculated at 4 kW BUT all loads never drawing maximum power at once
Realistic worst case vehicle power draw (all thrusters, lights, core instruments on) calculated to be 3.3 kW
Measured maximum power draw from field deployments over the past two years ~ 2.66 kW
Thus:
4.7 kW available power on bottom side
1.2 kW power for smart clump
2.66 kW measured worst case
= 0.84 kW based on power measurements
(= 0.2 kW remain in calculated worst case scenario )

## Slide 19: In Summary
In practice the vehicle is using about half of the total power capacity and a conservative estimate is that the clump will consume 1/3 of the power of the vehicle
Current to the clump/ROV and voltage at the ROV can be measured and trigger an alarm
There is enough reserve in the original design to handle the additional power consumption of the clump.
Software can disable additional loads during peak usage ??

## Slide 20: Proposed Design – Software/Hardware
LabVIEW Development
  Incorporated into existing ROV GUI
  Reuse existing instrument drivers
  Auto heading function (small USB joystick controller topside)
Electronics pod – Clone of Mini’s
  WAGO Modbus field point I/O system
  FOCAL fiber optic multiplexor (Analog video & data)
    Serial data channels (RS-232 & 485)

## Slide 21: Questions

## Slide 22: MiniROV Power Budget
load | Man./Model | qnty | voltage (Volts) | current (Amps) | power per unit (watts) | Total power (Watts) |  | Watts
+5V |  |  |  |  |  |  |  | 
Heading | PSN ForceField TCM | 1.00 | 5.00 | 0.120 | 0.60 | 0.60 |  | 
Fiber Mux | Focal 20907 | 1.00 | 5.00 | 1.000 | 5.00 | 5.00 |  | 
GigE-Fiber | Focal Dual GigE | 1.00 | 5.00 | 1.500 | 7.50 | 7.50 |  | 
Humidity Sensor | TE connectivity HM1520 | 1.00 | 5.00 | 0.008 | 0.04 | 0.04 |  | 
Lasers | OIS Model 400-37 | 2.00 | 5.00 | 0.040 | 0.20 | 0.40 |  | 
Depth sensor | Valeport ultra-p? | 1.00 | 5.00 | 0.040 | 0.20 | 0.20 |  | 
Serial Expansion | Focal 907-SER | 1.00 | 5.00 | 1.500 | 7.50 | 7.50 |  | 
 |  |  |  |  |  |  | 5V Power Sum | 21.24
+12V |  |  |  |  |  |  |  | 
CTD | FSI micro-CTD | 1.00 | 12.00 | 0.120 | 1.44 | 1.44 |  | 
Science port | Science port | 2.00 | 12.00 | 1.000 | 12.00 | 24.00 |  | 
Rattler | Rattler | 1.00 | 12.00 | 0.050 | 0.60 | 0.60 |  | 
 |  |  |  |  |  |  | 12V Power Sum | 26.04
+24V |  |  |  |  |  |  |  | 
Color Pencil Cam | Insite Tritech Nova | 2.00 | 24.00 | 0.175 | 4.20 | 8.40 |  | 
Sonar | Imagenex 881A | 1.00 | 24.00 | 0.200 | 4.80 | 4.80 |  | 
B&W Camera | Insite Tritech IT-1000 | 1.00 | 24.00 | 0.150 | 3.60 | 3.60 |  | 
Lights (Mains) | DSPL Multi-SeaLite | 4.00 | 24.00 | 3.200 | 76.80 | 307.20 |  | 
Lights (Secondary) | DSPL Nano sealites | 2.00 | 24.00 | 0.583 | 13.99 | 27.98 |  | 
DVL | Rowe RTDP1200DR | 1.00 | 24.00 | 0.170 | 4.08 | 4.08 |  | 
Tilt motor | MBARI stock | 1.00 | 24.00 | 1.000 | 24.00 | 24.00 |  | 
Manipulator | ECA ARM-5E | 1.00 | 24.00 | 5.000 | 120.00 | 120.00 |  | 
Controller | Wago stack | 1.00 | 24.00 | 1.000 | 24.00 | 24.00 |  | 
HD Cam | Insite Pacific MiniZeus II | 1.00 | 24.00 | 0.300 | 7.20 | 7.20 |  | 
Drawer Motor | MBARI stock | 1.00 | 24.00 | 2.000 | 48.00 | 48.00 |  | 
Swing Arm | MBARI stock | 1.00 | 24.00 | 2.000 | 48.00 | 48.00 |  | 
+24V Relays | Crydom CMXE100D10 | 4.00 | 24.00 | 0.012 | 0.29 | 1.15 |  | 
HV Solid state relays | Crydom SSC800-25-24 | 2.00 | 24.00 | 0.015 | 0.36 | 0.72 |  | 
Science Port |  | 2.00 | 24.00 | 0.500 | 12.00 | 24.00 |  | 
 |  |  |  |  |  |  | 24V Power Sum | 653.14
+48V |  |  |  |  |  |  |  | 
Thrusters | Cleveland Mtr | 6.00 | 48.00 | 9.000 | 432.00 | 2592.00 |  | 
Suction sampler | Cleveland Mtr | 1.00 | 48.00 | 9.000 | 432.00 | 432.00 |  | 
 |  |  |  |  |  |  | 48V Power Sum | 2592.00
Total Power |  |  |  |  |  | 3724.42 |  | 
Total Power- PreConverter |  |  |  |  | At 85% eff | 4096.86 |  | 

## Slide 23: Proposed Design - Electrical
Total combined power for vehicle (all components consuming maximum power draw) = 4 kW
Realistic worst case vehicle power draw (all thrusters, lights, core instruments on) ~ 3.3 kW
load | qnty | voltage (Volts) | current (Amps) | Total power |  | Watts
+5V: Heading, Focal Stack, Lasers, Depth, Humidity | 1.00 | 5.00 | 4.208 | 21.04 | 5V Power Sum | 21.04
+12V: CTD, Rattler | 1.00 | 12.00 | 0.170 | 2.04 | 12V Power Sum | 2.04
+24V: Aux Cams, Sonar, Lights, DVL, Controller, HD Cam, Sci Ports, Hotel load | 1.00 | 24.00 | 16.040 | 385.15 | 24V Power Sum | 385.15
48V: Thrusters | 6.00 | 48.00 | 9.000 | 2592.00 | 48V Power Sum | 2592.00
Total Power |  |  |  |  |  | 3000.23
Total Power- PreConverter |  |  |  |  |  | 3300.26
Does not include suction pump (400 W), manipulator (120 W), draw motor (48 W), and swing arm (48 W) – none of these loads would likely be in use when all thrusters are on.

## Slide 24: Electrical – Power Considerations
Date | Max Current Draw topside @ 400V | Deployment
2/4/2017 | 8.07 | Flyer
2/6/2017 | 8.2 | Flyer
10/1/2016 | 8.08 | Arctic
9/27/2016 | 8.02 | Arctic
9/26/2016 | 8.1 | Arctic
5/5/2016 | 6.87 | Carson
5/3/2016 | 5.38 | Carson
Top side power supply current measurements from last two years:
Power draw never exceeded 8.2A @400V = 3.28 kWatts
Estimated max power at vehicle 2.66 kWatts

## Slide 25: Umbilical Power Loss Calculations
SOUTH BAY |  | 
1700 m tether calculated based on acceptance testing |  | Units
Tether length | 1710.00 | m
13 AWG conductor resistance | 7.58 | Ohms/km
3 pair 13 AWG | 2.53 | Ohms/km
total resistance for round trip | 9.20 | Ohms
Max Safe Current for 13 AWG conductor | 8.00 | A
topside voltage | 425.00 | V
Current to vehicle | 18.50 | A
drop in cable @ specified current | 170.22 | V
Voltage @ veh for specified current | 254.78 | V
power @veh for specified current | 4713.34 | Watts
power on deck | 7862.50 | Watts