## Slide 1: MiniROV Video Improvements
2016 upgraded lighting capabilities and jumped to 1080p
2017-18 Smart clump for “birds-eye” view of surrounding environment
2018 added CWDM for 2 additional HD cameras for 200+ degree field of view or stereo
2018 Hope to add light booms (swing-arms) for improved lighting
Propose replacement of Mini Zeus HD camera with new COTS 4k-UHD system.

## Slide 2: Video Transmission
Video signal is converted to fiber CWDM wavelength in the camera. (fiber connector req.)
UHD signal sent up the fiber on 1311 or 1331 CWDM wavelength.
Topside the signal is converted back to copper and is split and down converted to HD-SDI 1080i
Both HD and UHD signals are brought into the video switcher for distribution and viewing.

## Slide 3: Storage and Annotation
The HD-1080i signal is sent to the main M3RS for recording and VARS annotation.
The UHD signal is sent to a second M3RS for limited “High light” only recording and VARS annotation.
Suggested 1 hr max. of UHD recording time /dive
UHD or HD signals available for display