## Slide 2
F55/CA4000/BPU4000
HDCU2000/RCP1500 Studio application

## Slide 3: Versatile Live Production Camera System

## Slide 4: PMW-F55: Application
4K
Live
HFR
POV
Drama
Multi Application
4K-Live System

## Slide 5: Camera Weight
Approx. 5.85kg
including F55,CA4000.DVF100
Handle & Shoulder pad
VCT-FS5 can be mounted on VCT-14
Fuji 4.7x Lens
(ZK-4.7x19SAF)
2.7KB
PMW-F55+ Fuji 35mm (ZK-4.7x19SAF)+CA-4000 +DVF-EL100 +VCT-FSA5

## Slide 6: PMW-F55
S35mm 4096 x 2160 Single CMOS Imager,
FZ Mount, PL adapter provided, B4 adapter as option
14 F-stops Exposure latitude
Up to 180P in 4K, Up to 240P in HD
Variable Electronic Shutter angle : 1/24 to 1/6000 Sec
Modular Design
Light weight : 2,2Kg

## Slide 7: CA-4000
  System Camera Adapter for F55
  Fibre connection to BPU
  RAW data from F55 and transmit to BPU
  System camera IF :
    HDVF Viewfinders, Intercom, Tally, Tracker, Aux, Remote, Ret CTRL, Genlock, Moni Out
  Power Booster kit for Large Lens power supply

## Slide 8: CA4000 & SKC-PB40
CA-4000 (for portable)
CA-4000 + SKC-PB40 (For Large BOX Lens opération )

## Slide 9
CA4000 Rear View
Similar to HDC arrangement
Intercom
Audio in
DC-IN (XLR)
SMPTE Fiber Connecter
RET-control
Accessory
DC-out
Mic Line,AES/EBU,48v
8-pins Remote
(CCA)
Trucker
EXT tally contact closure
Tally on/off
Rear Tally
RET 1&2,3,4
Aux (12 pins lens connecter for lens
which does not have Hot-shoe I/F
Income: Mic/PGM
Menu (VF operation,
sw assign ,etc)
Call
Prompter/GL (VBS/HD-tri-level)
Prompter-2 (VBS)
SDI-Monitor (Menu select
HD-SDI,VF, HD-prompter )

## Slide 10: CA-4000 w/ SKC-PB40
Power Module: 3x DC OUTs—Total 135w
  ex: 2=appprox.65w each
  2x 4p XLR (12V) : use for powering box type HD lenses
  1x 3p round mini conn (24Vdc) (used for Cine accessories )

## Slide 11: CA4000 Front View
Front Tally
&
Lens Tally
Sw on front
F55 IF connecter

## Slide 12: Tally on Handle (Front and Rear)

## Slide 13: CA4000 (4K Camera System Adapter)
Power SW
Handel slide Lock lever
Coin Screws
for mounting handle on
the F55 body
Ventilators

## Slide 14: CA4000 (4K Camera System Adapter)
DVF Connecter
HDVF Connecter
USB
-Soft version-up
-Others
(Under the study)
Ventilators
Coin Screws
for mounting handle on
the F55 body

## Slide 15: CA4000 (4K Camera System Adapter)
VF Shoe
Assignable SW
Coin Screws
for mounting handle on
the F55 body

## Slide 16: F55 + CA4000 Mounting Method
F55＋VCT-FSA5
Handle can slide
Not require tools, only needs a coin
Handle can slide for balancing when heavy lens is mounted
Handle can open
Close handle and
use coin to tight
4 screws on the F55

## Slide 17: Portable Configuration F55+ CA4000+HDVF-EL75
Fujinon 19-90mm Cabrio Lens (PL)
PMW-F55
CA-4000

## Slide 18: Large Box Lens configuration
Fujinon 99x Zoom Lens (2/3’’)
LA-FZB2
(FZ to B4 Optical Adapter)
PMW-F55
CA-4000
+ Power Booster
(SKC-PB40)
VCT-FSA5

## Slide 19: BPU-4000
Base band Processor Unit
  RAW data from F55
  De-bayering and Signal processing (DSP: same as HDC camera)
  Connection to HDCU-2xxx series
    for Camera Power / Intercom, Tally/ Return/Prompter / RCP, MSU & other required Signals
  4K & HD outputs
  Cut out video outputs
  HFR video outputs
  3G out Level-A/B
  (Selectable via
  Menu sw on BPU, RCP・MSU)
Front View
Rear View

## Slide 20: BPU (Base Band Processor Unit)
1.5U
Tally
Menu
-Configuration
-Diagnostic
-Service
Fiber Status info
Ventilator
Front Panel arrangement will be same as HDCU 2000/2500
DSP Processor inside is same as HDC2000 series
No power to camera from this unit (Head needs local power)

## Slide 21: BPU4000 Rear Panel
2 BNC Pair
小さいプロダクションではHDCUなくて使用可能
ただし、incom,.tally audio が無い
REF
(HＤ,VBS)
LAN
(RCP or PC for CUT-OUT)
SDI I/O
To camera
(SMPTE Fiber)
RCP/CNU
From HDCU
(SMPTE Fiber)
SDI OUT
(HD-SDI
Monitor
-Wire out
４K OUT
3G Out
No IF for:
-Income
-Tally
-Audio
We can use without HDCU
for small productions:

## Slide 22: BPU 4K/HD output connector arrangement
４K OUT(SLOT2)
3G/HD-SDI（SLOT3）
HD-SDI（SLOT4）
４K OUT(SLOT1)

## Slide 23: Application
4K Mode
HFR Mode*
HD Cut Out (Option)
4K/QFHD
1080P
1080P/I
1080P/I
1080P/I
1080P
1080/240p
4K/QFHD
Return / intercom / Ref /Tally / RCP
Return / intercom/ Ref /Tally/ RCP
Return/intercom/ Ref /Tally/RCP
4K Broadcast
HD
Live Sports
HD
Live Sports
Virtual Camera
1080P

## Slide 24: 4K Broadcast
4K Mode
4K/QFHD
1080P
1080P/I
Return / intercom / Ref /Tally / RCP
4K Broadcast
A
B
C
D
4K-OUT(A)
4K-OUT(B)
4K-OUT(C)
4K-OUT(D)
-Slot-1: Main
-Slot-2: Monitor

## Slide 25: High Frame Rate HD 240P
HFR Mode*
1080P/I
1080P
1080/240p
Return / intercom / Ref /Tally / RCP
HD
Live Sports
*Require F55 v1.4, Dec13
HFR monitor
HFR out
Normal Speed 3G/HD
Normal Speed
HD/Moni

## Slide 26: LA-FZB2 : Lens 35mm –2/3”Optical Converter
LA-FZB2
– FZ to B4 lens adapter
  2.6x Magnification
  ALAC
  ND/CC Servo, Filter Wheels
    4 ND: Clear, ¼,1/16,1/64
    4CC:Cross, 3200K,4300K,6300K
  12pin Lens Connecter
  W91mm x H173.4mm x D96mm
  1Kg
  12 PIN connecter IF under standalone operation ex: Rec Trigger:
    Same as LA-FZB1—See following page
Screw 3/8”
Cramp
Φ15mm Rod
12P Lens CN

## Slide 27: ALAC function with LA-FZB2 Available Lenses
For Prototype & Pre-Production Models
  Studio Box lens
    Fuji Film XA88x8.8BEPS
    Fuji Film XA99x8.4BESM
  Portable lenses
    Fuji Film HA23x7.6BERD
    Fuji Film HA19x7.4BEZD
For Production Model: TBA

## Slide 28: LA-FZB1 : Lens 35mm –2/3”Optical Converter

## Slide 29: LA-FZB1 Product Overview
FZ to B4 lens adapter
  2.6x Magnification
  ALAC
  12pin Lens Connecter
  No ND/CC Filters are available ( use Filters on Camera)
Applicable model:
  PMW-F55/F5
  Can not be used with PMW-F3
2/3” Portable Lens Use w/ LA-FZB1
LA-FZB1 : Lens 35mm –2/3”Optical Converter

## Slide 30: 12 pin interface
12-pin interface make lots of functions be possible.
Available from F55/F5 Ver1.3 (September/2013)
  Rec trigger
  Zoom button
  Lens Information
    (zoom, focus, iris, serial number, model name)
  Control from RM controller (iris)
  Control from CBK-DCB01( zoom controller)
Available from F55/F5 Ver1.4 (December/2013)
  Auto iris

## Slide 31
 | LA-FZB1 (w/o FDU) | LA-FZB2 (w/ FDU)
Manufacturer | SONY | SONY
Magnification | 2.6x | 2.6x
Max. Input F Number | 1.44 | 1.44
Mount | FZ to B4 | FZ to B4
Dimensions | Φ91x92.9 | Φ91x95.84
Mass | 664g (1lbs, 7.40oz) (w/ support rod bracket) 505g (1lbs, 1.8oz) (adaptor only) | 848g (w/ support rod bracket)
External interface | 12P | 12P
Filter Disc Unit | n/a | 1:ND0(CLEAR) A:CROSS 2:ND0.6(1/4) B:3200K 3:ND1.2(1/16) C:4300K 4:ND1.8(1/64) D:6300K
LAFZB1& LAFZB2 comparison
Note: No other manufacture optical adapter has Filter disc

## Slide 32: w/ 15mm support rod bracket

## Slide 33: w/ 15mm support rod bracket

## Slide 34: w/o 15mm support rod bracket

## Slide 35: w/o 15mm support rod bracket

## Slide 36
DVF-EL100
0.7” OLED
DVF-L350
3.5” color LCD
DVF-L700
7” LCD
HDVF-EL75
7.4” Color OLED
Viewfinder Choices

## Slide 37: Control Panels
New Features
MSU-1000
MSU-1500
RCP-1000/1001
RCP-1500/1501
RCP-1530
Conventional multi-pin cable control
Network control by LAN cable
Programmable menu

## Slide 38: MVS-7000X & 8000X
Currently: 4K production by setting bus-link of 4M/E (or 2ME+MP2) in 1080P(3G)
  Simple operation with Cut, MIX etc.
Future: 4K Upgrade software
  Wipe, Choma Key etc. will be available
Future: 4K Up-converter Option:
  HD (I or P) to 4K up-conversion will be available

## Slide 39: SR-R1000
Recording on ultra-reliable SRMemory
HD, 3D and 4K recording
Simultaneous record and slow motion replay
Compatible with 3rd party external controllers
Open SStP recording format

## Slide 40: PVM-X300
30’’ True 4K (4096 x 2160) LCD Panel
Versatility with 3G-SDI x4, HDMIx4 and DisplayPort x2
Quad View Modeamera focus function
Auto White Adjustment with colour probes
Markers setting and Gamma selection