## Slide 1: Proposed assembly procedure for I2map optics
Francois Cazenave, MBARI
5/21/15

## Slide 2: Myriad to provide: - clean work environment - glass handling supplies - vacuum pump with vacuum gauge and appropriate hoses - cleaning supplies for glass and metal parts - o-ring lubricant MBARI to provide: - dome port - all metal components (titanium ring, spacers, retainer) - Kapton ring - plastic dome retainer and screws - all o-rings - vacuum port plugs and hose barb adapter - vacuum cup for lifting lenses - cap for dome port Fathom imaging to provide: - 3 lenses.

## Slide 3
1- Thoroughly clean all components. Place titanium ring on bench, dome side down.
Ring OD: 11”. Weight: 20 lbs

## Slide 4
2- Insert o-ring in rear lens o-ring groove.

## Slide 5
3- Insert rear lens

## Slide 6
4- Secure rear lens with threaded retainer.

## Slide 7
5- Mount aluminum ring to give lens some protection

## Slide 8
6- Place titanium ring dome side up

## Slide 9
8- Insert middle lens. Suction cup can be used to lower lens.

## Slide 10
9- Insert lens spacer

## Slide 11
10- Insert double concave lens

## Slide 12
11- Secure lens with threaded retainer

## Slide 13
12- Insert Kapton ring

## Slide 14
13- Insert dome in titanium ring. Insert back-up ring in groove around dome using fine tipped tool.

## Slide 15
14- Insert o-ring in the groove using fine tipped tool.

## Slide 16
15- Place ABS retainer on top of dome port

## Slide 17
16- Secure retainer with 8 screws.

## Slide 18
Final steps:
Place cap on dome port
Turn assembly dome side down
Connect hose barb adapter to check valve equipped vacuum port
Connect vacuum pump to hose barb
Very slowly pull vacuum to avoid creating a potentially dangerous pressure differential between lenses.
Disconnect vacuum pump, cap vacuum port.