## Slide 1: Vehicle Control And Stability

## Slide 2: Wings 14” Behind Eye Center, With Bars

## Slide 3: Outline
Review analysis that leads to wings and winglets.
  Round bar, different nose.
  Increased gains.
Proposed dive plan.
Propulsion power budget if time permits.
  From LR AUV work.

## Slide 4: Two Mostly Independent Problems
Low speed versus buoyancy:
  Steady-state “trim” analysis in straight and level flight.
    Nonlinear algebraic equations instead of differential equations.
    Time is not the independent variable.
  Control gains, time constants, open/closed loop etc. don’t apply.
Destabilizing effect of light bars:
  Affects dynamics. Must include derivative terms.
    Angles versus time.
  Solve linearized ODEs to determine stability.
  Final step is to verify with simulation of nonlinear ODEs.

## Slide 5: Free-Body Diagram
Steady-State Force and Moment Balance in
Heave/Pitch (Vertical Plane).
Drag vector not dependent on vertical v.s. horizontal plane with round bar.

## Slide 6: Buoyancy is Difficult to Measure
But speed is easy to measure with the Dvl.
Flip the problem:
  Assume constant worst-case speed of .5 m/s, vary buoyancy.
Review: what are we trying to determine?
  How much buoyancy before the Auv can’t fly level?
  How much do body wings help?
  If body wings, how far aft?
  Winglets or not?

## Slide 7: Bare Vehicle with Lights
2.25 lbf
6.74 lbf
Guess: Hull stalls at ~10 Deg.
2.25 lbf => 0.29-0.58 kg/m3.
Power analysis carried over from LR AUV.
4.50 lbf

## Slide 8: With Body Wings 37” Aft of Lifting Eye
Wing COL is 93 cm aft of c.g.;
-81 cm from origin;
40” aft of eye.

## Slide 9: With Body Wings at 37” and Winglets

## Slide 10: Body Wings 11” Aft of Eye and Winglets
Wing COL is 27 cm aft of c.g.
-15 cm from origin;
14” aft of lifting eye

## Slide 11: Stability Analysis
Vehicle depth control sluggish at .5 m/s.
Lift ~ speed2.
  At 1/3 the speed (.5 m/s) lifting surfaces produce 1/9 the lift.
  Control gains are a function of speed.
Increase gains to speed time constants back up.
  Tentative set selected.
  Work in progress.

## Slide 12: Objectives for Next Dive
  See if it can hold depth at .5 m/s, with usual ballasting, with final nose.
  Test controllability in depth and heading.
  Test the above w/o wings with low buoyancy.

## Slide 13: Tentative Dive Plan
Vehicle:
  Ballasted as usual ~ 4.5 lbf.
  New nose with circular bar and lights.
  Wings on. Leading edge 11” aft of center of lifting eye.
  Winglets on duct.
Launch and run:
  Straight & level (S&L) speed steps.
  50m depth; .5 m/s, S&L, step down 10m, step back up. Expect sluggish response. This tests depth control.
  Repeat with higher control gains (TBD). Should respond faster.
  Box run to test heading control.
Recover. Remove winglets. Possibly shift wings back.

## Slide 14: Tentative Dive Plan (con’t)
Launch and run:
  Repeat speed steps. (2.1)
  Repeat depth step response. (2.2)
  If necessary adjust gains, repeat.
  Box run or possibly out-and-back to test heading control.
Recover. Remove wings. Redeploy.
  Repeat speed steps. (2.1)
  Repeat step response to test depth control. (2.2)
  Adjust gains, repeat.
  Test heading control.
Recover. Hans adds lead to lower buoyancy as much as possible.
  Repeat above four.

## Slide 15: Static Angles Versus Speed

## Slide 16: Total Power

## Slide 17: Propulsion Power Stackup

## Slide 18: End