## Slide 1: Overall System Design
  System Layout
  Energy budget
  AUV interface
  CTD and other environmental sensors

## Slide 3: Camera System
  Camera and Lens Testing
  Optical Dome and adapter design
  Video Format Selection
    Temporal Resolution
    CODEC Performance
  Recorder
    Recording Capacity
    Post mission workflow
  Conclusions

## Slide 4: Distance Requirements for the Identification of Representative Organisms in the Camera Field-of View
Chart: 
| Aegina | Aegina citrea | Apolemia | Atolla | Atolla wyvillei | Bargmannia elongata | Beroe | Chuniphyes | Clione | Doliolula | Forskalia | Gigantocypris | Hastigerinella digitata | Kephyes ovata | Lampocteis cruentiventer | Melanostigma pammelas | Mysidae | Nanomia bijuga | Pasiphaeidae | Periphylla | Periphylla periphylla | Poeobius meseres | Pseudothecosomata | Salpa | Salpa fusiformis | Solmissus | Solmundella bitentaculata
Calculated First I.D. Distance (cm) | 183.3 | 220 | 275 | 110 | 165 | 165 | 165 | 137.5 | 110 | 110 | 165 | 110 | 100.8 | 110 | 110 | 165 | 110 | 187 | 220 | 165 | 165 | 180 | 110 | 220 | 165 | 192.5 | 137.5
Front of Camera Dome
Measured First I.D. Distance (cm) (Rob Sherlock)
Species
Required I.D. Distance

## Slide 5: Close Focus Test (~10cm from dome)

## Slide 6: Resolution Testing (~ 0.5 m from dome)

## Slide 7: Far Focus (~2.5m from dome)

## Slide 8: Camera Test Setup

## Slide 9: Camera Test Work Flow
AJA Quad Pro ProRes 10 bit 422 (HQ) Recording
Sony XAVC Recording (F-5 only)
Sony 16 bit Raw Recording (F-5 only)
CAMERAS
Ikegami
HDL 50/HS
Sony
HDCP1,
NEX-FS700U
Capture Still Frame in .tiff Format
Export to ProRes 10 bit 422 HQ
Export to DPX Frames
Open in PhotoShop
Export to ProRes 10 bit 4444
2k
4k
1.9k
1.9k
Pixel Resolutions
1.9k = 1920 x 1080
2k = 2048 x 1080
4k = 4096 x 2160
Export to DPX Frames
Open in PhotoShop
1.9k
CAMERA
Sony F-5
CODEC Comparison Reference

## Slide 10: Camera Detail Resolution Comparison Locations Target Distance at “Sweet Spot” ~ 0.5 Meters From Dome
Sony F-5, SCL-P11X15 Lens, 400 lux, 70 IRE, Target 36 inches
Detail Areas
Center
Edge

## Slide 11: Camera Comparison Sony HDCP1 vs. Ikegami HDL50/HS
The B4 Mount Lens Winner Was Used for The Camera Test
Zeiss Digi Prime T1,9/5mm

## Slide 12: Camera Comparison Sony NEX-FS700U vs. Ikegami HDL50/HS
The PL and B4 mount Lens Winners Were Used for The Camera Test
Sony SCL-P11X15 Lens and Zeiss Digi Prime T1,9/5mm

## Slide 13: Camera Comparison Sony F-5 vs. Ikegami HDL50/HS
The PL and B4 mount Lens Winners Were Used for The Camera Test
Sony SCL-P11X15 Lens and Zeiss Digi Prime T1,9/5mm

## Slide 14: Finalist #1 Sony F-5 and Sony SCL-P11X15 Lens
Sony F-5, SCL-P11X15 Lens, 400 lux, 70 IRE, Target 36 inches File: Test_13X.tiff

## Slide 15: Finalist #2, Ikegami HDL-50/H and Zeiss Digi Prime T1,9/5mm Lens
Ikegami HDL50/HS, 5mm Lens, 140 lux, 80 IRE, Target 39 inches File: Test_77.tiff

## Slide 16: Sony F-5 vs. Ikegami HDL50/HS Center Resolution
Sony F-5, Sony 11mm Lens, 400 lux,
ISO 800, Target 36 inches, 1920x 1080 P60
File: Test_13X.tiff
Ikegami HDL-50/HS, Zeiss 5mm Lens, 140 lux, 80 IRE, Target 38 inches
File: Test_77.tiff

## Slide 17: Sony F-5 vs. Ikegami HDL50/HS Edge Resolution
Ikegami HDL-50/HS, Zeiss 5mm Lens, 140 lux, 80 IRE, Target 38 inches
File: Test_77.tiff
Sony F-5, Sony 11mm Lens, 400 lux,
ISO 800, Target 36 inches, 1920x 1080 P60
File: Test_13X.tiff

## Slide 18: Sony F-5 1920 X 1080 vs. Sony F-5 4096 X 2160 (4K) Center Resolution
Sony F-5, Zeiss 12mm Lens, 400 lux,
IE 800, Target 36 inches, 1920x 1080 P60
(no color correction)
File: Test_54_1920_4444.tiff
Sony F-5, Zeiss 12mm Lens, 800 lux,
IE 2000, Target 34 inches, 4K P60
(no color correction)
File: Test_54_4K4444.tiff

## Slide 19: Sony F-5 1920 X 1080 vs. Sony F-5 4096 X 2160 (4K) Center Resolution - Detail
Sony F-5, Zeiss 12mm Lens, 400 lux, ISO 800, Target 34 inches, 1920x 1080 P60
(no color correction)
File: Test_54_1920_4444.tiff
Sony F-5, Zeiss 12mm Lens, 800 lux, IE 2000, Target 34 inches, 4K P60
(no color correction)
File: Test_54_4K4444.tiff

## Slide 20: Sony F-5 1920 X 1080 vs. Sony F-5 4096 X 2160 (4K) Edge Resolution
Sony F-5, Zeiss 12mm Lens, 400 lux, ISO 800, Target 34 inches, 1920x 1080 P60
(no color correction)
File: Test_54_1920_4444.tiff
Sony F-5, Zeiss 12mm Lens, 800 lux, IE 2000, Target 34 inches, 4K P60
(no color correction)
File: Test_54_4K4444.tiff

## Slide 21: Sony F-5 vs. Ikegami HDL50/HS Color Reproduction (4:2:2 Format)
Sony F-5, Sony 11mm Lens, 400 lux, ISO 800, Target 36 inches, 1920x 1080 P60 (no color correction)
Ikegami HDL-50/HS, Zeiss 5mm Lens, 140 lux, 80 IRE, Target 38 inches
(no color correction)

## Slide 22: Test Showing the Sony F-5 and the Sony SCL-P11X15 Lens Meets the i2MAP Depth of Field Requirements (at F 5.6)
Sony F-5, Sony SCL-P11X15 lens set to 11mm, 560 lux, 75 IRE, Target 18 inches (10cm from dome equiv.), F 5.6, focus distance 31.5 inches
File: Test_14.tiff
Sony F-5, Sony SCL-P11X15 lens set to 11mm, 560 lux, 75 IRE, Target 113 inches (2.5m from dome equiv.), F 5.6, focus distance 31.5 inches
File: Test_45.tiff

## Slide 23: Sony F-5 1920 X 1080 vs. Sony F-5 4096 X 2160 (4K) Resolution Example
Sony F-5, Zeiss 12mm Lens, 500 lux, IE 2000, Target 113 inches, 2K P60
(no color correction)
File: Test_53_2K.tiff
Detail Area

## Slide 24: Sony F-5 1920 X 1080 vs. Sony F-5 4096 X 2160 (4K) Resolution Example 2A
Sony F-5, Zeiss 12mm Lens, 500 lux, IE 2000, Target 113 inches, 2K P60 (Lightened 10%) File: Test_53_2K.tiff

## Slide 25: Sony F-5 1920 X 1080 vs. Sony F-5 4096 X 2160 (4K) Resolution Example 2B
Sony F-5, Zeiss 12mm Lens, 500 lux, IE 2000, Target 113 inches,
4K P60 (Lightened 20%) File: Test_53_4K444.tiff

## Slide 26: Sony F-5 1920 X 1080 vs. Sony F-5 4096 X 2160 (4K) Resolution Example 1
Sony F-5, Zeiss 12mm Lens, 400 lux,
IE 800, 1920x 1080 P60
(+20% brightness correction)
File: Test_53_2K4444.tiff
Sony F-5, Zeiss 12mm Lens, 800 lux,
IE 2000, 4K P60
(+20% brightness correction)
File: Test_53_4K4444.tiff

## Slide 27: Optical Dome Design
In the final process of selecting the optical design consultant.
Aspherical front dome design is recommended to support 4k resolution (minimize field curvature).
Mechanical design would be done in house.

## Slide 28: Temporal Resolution Testing
Rotating Test Target Reproduced Object Angular Velocities Simulating AUV Speeds of 0.55 and 1.0 meters per second

## Slide 29: Translation of Vehicle Motion to Focal-Plane
x_3p – focal plane to particle
x_3t – focal plane to disk
Eqn. 3 => 4 if they’re equal.
2/3” Camera Distance
Super-35 Camera Distance
(adjusted for 0.5 meters from dome front)
1.0 m/sec. = 11 RPM
0.55 m/sec. = 6 RPM

## Slide 30: Temporal Resolution, Can We Get Good Image Quality at 1 Meter Per Second? Enter The Wheel of Death
Ikegami HDL50/HS, Zeiss 5mm Lens, 100 lux, 1920x 1080i 30
Disk 6 RPM (~0.5 m/sec), File: Test_73_White.tiff (DeInterlaced)
Detail Test Area

## Slide 31: Comparison of Current (0.5 m/sec.) and Planned (1.0 m/sec.) Temporal Resolution at the 0.5 Meter from Dome “Sweet Spot”.
Ikegami HDL50/HS, Zeiss 5mm Lens,
110 lux, 1920x 1080i 30
Disk 6 RPM (~0.5 m/sec)
File: Test_73_White.tiff (DeInterlaced)
Ikegami HDL50/HS, Zeiss 5mm Lens,
170 lux, 1920x 1080 P60
Disk 11 RPM (~1 m/sec)
File: : Test_76_White.tiff

## Slide 32: The Effect of Camera Shutter at The Planned (1.0 m/sec.) AUV Velocity tested at the 0.5 Meter from Dome “Sweet Spot”.
Sony HDCP1, Zeiss 5mm Lens,
800 lux, 1920x 1080 P60
Disk 11 RPM (~1 m/sec), Shutter 1/250
File: Test_68_White.tiff
Sony HDCP1, Zeiss 5mm Lens,
120 lux, 1920x 1080 P60
Disk 11 RPM (~1 m/sec), No Shutter
File: Test_66_White.tiff

## Slide 34: Post-Mission Work Flow
AJA Quad Pro ProRes 10 bit 422 (HQ) Recording (.mov)
Export to H.264
CAMERA
Sony F-5 or F-55
Annotate in VARS using current H.264 file based version
Archive .mov files in Atlas Server
6 TeraBytes Maximum thru 2015
Annotate in VARS using updated QuickTime file based version
Timecode must be reconstructed
Timecode preserved
Timecode lost
2014-2015
Beyond 2015

## Slide 35: Estimated System Cost Comparison
Budget was ~ $57,592

## Slide 36: Camera and Recorder Testing Conclusions
Camera
  The F-5 camera is about 2 stops slower when depth of field control is taken into account.
  Shutter speed of 1/250 is needed to completely freeze the motion of 1 meter per second transect.
  Ikegami has black adjustment issues on power-up boot. Suggest putting 100% filter in one position in filter wheel – would require camera control.
Video Recorder
  The Apple ProRes 422(HQ) CODEC is visually lossless.
We should have adequate illumination.
  Need ~ 3200 lux maximum with F-5 at 0dB gain and 1/250th shutter.
  4 lights measure at ~ 3500 – 5000 lux at 0.5 meters from dome.

## Slide 37: Which is the best camera for us?
Ikegami HDL-50/HS 2/3” box camera
  Box camera has a great picture but is limited to 1920 X 1080 60 frames per second.
  Box camera is the smallest and would be slightly easier to integrate – except for auto black balance on boot-up.
Sony F-5 super 35 format camera.
  F-5 Cine camera has 4K sensor and offers a migration path to higher resolution formats, 2K and 4K.
    Current recording limitation is 2048 X 1080 60 frames per second.
    AJA has recording hardware in development that supports 4K at 60 frames per second that may be available in the future.
    Sony F-5 can be upgraded to 4K output for $12,000.
Cost is very similar – Go with the F-5

## Slide 38: CAMERA HOUSING BLOCK DIAGRAM