## Slide 2: xFOCE Electrical System (Subsea Node)
Chad Kecy
Electrical Engineer

## Slide 3: System Level Functions
Distribution of DC power to external instruments and internal subsystems
Bidirectional communication to external instruments and internal subsystems
Health monitoring for entire the subsea node
Computer
  Collection and dissemination of data
  Closed loop control of the experiment

## Slide 4: DC Power
DC-DC Converters
  Converts input DC voltage to all necessary lower DC bus voltages.
Conditioning and monitoring
  Provides filtering and power monitoring.
Patch panel
  Distributes lower DC bus voltages to internal subsystems.
Load switching to individual instruments
  Provides galvanic isolation, over/under current/voltage protection, power monitoring, and ground fault detection to each instrument.

## Slide 5: DC Power Example
48V to 24V
Inrush
Limiting
48V to 12V
Conditioning
Conditioning
Load Switching
Patch Panel
Ethernet
Switch
Computer
pH Probe
CTD
ADCP
Camera
Thruster
12V
12V
24V
24V
Subsea Node

## Slide 6: Instrument Level Power Control
ADCP
Load
Switching
Inrush
Limiting
Volt/Curr
Monitoring
Circuit
Breaker
Volt/Curr
Filtering
Over/Under
Volt/Curr
Detection
ADC
ADC
Amp
Curr Limit
R
Mosfet
Load Switcher
Ground Fault Monitor
12V
Seawater Ref

## Slide 7: Communication
Communication from shore to subsea node
  Factors:
    Is your FOCE tethered or standalone?
    Distance
    Bandwidth requirements
    Shore based infrastructure
  Potential choices:
    Tethered: Ethernet, RS-422, DSL
    Standalone: Wireless ethernet
Communication from subsea node to individual external instruments
  Most instruments utilize serial comms
    RS-232 and RS-485 most common

## Slide 8: Communications Example
Video
Server
Ethernet
Switch
Computer
pH Probe
CTD
ADCP
Camera
Thruster
Subsea Node
Serial
Expander/Server
Serial
UARTs +
Transceivers
Optional Paths

## Slide 9: System Health Monitoring
Provides top side users with status of environmental conditions in the subsea node.
Can be used to automatically power down instruments in the event of a failure.
Conditions measured:
  Temperature
  Humidity
  Water presence
  Housing pressure
  Orientation

## Slide 10: Health Monitoring Example
Thermocouple
Health
Monitor
Ethernet
Switch
Computer
Subsea Node
48V to 24V
48V to 12V
Ambient Temp
Ambient Humidity
Ambient Pressure
H2O Sensor
Thermocouples
Cooling Fan

## Slide 11: Computer
Can be of almost any variety based upon intended usage in subsea node.
Potential usage:
  Collection and dissemination of data from external instruments and internal subsystems.
  Performing the closed loop operation control of the pH experiments.
  Housing the individual instrument drivers.

## Slide 12: Four Potential Electrical Systems
1. PC/104 Stack
2. Wago I/O System
3. Instrument Chassis
4. Sensor Node

## Slide 13: PC/104 Stack
What is PC/104?

## Slide 14: PC/104 Stack
Modules available (multiple manufacturers):
  CPU
  Data storage
  Power Supply
  Digital I/O, Analog I/O (DAQ)
  Relay control
  Serial expansion
  Environmental input (temp, hum, etc…)
  Video Server/Encoder
  Ethernet switch
  Others

## Slide 15: PC/104 Stack
Advantages
Rapid prototype/design
Expandable/reconfigurable
Extensive functionality
Relatively inexpensive
Industry standard
Often software drivers included
Can incorporate custom boards
Disadvantages
Power consumption
Maintenance
  Need to disassemble the stack to get to middle boards.
Limit on # of boards in stack
Sometimes, no software drivers….

## Slide 16: PC/104 Stack
Function | Model # | Manufacturer | Notes | Watts | Cost | Quan | Tot Watts | Tot Cost
Computer | Cool RoadRunner-LX800 | Lippert |  | 6.5 | 500 | 1 | 6.5 | 500
Storage | 500Gb Scorpio Blue | Western Digital |  | 4 | 100 | 1 | 4 | 100
Power Supply | HE104+ DX | Tri-M |  | 10 | 300 | 1 | 10 | 300
Load Switching | DM6956 | RTD Embedded Tech | 16 Channels | 5 | 500 | 2 | 10 | 1000
Circuit Breaker | N/A |  |  |  |  |  |  | 
Ground Faulting | N/A |  |  |  |  |  |  | 
Load Power Monitoring | MM-32DX-AT | Diamond Sys | 32 Chan Analog | 3 | 600 | 1 | 3 | 600
Environmental Sensing | Model 518 | SensoRay | Temp/Hum only | 1 | 325 | 1 | 1 | 325
Serial Expansion | Xtreme/104-Plus Port | Connect Tech | 16 Channels | 4 | 350 | 2 | 8 | 700
 |  |  |  |  |  |  | 42.5 | 3525

## Slide 17: Wago I/O System
What is a Wago I/O System?

## Slide 18: Wago I/O System
Modules available:
  Controller
  Power Supply
  Relay Modules
  Digital I/O, Analog I/O (DAQ)
  Thermocouple inputs
  DC Motor Driver
  Others

## Slide 19: Wago I/O System
Advantages
Rapid prototype/design
Expandable/reconfigurable
Industry Standard
Generic software interface
Can incorporate custom boards
Disadvantages
Limited functionality for our requirements
  More custom designs
Power consumption

## Slide 20: Wago I/O System
Function | Model # | Manufacturer | Notes | Watts | Cost | Quan | Tot Watt | Tot Cost
Computer | 750-341 | Wago | Eth-Fieldus Coupler | 12 |  | 1 | 12 | 0
Storage | N/A |  |  |  |  |  | 0 | 0
Power Supply | N/A |  |  |  |  |  | 0 | 0
Load Switching | 857-304 | Wago | Single SPST Relay | 0.5 |  | 20 | 10 | 0
Circuit Breaker | N/A |  |  |  |  |  | 0 | 0
Ground Faulting | N/A |  |  |  |  |  | 0 | 0
Load Voltage Monitoring | 750-483 | Wago | Dual Voltage Analog Inputs | 2 |  | 10 | 20 | 0
Load Current Monitoring | 750-475 | Wago | Dual Current Analog Inputs | 2 |  | 10 | 20 | 0
Envr Sensing - Temp | 750-469 | Wago | Dual Thermocouple input | 1.5 |  | 3 | 4.5 | 0
Envr Sensing - Hum |  |  |  |  |  |  | 0 | 0
 |  |  |  |  |  |  | 0 | 0
Serial Expansion | N/A |  |  |  |  |  | 0 | 0
 |  |  |  |  |  |  | 66.5 | 

## Slide 21: Instrument Chassis
What is the Instrument Chassis?

## Slide 22: Instrument Chassis
Modules available:
  CPU Board
  Power Supply
  Environmental Monitoring Board
  Low Voltage Load Switcher (8 channels)
  Medium Voltage Load Switcher (4 channels)
  Ground Fault Detection Board (16 channels)
  Others

## Slide 23: Instrument Chassis
Advantages
Was designed specifically for use in the shallow water FOCE system
Modular; new boards can be designed.
Low Power design
Simple software interface
Disadvantages
Design complexity
Expensive to produce
Custom firmware needed
Currently, no serial expansion included

## Slide 24: Instrument Chassis
Function | Model # | Manuf | Notes | Watts | Cost | # | Tot Watt | Tot Cost
CPU |  | MBARI |  | 0.680 | 253 | 1 | 0.680 | 253
Power Supply |  | MBARI |  | 0.335 | 324 | 1 | 0.335 | 324
Backplane |  | MBARI |  | 0.000 | 193 | 1 | 0.000 | 193
Environmental Board |  | MBARI | 8-hum, 4-temp, pressure, X,Y,Z, H2O Sense | 0.200 | 316 | 1 | 0.200 | 316
Low Voltage Load Switcher |  | MBARI | 8-channels, 0-24V | 0.250 | 550 | 3 | 0.750 | 1650
Medium Voltage Load Switcher |  | MBARI | 4-channels 24V-48V | 0.250 | 425 | 1 | 0.250 | 425
Ground Fault Detection Board |  | MBARI | 16-Channels (with 4 HV) | 0.200 | 325 | 1 | 0.200 | 325
 |  |  |  |  |  | Q | 2.4 | 
 |  |  |  |  |  | Act | 10 | $3,486

## Slide 25: Sensor Node Board
What is the Sensor Node Board?
Pluggable
CPU
Module
BeagleBone?
Arduino?
Microchip PIC?
UART
Serial Transceiver
Load Switching
Ground Fault Detection
Over/Under
Curr/Volt
Det / Mon
Inrush
Limiting
Circuit
Breaker
DC Power from Bus
Ethernet Comms from Switch
DC Power to Instrument
Serial comms to Instrument

## Slide 26: Sensor Node Board
Modules available?
  None, it is a fully functional standalone unit
  1-3 instruments per Sensor Node board
Functions available:
  CPU, storage
    Device driver could be active locally
  Serial interface (uart + transceiver)
  Load switching
    Over/under curr/voltage detection
    Ground fault monitoring
    Current/Voltage monitoring

## Slide 27: Sensor Node Board
Advantages
All functions on one board
CPU simple to program
Single board design can handle a large variety of instruments
Open source HW and SW
Disadvantages
Custom design
Cost?
Distribution

## Slide 28: Electrical System Comparison
 | PC/104 | Wago | Instrument Chassis | Sensor Node Board
Central CPU | Yes | No | No | No
Local CPU | No | Yes | Yes | Yes
Local Storage | Hard Drive | No | SD Card | ?
Ethernet Interface | Yes | Yes | Yes | ?
Serial Expansion | Yes | No | No | One per
Load Control Relays | Yes | Yes | Yes | Yes
Circuit Breaker Protection | No | No | Yes | Yes
Inrush Limiting | No | No | Yes | Yes
Ground Fault Detection | No | No | Yes | Yes
Thermal Inputs | Yes | Yes | Yes | Yes
Humidity Inputs | Yes | No | Yes | Yes
H2O Sensor Inputs | Yes | Yes | Yes | Yes
Pressure Sensor Input | Yes | Yes | Yes | Yes
3-Axis Orientation | No | No | Yes | ?
Power Usage (Watts) | 45 | 70 | 10 | 
Cost per System ($) | 3500 |  | 3486 |