## Slide 2: Build and Configure System occurs: [basic system setup]
install/configure OS, system utils | Linux (Debian) Serial console terminal program Apt-get, aptitude Adduser, GRUB, tar, inittab, NTP, sudo(ers) | Linux (e.g. Debian) already installed Using serial console, terminal program: Configure console, IP addr, routers Add users, groups Config boot, apt sources Install optional packages (28) Configure NTP Configure sudoers
acquire/install/configure 3rd party software | Make menuconfig Patch, make-kpkg, dpkg, tar, aptitude (or other) Update-rc.d, startDataTurbine Configure, make, vi (e.g.) | Configure kernel support for serial drivers, install and test drivers Download/configure/make/install: RXTX, log4j, OSDT, ant… Install A/D drivers (tar), copy

## Slide 3: Build and Configure System occurs: [basic system setup]
acquire/install/configure development tools | JSDK, IDE, compiler Tar, aptitude (or other) Configure, make, vi (e.g.) | JSDK make ant
install/configure FOCE software | Ant/make, vi (e.g.) İnit.d, rc.d | Install SIAM Edit siamPort.cfg, Makefile.foce Build SIAM java sources Make foceio and other drivers Configure startup scripts (siam, osdt)
Set up OSDT server |  | Install JVM, OSDT
configure data collection | Ant/make vi (e.g.) | Make: foce, siamjar, siamif.jar, install Edit siamPort.cfg

## Slide 4
configure experiment | Ant/make vi (e.g.) | configure SIAM control svc properties Make control svc jar, (siamjar, siamif)
test data collection | OSDT, RDV Bash listPorts, logUtil, etc. | Start OSDT, SIAM Check SIAM logs, services Check data streams
test experiment | SIAM, RDV, OSDT NetBeans, CLOOP-GUI | Start SIAM, OSDT, CLOOP-GUI, RDV Start model, sim (from GUI) Send commands, watch output