## Slide 1: Instrument drivers, data and comm links: some guidelines

## Slide 2: Instrument data
Always keep “raw” data retrieved from instrument
Save instrument characteristics; make, model, serial #, calibration, etc
  Critical for data interpretation
  Often accessible from instrument itself
Further processing...
  Format conversion, e.g. for MatLab, WWW access, other tools

## Slide 3: Acquiring raw data
Self-logging instruments
  Autonomously log and store data internally for later retrieval, often not needed in real-time
Instrument driver: acquires and logs data to external storage
  Runs on shore workstation (cabled) or at-sea computer
  Can also retrieve & log instrument serial number, characteristics
  May provide data/control access to other system components (e.g. CO2 control loop)

## Slide 4: Where to get instrument drivers?
Manufacturer usually provides driver for Windows only
  May be usable on cabled system
3rd party drivers (e.g. MBARI SIAM, OASIS, UCSD SensorPod, ...)
  Often suitable for cabled or moored; maybe portable to multiple OSes
  Requires programmer; can customize code, extend to new instruments
Write your own drivers from the ground up
  LabView, Java, C/C++, C#, etc...

## Slide 5: Communication links
Cabled or high-speed wireless
  “Transparent” access to serial port; driver/logger can run on shore
  Generally reliable, but consider possible outage
Low-bandwidth/intermittent wireless
  Design system for outages
  Keep raw data on deployed platform
  Summarize raw data for telemetry (e.g. averaging, “snapshots”)

## Slide 6: Shore data base
User access to raw and processed data via Web or other interface
  Retrieve/display data based on user criteria
  Long-term data, metadata archive
  Many choices available
MBARI Shore Side Database
  Open source
  Automated data ingest, processing and display