## Slide 1: Free Ocean CO2 Enrichment
An illustration of the atmospheric CO2 increase and the change in ocean pH

## Slide 2: FOCE and OA Research
Free Ocean CO2 Enrichment experiments are based on an existing base of scientific work that started in the early 1990’s. The Free Air CO2 Enrichment (FACE) experiments.
Dr. Peter Brewer first proposed this type of experiment to MBARI engineering in 2003 as part of his greenhouse gases research. The drawing to the right is the initial concept from engineering and presented to NOAA’s Dr. Dick Feely later that year.
Concept using the MARS cable in Monterey Bay, later deployed as deep FOCE (dpFOCE)

## Slide 3
Why xFOCE?
The problem: Some scientists are misinterpreting our publications and what is required to make a FOCE system work.
MBARI was contacted and we gave feedback about how to use the existing hardware and reconfigure it to become a functional FOCE.
The scientist did some of it but still didn’t grasp what FOCE is an how to properly set up a system to get meaningful science results.
It became apparent that a resource clearly outlining FOCE and how to get started would be useful.

## Slide 4: xFOCE
European FOCE (eFOCE) is currently under construction and scheduled for deployment in May 2012. This system uses a cable but the CO2 is delivered in bottles to a surface expression.
Deep FOCE (dpFOCE) is the original FOCE built for multi-science users on a cabled observatory.
Coral Prototype FOCE (cpFOCE) is the first tech transfer of FOCE built for multi-science users on the Great Barrier Reef. Solar and wind powered except for the creation of the enriched CO2 water.
Antarctic FOCE (antFOCE) proposal submitted and partially funded. Proposal for other 50% of funding underway.

## Slide 5: xFOCE
xFOCE shall support 2 test chambers (1 active and 1 control)
xFOCE shall maintain a desired pH offset from ambient within +/- .2 pH
xFOCE shall be capable of pH offsets of between .2 and .8 pH units
xFOCE shall hold a selected pH offset for a minimum of 2 weeks
xFOCE shall be capable of deployments greater than 6 months in duration
xFOCE shall be fully functional in external currents of 50 cm/sec
xFOCE shall mimic surge to the extent possible based on chamber scale
xFOCE shall maximize the allowance of full spectrum natural light
xFOCE shall include pH, CTD, O2, flow rate or calculated flow using velocity

## Slide 6: xFOCE
xFOCE shall provide internal environmental data for all instruments on the required list from each active chamber
xFOCE shall provide internal environmental data for
xFOCE shall be diver maintainable
xFOCE shall not use materials that are toxic to the marine environment
xFOCE shall not be dangerous to maintenance divers
xFOCE shall minimized impacts on local marine life
xFOCE shall be capable of being fully recovered and leave no components behind
xFOCE shall be capable of being built, installed and maintained by a typical university oceanographic research lab with a minimum of 1 scientist and 2 graduate students

## Slide 7: xFOCE
xFOCE shall maximize use of commercially “off-the-shelf” or readily available technology to the fullest extent possible
xFOCE shall be capable of working in ocean waters where the velocity does not exceed 75 cm/sec.

## Slide 8: swFOCE
swFOCE shall meet all xFOCE requirements
swFOCE shall not require a support ship greater than 50’ for deployment and recovery
swFOCE shall include a camera system capable of variable time lapse digital data collection suitable for publication, the camera (and light source if included) shall also be adjustable within the swFOCE structure
swFOCE shall use the Stanford Hopkins
Marine Station’s submarine cable
swFOCE shall provide a separate power and communications links form the planned Hopkins science use and will not interfere with other science operations.

## Slide 9: xFOCE Concept of Ops cable
Science interface on shore
CO2 and Enriching process on shore
Air / sea interface managed using buried cable
Capable of supporting 6 to 8 xFOCE units
(4 active pH chg and 4 control)
Depth rating
min - XX
max - XX
Anchored to bottom
Uses ??? to prevent erosion

## Slide 10: xFOCE Concept of Ops no cable
Science interface on shore
CO2 and Enriching process off shore
Air / sea interface managed using surface expression
Capable of supporting 2 xFOCE units minimum
1 active pH chg and 1 control, 3 active and 3 control desired
Depth rating
max – 40m
Anchored to bottom
Comms by telemetry
Buoy or Platform

## Slide 11: xFOCE Functional Requirements
Max depth: 40m (130 ft)
pH Range: 0.0 to -0.6 continuous based on CO2 available. Brief excursions to -0.8 or -1.0 offset potentially
pH resolution: resolution: 0.05 pH units, 0.1 unit may be OK (prefer best resolution possible)
Temp range: -2 to 30 degrees C
Max ext. velocity: 50 cm/sec
Max int. velocity: 10 cm/sec
Full spectrum light: Max transmission of sunlight at depth
Number of Units: System support for 1 active and 1 control chamber

## Slide 12: swFOCE Additional Requirements
Surge: Imitate surge to extent possible
Temp range: -2 to 30 degrees C
Number of Units: System support for 3 active and 3 control chamber

## Slide 13
xFOCE/swFOCE Concept of Ops
Flow Vel
Science selected velocity

## Slide 14: xFOCE Functional Interfaces
CO2
SW Pump
ESW
ESW Distributor
Data Archive
Data Acquisition
Data
Distribution
Console
Instruments
ESW injector(s)
Flow effector(s)
Camera(s)
Control System
Generation
Storage
Distribution/Protection
GUI
Configuration & Control
Monitoring/
Health/Status
Comms
ESW injector(s)
Flow effector(s)
Mixer
Subsea Electronics
Surface
Subsea
Power
House Power
Science / Control System
Internet
xFOCE Control
Enriched
Seawater
System

## Slide 15: xFOCE Mooring Concept
CO2 Mix Electronics
System Control Electronics
Diesel Fuel
Exhaust used for CO2
Particle Scrubber

## Slide 16
xFOCE Systems concept
Blue circles are included for swFOCE
Proposed minimum instrumentation for an active pH controlled chamber. The blue elements are options and controls would only have CTD and pH. Not shown is the other option of a motor and fan to control flow.

## Slide 17
Shallow Water Corals
Benthic Biology
Multi-Site
Multi- Discipline
Multi-Year
swFOCE Basic Concept
Shallow Water
Off-Shore
Schematic View of the Hopkins Site

## Slide 18
pH Sensor
Thruster
CTDO Sensor
Camera and Light
FOCE Controller
Power and Comm
Cabling
Animal
Restrictor
Anchors
CO2 Enriched Water
swFOCE Concept
Flow meter
Ducting
(Time delay)
Bottomside FOCE chamber for swFOCE
Notes: ----- Meeting Notes (4/26/12 09:45) -----
more contrast

## Slide 19
Sea Level
Intake Filter
Existing Drain at
Hopkins
Barrier End Cap
Sea Water
Low pH Sea Water
Power and Comms
swFOCE Cable Concept

## Slide 20: xFOCE Core Instrument Suite
pH : +/- .01 pH unit or better and suitable for
control loop applications
CTD: Comparable to current units at MBARI, unit is
FastCAT SBE49 (oxygen can be included)
Flow sensor: TBD, likely electromagnetic to get smooth
flow numbers and volumetric data. From dpFOCE acoustic velocity sensors are not suitable.
Suggested architecture allows for expansion of additional instrumentation
PAR* - Photosynthetically Active Radiation
Notes: ----- Meeting Notes (4/26/12 09:45) -----
PAR not mentioned on this slide

## Slide 21: swFOCE Core Instrument Suite
pH : +/- .01 pH unit or better and suitable for control loop applications
CTD: Comparable to current units at MBARI, baseline unit is FastCAT SBE49 (oxygen can be included)
Flow sensor: TBD, likely electromagnetic to get smooth
flow numbers and volumetric data. From dpFOCE acoustic velocity sensors are not suitable.
PAR* Sensor: 400 – 700 nm / calibrated t0 0 – 5000 μmol photons•m -2 •s -1
Camera/Lights: 1080p - 16:9 ratio format – light source either natural and/or color balanced LED
PAR* - Photosynthetically Active Radiation
Notes: ----- Meeting Notes (4/26/12 09:45) -----
aspect ratio

## Slide 22
Humidity Sensor
Flash Storage
CPU
Battery Charger
Voltage Regulator
Deep Cycle Batteries
Wireless Comm
Instrument Interface
Wind ??
xFOCE /swFOCE Components

## Slide 23
CPU
Voltage Regulator
Deep Cycle Batteries
Level Sensor
Small Water Pump
Motor Controller
xFOCE /swFOCE Components

## Slide 24: xFOCE /swFOCE Data Reqs.
Health and Status: Ability to query system status from web page (data dependent on sensors included)
Timing Accuracy: Network Time Protocol (NTP) protocol for synchronizing computers
Sample Rates: System will support 10 Hz standard operation
Basic Data Format: Comma delimited string, time stamped
swFOCE: Compatible with the current dpFOCE data streams and SSDS (Shore Side Data System*)
Near real time ground fault monitoring
*SSDS – Open source from MBARI
Notes: ----- Meeting Notes (4/26/12 09:45) -----
move to elec section, w/ component picture slides
requirements? "data needs?" should have number
NTP is implementation name a number - better than 1 sec required?
specify as abs timing accuracy
specify as
*up to* 10 hz - up to 2 Hz - what is standard operation?
MBARI SSDS
metadata capture - add for swfoce

## Slide 25: xFOCE Engineering Trades
Color Frequency Wavelength
violet 668–789 THz 380–450 nm
blue 631–668 THz 450–475 nm
cyan 606–630 THz 476–495 nm
green 526–606 THz 495–570 nm
yellow 508–526 THz 570–590 nm
orange 484–508 THz 590–620 nm
red 400–484 THz 620–750 nm
infrared longer than 750 nm
Since these wavelengths penetrate water easier but most plastic materials respond poorly to high freq light the materials selections will focus on this end of the spectrum
The selection of materials will likely transmit this end of the spectrum fairly well but in selection, if required, we would trade attenuation here to maximize shorter frequencies.
Acrylic (vs Polycarbonate) has less attenuation overall and carries much further into the ultraviolet when comparing the blue lines.
Notes: ----- Meeting Notes (4/26/12 09:45) -----
move to mechanical (Farley also has version)

## Slide 26: FOCE: A tool to understand local impacts of Ocean Acidification
Funding Provided by The David and Lucile Packard Foundation

## Slide 27: An Idea Takes Shape
Build a consortium of researchers and engineers to tackle large, real-world issue of increasing relevance
Center for Ocean Solutions: Ideal fit to highlight ocean acidification
Hopkins: Cable infrastucture and numerous potential research opportunities
Notes: ----- Meeting Notes (4/26/12 11:22) -----
title: swFOCE takes shape

## Slide 28: Pushing the Limits of Permitting
Brock Woodson initially procured permit from Sanctuary to install cable.
Innovative work, like SW-FOCE, would require the involvement of multiple regulatory agencies
First research project request in recently established MPA, as well as Area of Special Biological Significance
Exposed several shortcomings in permitting process among multiple agencies

## Slide 29: Permits at Every Level
Monterey Bay National Marine Sanctuary
California Coastal Commission
California Department of Fish & Game
Central Coast Regional Water Quality Control Board
City of Pacific Grove
Notes: ----- Meeting Notes (4/26/12 11:22) -----
re-order
time to permit )

## Slide 30: How to Move Forward - Go to the Top
Agencies had no procedures to move forward or interact
Peter Brewer met with Governor Brown
Meg Caldwell helped streamline the process with two key State agencies (CCC & CDFG) through discussions with high level personnel
Notes: ----- Meeting Notes (4/26/12 11:22) -----
enlarge cartoons
stacked jurisdiction overlaps

## Slide 31: Lessons Learned
Allow plenty of time for permitting
  Process took 2 years to complete
Good rapport with agency personnel key
  Not necessarily trying to make life difficult, but often operating within bureaucratic box
Well-placed connections are valuable
Getting the process streamlined is critical to prevent valuable research from being discouraged due to concerns about permitting.
Notes: ----- Meeting Notes (4/26/12 11:22) -----
enlist an advocate who can work w/ beaurocracy
put in terms that agencies can understand: divers, cans of coke
site location can make a difference (map of govt jurisdictions)
early slide - the problem: many agencies, co2 viewed as toxic waste

## Slide 32: Computing elements of xFOCE
(Architecture and system trades)

## Slide 33: Computing Architectures User Concerns
Performance: valid scientific approach, data quality
Flexibility: wide range of environments, scenarios
Ease:
  Build
  Test
  Use, maintain
  Extend
Cost
Notes: ----- Meeting Notes (4/19/12 09:27) -----
power constrained slide 2

## Slide 34: A few assumptions
Implementer profile | Researchers plus 2-4 post docs, grad students 0-1 engineer
Technical | Access to modest manufacturing facilities Software is harder than hardware, mechanical Strong preference for familiar COTS solutions
Implementation schedule | ~6 months
Experiments | Campaign-style deployments 12 month service life Remote and/or restricted sites
Lifecycle | Prefer to extend capability, rather than re-spin from scratch for successive funding rounds

## Slide 35
Controller
Enriched
Seawater
Power
Data
CO2
H2O
FOCE Essentials
Flow
Flow
CTD
pH
CTD
pH
DO
DO2
Flow
ESW
Chamber
External
Notes: ----- Meeting Notes (4/19/12 09:27) -----
pump hard to recognize
workstation graphic
remo
----- Meeting Notes (4/19/12 09:36) -----
expand DO2?

## Slide 36: Computing Architectures Elements
Instruments
Software
Housings
Electronics
Computers
Cabling
For each, many options
Many ways to arrange them
In a FOCE experiment
Notes: ----- Meeting Notes (4/19/12 09:36) -----
computer heads in periodic table
----- Meeting Notes (4/26/12 11:22) -----
graphics aliasing

## Slide 37: Computing Architectures Shrinking the Universe of Trades
Look at decisions that have greatest impact on user concerns
  Build vs Buy
  Location matters: Shore vs Surface vs Seafloor
  Topology: how the pieces are connected

## Slide 38: Build vs Buy General Principles
Buy what you can’t/shouldn’t build
  Processors, instruments, cabling
  Software
Build (or borrow) as needed
  Chambers, housings
  Use COTS components if possible
  Get help on tough key builds
    contract, open source
Beware Frankensystem
  Patchwork integration of COTS parts
  Power consumption
  Rube Goldberg-ness of mechanical/electrical interfaces

## Slide 39: Location Matters General Principles
Connected vs Disconnected
  Generally easier to generate and store power, ESW on shore
  Telemetry bandwidth
Trades for off-shore elements
  Accessibility (to you, the elements, others)
  Reliability
Keep what’s offshore/sub-surface as simple and robust as possible
  Basics: Enriched seawater, power
  HW: Cables, connectors, housings
  SW: Applications, protocols, processes
Play to your application, tech strengths and budget
  Permits, environment
  Experiment duration, depth
  Data access requirements
  Maintenance schedule, spares
  Available design/fabrication resources

## Slide 40
Controller
Enriched
Seawater
Power
Data
What’s inside?
Build or Buy?
Where to put the pieces?
How are pieces connected?
CO2
H2O
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
The software developer sees…
The user needs to consider
Flow
ESW
DO2
Chamber
External
Notes: ----- Meeting Notes (4/19/12 09:45) -----
not clear about thought bubbles

## Slide 41
Some things must be on the seafloor
  Chamber, instruments
  Actuators (pumps, fans, etc.)
But location of everything else is flexible…
  Power, ESW
  Controller
  Data storage, user interfaces
And, there are many ways to implement all of it…

## Slide 42
Our goal is to simplify the choices
Choices depend on experiment and constraints
  Budget, schedule
  Environment
  Technical resources
xFOCE community may draw from different approaches

## Slide 43
A study of some approaches
  Centralized Workstation
  Industrial Computers
  Sensor Node
3 views to evaluate key features and trades
  Build/buy what and why: hardware, software
  Location: shore, surface, seafloor
  Connections: topology and infrastructure

## Slide 44
Next up: Centralized Workstation…
  Workstation computing
  Mixed Common Off The Shelf (COTS) /custom hardware
  Shown here using cabled configuration

## Slide 45
Controller
Power
Data
Grand Centralized Workstation
Location View
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Flow
Component | Location | Why
Controller HW | Seafloor | Experiment continues if comms fails
Controller Software | Seafloor | ‘’
UI Software | Shore | Easier maintenance
Power | Seafloor | Need fine-grained power management at site
Data | Seafloor And Shore | Experiment continues if comms fails
Seafloor
Shore
Surface
ESW
Chamber
External
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow
----- Meeting Notes (4/26/12 11:22) -----
power dist on seafloor,
power source on shore
views grand

## Slide 46
Controller
Power
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Grand Centralized Workstation
Data
Build/Buy
View
Seafloor
Shore
Surface
Flow
ESW
Component | Build/Buy | Implementation
Controller HW | Buy | PC104 Serial port cards (16 total)
Controller Software | Build Open Source | Linux, Java Custom: SIAM Data Acquisition software Open Source: DataTurbine, e.g.
Archive, UI | Build | PC Workstation MacOS, Windows, Linux, Java Custom: Shore Side Data System (SSDS), FOCE GUI
Power | Build | Custom: chassis
ESW | Build | Custom: electronics, software, chassis COTS: pumps, controllers
Chamber
External
Notes: ----- Meeting Notes (4/26/12 11:22) -----
power distribution
define SIAM
label dpFOCE variant
animate to make one slide

## Slide 47
ESW
Flow
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Controller
Power
Data
Data
100 MBps
Ethernet
Serial
1 kW Cable
Grand Centralized Workstation
Ethernet-Serial
Connection
View
Seafloor
Shore
Surface
Ethernet
Chamber
External
Notes: ----- Meeting Notes (4/26/12 11:22) -----
combine connection and location views
animate into one slide

## Slide 48: Summary Centralized Workstation
Pros
  One software platform
  COTS computers
  COTS serial I/O solutions
Cons
  Extensibility in packaging and housings…have to put a lot of holes in housings
    Can use junction boxes
  Power consumption
  Less modular
  Need lots of serial ports
    Custom serial IO
  Custom HW/SW

## Slide 49
Next up: Industrial Computers…
  Industrial automation computers (WAGO, Compact Rio, e.g.)
  Heavy use of COTS hardware and software
  Shown here using moored configuration

## Slide 50
Controller
ESW
Controller
Power
Data
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Component | Location | Why
Controller HW | Surface and/or Shore | Easier access Large housings
Controller Software | Surface And Shore | Co-located w/ HW
UI Software | Shore | Easier maintenance
Power | Surface or Shore | Easier access
Data | Surface and/or Shore | Co-located w/ control
ESW | Shore Or Surface | Permitting, depth, distance from shore
Controller
UI
Seafloor
Shore
Surface
Junction
Flow
Industrial Computers
Location View
Mooring pic
Wireless
Chamber
External
Controller
Notes: ----- Meeting Notes (4/26/12 11:22) -----
say like cpFOCE
move pump to surface

## Slide 51
ESW
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Controller
UI
Seafloor
Shore
Surface
Junction
Flow
Industrial Computers
Build/Buy
View
Chamber
External
Wireless
Controller
Controller
Power
Data
Controller
Component | Build/Buy | Implementation
Controller HW | Build/Buy | COTS: WAGO, National Instruments Compact-Rio (NI-CRIO), Serial Multiplexer (MUX), Video MUX
Controller Software | Build/Buy COTS Open Source | COTS/Custom: LabView Open Source: DataTurbine
Archive, UI | Build/Buy COTS Open Source | PC Workstation MacOS, Windows, Linux Open Source: DataTurbine, RDV, Pachube... COTS/Custom: LabView
Power | Buy Build | COTS: WAGO, NI-CRIO Custom: GF, isolation
ESW | Build/Buy | COTS: WAGO, NI-CRIO, LabView, pumps, motor controllers

## Slide 52
Controller
ESW
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Flow
Controller
Power
Data
Data
Controller
UI
Seafloor
Shore
Surface
Junction
Industrial Computers
ConnectionView
Serial
Ethernet
RF Wireless
WiFi
Cell
Satellite
Controller
Chamber
External

## Slide 53: Summary Industrial Computers
Pros
  Mostly COTS components
  Vendor and user community support
  Easier to build
  COTS software provides much infrastructure
Cons
  High cost of software and hardware
  High power consumption
  Cable may be somewhat technical, especially from surface expression in active environment
  Large electronics form factors require larger housings

## Slide 54
Next up: Sensor Node…
  Focus on small COTS embedded PCs and microprocessors
  Modularize and aggregate power switching and/or data acquisition
  Reduce power consumption
  Shown here using moored configuration

## Slide 55
Controller/
Gateway
Power
Data
Sensor Node
Location View
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Flow
Component | Location | Why
Controller HW | Surface/Seafloor | Surface: telemetry, UI Seafloor: experiment control
Controller Software | Seafloor | Gateway: control, telemetry Node: data acquisition
UI Software | Shore/Surface | Easier maintenance
Power | Surface | Probably use generator, solar, wind on surface
Data | Seafloor And Shore | Local data needed for control Central archive for redundancy, easier access
Seafloor
Shore
Surface
ESW
Controller
/Gateway
Node
Node
Node
Node
Data
Load switching,
Data Acquisition for
1-4 Devices
Chamber
External
Wireless
Experiment Control for 1 chamber
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow
----- Meeting Notes (4/26/12 11:22) -----
say: similar to eFOCE...
ESW pump on surface
bilge pump?

## Slide 56
Wireless
Controller
Gateway
Power
Data
Sensor Node
Build/Buy View
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Flow
Seafloor
Shore
Surface
ESW
Controller
Gateway
Node
Node
Node
Node
Data
Open source:
options./examples vs required
Component | Build/Buy | Implementation
Controller HW | Buy | Gateway: BeagleBoard, Android Node: Arduino, MSP430
Controller Software | Build | Gateway: Linux, Java, C++/Java Node: C/C++, Wiring, e.g.
Archive, UI | Build/Buy | Custom: back end interface Open Source: web server on gateway
Power | Build | Custom: load switch, GF/iso
ESW | Build/Buy | 
Chamber
External
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow
----- Meeting Notes (4/26/12 11:22) -----
mention sensor node

## Slide 57
Node
Node
Node
Node
Controller
Gateway
Power
Data
Sensor Node
Connection
View
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Flow
Seafloor
Shore
Surface
ESW
Controller
Gateway
Data
Ethernet
(Serial?)
Serial
Serial
RF Wireless
Cell
Satellite
WiFi
Chamber
External
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow

## Slide 58: Summary Sensor Node
Pros
  Reduce power
  No custom serial IO expansion
  Modularizes data acquisition
  Many variations possible
    COTS processors, languages
    Topologies
    Connection backbone (cost: power)
    Component upgrades
    Drivers on Gateway
Cons
  Two software development platforms
  More custom hardware to build, configure, maintain
  More cables, connectors, housings
  Video expansion path unclear
  Multiple system clocks
Notes: The Bottom Line
  It’s a good design pattern, with balance of build/buy
  flexible, extensible, moderate cost
  Variants trade complexity, power, modularity

## Slide 59: Approach Tradeoffs
Approach | Performance | Flexibility | Ease |  |  | Cost
 |  |  | Build | Use | Extend | 
Centralized Workstation |  |  |  |  |  | 
Industrial Computer |  |  |  |  |  | 
Sensor Node |  |  |  |  |  | 

Pro
Con

## Slide 60: UI
Help users to understand and simplify key choices
What UI choices will the user make related to UI
  Network, interfaces, security
How do those choices affect concerns (performance, flexibility, ease, cost)
What are pros/cons of various choices
  Cost, power, bandwidth, software skill, processing capability, software/system dependencies
Modularity
  Interfaces that support flexibility in UI choices
  Expansion path: what’s needed up front to start simply and build capability
Sketch out a couple of concepts at either end of the spectrum
Specific choice/detail more important for SWFOCE
Notes: ----- Meeting Notes (4/26/12 11:22) -----
move UI to end SW FOCE
most users won't have GUI, security

## Slide 61: Tethers?

## Slide 62
Questions?

## Slide 63: xFOCE Power/Comms
Chad Kecy
Electrical Engineer

## Slide 64: Intro Slide
Say something smart, dummy!

## Slide 65: Cabled System

## Slide 66: Cabled System
Shore Side
Tether
Underwater Connection
Notes: ----- Meeting Notes (4/26/12 11:22) -----
put on picture before

## Slide 67: Shore Side
Physical Location
Type of Installation
Weather / Environmental Conditions
Power Source
Communication Equipment
Ground Fault Detection / Safety
Permitting?

## Slide 68: Cabled Tether
Power Requirements
Communication Speed/Bandwidth
Length
Strength (Stiffening Rod?)
Number of Conductors
Type of Underwater Connectors
Use of Fiber Optics?
Notes: ----- Meeting Notes (4/26/12 11:22) -----
not use stiffening rod
interface at ocean
trawl protection
anchoring
FO could be subbullet of comms

## Slide 70: High Voltage Source
Advantages
Minimizes i2r losses in cable.
Allows for less copper in cable (less $$)
Disadvantages
Need to down convert to lower DC voltages downstream.
Safety isses
Notes: ----- Meeting Notes (4/26/12 11:22) -----
water blocking
insulation resistance
isses -> issues

## Slide 71: Ethernet Standards
Notes: ----- Meeting Notes (4/26/12 11:22) -----
make sure cable, connectors support speed, length
bends, temp issues
deployment of cable

## Slide 72: Serial Standards
Specifications | RS-232 | RS-422 | RS-485
Mode of Operation | Single-Ended | Differential | Differential
Total # of Transmitters and Receivers | 1 Trans 1 Rcvr | 1 Trans 10 Rcvrs | 32 Trans 32 Rcvrs
Maximum Cable Length | 50 ft | 4000 ft | 4000 ft
Maximum Data Rate | 1MBit/s | 10MBit/s | 10MBit/s
Notes: ----- Meeting Notes (4/26/12 11:22) -----
how about DSL?

## Slide 73: Underwater Connections
Types
  Wet-mateable
  Dry-mateable
Considerations
  Deployment
  Servicing
Notes: ----- Meeting Notes (4/26/12 11:22) -----
ethernet
note: number one failure point
pictures

## Slide 74: Non-Cabled System
Comms by telemetry
Buoy or Platform
Notes: ----- Meeting Notes (4/26/12 11:22) -----
put mechanical in front of electrical
add me slide w/ mooring options: dive platforms, regular moorings,
2+ anchor points, cable, strength member
subsurface moorings

## Slide 75: SW-FOCE Electrical Architecture (Subsea Node)
Chad Kecy
Electrical Engineer

## Slide 76: System Level Functions
Distribution of DC power to external instruments and internal subsystems
Bidirectional communication to external instruments and internal subsystems
Health monitoring for entire the subsea node
Computer
  Collection and dissemination of data
  Closed loop control of the experiment

## Slide 77: DC Power
DC-DC Converters
  Converts input DC voltage to all necessary lower DC bus voltages.
Conditioning and monitoring
  Provides filtering and power monitoring.
Patch Panel
  Distributes lower DC bus voltages to internal subsystems.
Load Switching to individual instruments
  Provides galvanic isolation, over/under current/voltage protection, power monitoring, and ground fault detection to each instrument.

## Slide 78: DC Power Example
48V to 24V
Inrush
Limiting
48V to 12V
Conditioning
Conditioning
Load Switching
Patch Panel
Ethernet
Switch
Computer
pH Probe
CTD
ADCP
Camera
Thruster
12V
12V
24V
24V
Subsea Node

## Slide 79: Instrument Level Power Control
ADCP
Load
Switching
Inrush
Limiting
Volt/Curr
Monitoring
Circuit
Breaker
Volt/Curr
Filtering
Over/Under
Volt/Curr
Detection
ADC
ADC
Amp
Curr Limit
R
Mosfet
Load Switcher
Ground Fault Monitor
12V
Seawater Ref

## Slide 80: Communication
Communication from shore to subsea node
  Factors:
    Is your FOCE tethered or standalone?
    Distance
    Bandwidth requirements
    Shore based infrastructure
  Potential choices:
    Tethered: Ethernet, RS-422, DSL
    Standalone: Wireless ethernet
Communication from subsea node to individual external instruments
  Most instruments utilize serial comms
    RS-232 and RS-485 most common

## Slide 81: Communications Example
Video
Server
Ethernet
Switch
Computer
pH Probe
CTD
ADCP
Camera
Thruster
Subsea Node
Serial
Expander/Server
Serial
UARTs +
Transceivers
Notes: ----- Meeting Notes (4/26/12 11:22) -----
solid and dotted lines - label

## Slide 82: System Health Monitoring
Provides top side users with status of environmental conditions in the subsea node.
Can be used to automatically power down instruments in the event of a failure.
Conditions measured:
  Temperature
  Humidity
  Water presence
  Housing pressure
  Orientation
Notes: ----- Meeting Notes (4/26/12 11:22) -----
make sure we separate xFOCE from swFOCE

## Slide 83: Health Monitoring Example
Thermocouple
Health
Monitor
Ethernet
Switch
Computer
Subsea Node
48V to 24V
48V to 12V
Ambient Temp
Ambient Humidity
Ambient Pressure
H2O Sensor
Thermocouples
Cooling Fan
Notes: ----- Meeting Notes (4/26/12 11:22) -----
for sensor nodes, where is it env monitoring needed

## Slide 84: Central Computer
Can be of almost any variety based upon intended usage in subsea node.
Potential usage:
  Collection and dissemination of data from external instruments and internal subsystems.
  Performing the closed loop operation control of the pH experiments.
  Housing the individual instrument drivers.
Notes: ----- Meeting Notes (4/26/12 11:22) -----
Control

## Slide 85: Four Potential Architectures
1. PC/104 Stack
2. Wago I/O System
3. Instrument Chassis
4. Device Appliance Controller
Notes: ----- Meeting Notes (4/26/12 11:22) -----
Sensor Node
Instrument Chassis
This is only for

## Slide 86: PC/104 Stack
What is PC/104?

## Slide 87: PC/104 Stack
Modules available (multiple manufacturers):
  CPU
  Data storage
  Power Supply
  Digital I/O, Analog I/O (DAQ)
  Relay control
  Serial expansion
  Environmental input (temp, hum, etc…)
  Video Server/Encoder
  Ethernet switch
  Others

## Slide 88: PC/104 Stack
Advantages
Rapid prototype/design
Expandable/reconfigurable
Extensive functionality
Relatively inexpensive
Industry standard
Often software drivers included
Can incorporate custom boards
Disadvantages
Power consumption
Maintenance
  Need to disassemble the stack to get to middle boards.
Limit on # of boards in stack
Sometimes, no software drivers….

## Slide 89: PC/104 Stack
Function | Model # | Manufacturer | Notes | Watts | Cost | Quan | Tot Watts | Tot Cost
Computer | Cool RoadRunner-LX800 | Lippert |  | 6.5 | 500 | 1 | 6.5 | 500
Storage | 500Gb Scorpio Blue | Western Digital |  | 4 | 100 | 1 | 4 | 100
Power Supply | HE104+ DX | Tri-M |  | 10 | 300 | 1 | 10 | 300
Load Switching | DM6956 | RTD Embedded Tech | 16 Channels | 5 | 500 | 2 | 10 | 1000
Circuit Breaker | N/A |  |  |  |  |  |  | 
Ground Faulting | N/A |  |  |  |  |  |  | 
Load Power Monitoring | MM-32DX-AT | Diamond Sys | 32 Chan Analog | 3 | 600 | 1 | 3 | 600
Environmental Sensing | Model 518 | SensoRay | Temp/Hum only | 1 | 325 | 1 | 1 | 325
Serial Expansion | Xtreme/104-Plus Port | Connect Tech | 16 Channels | 4 | 350 | 2 | 8 | 700
 |  |  |  |  |  |  | 42.5 | 3525

## Slide 90: Wago I/O System
What is a Wago I/O System?
Notes: ----- Meeting Notes (4/26/12 11:22) -----
Industrial Computer

## Slide 91: Wago I/O System
Modules available:
  Controller
  Power Supply
  Relay Modules
  Digital I/O, Analog I/O (DAQ)
  Thermocouple inputs
  DC Motor Driver
  Others

## Slide 92: Wago I/O System
Advantages
Rapid prototype/design
Expandable/reconfigurable
Industry Standard
Generic software interface
Can incorporate custom boards
Disadvantages
Limited functionality for our requirements
  More custom designs
Power consumption

## Slide 93: Wago I/O System
Function | Model # | Manufacturer | Notes | Watts | Cost | Quan | Tot Watt | Tot Cost
Computer | 750-341 | Wago | Eth-Fieldus Coupler | 12 |  | 1 | 12 | 0
Storage | N/A |  |  |  |  |  | 0 | 0
Power Supply | N/A |  |  |  |  |  | 0 | 0
Load Switching | 857-304 | Wago | Single SPST Relay | 0.5 |  | 20 | 10 | 0
Circuit Breaker | N/A |  |  |  |  |  | 0 | 0
Ground Faulting | N/A |  |  |  |  |  | 0 | 0
Load Voltage Monitoring | 750-483 | Wago | Dual Voltage Analog Inputs | 2 |  | 10 | 20 | 0
Load Current Monitoring | 750-475 | Wago | Dual Current Analog Inputs | 2 |  | 10 | 20 | 0
Envr Sensing - Temp | 750-469 | Wago | Dual Thermocouple input | 1.5 |  | 3 | 4.5 | 0
Envr Sensing - Hum |  |  |  |  |  |  | 0 | 0
 |  |  |  |  |  |  | 0 | 0
Serial Expansion | N/A |  |  |  |  |  | 0 | 0
 |  |  |  |  |  |  | 66.5 | 

## Slide 94: Instrument Chassis
What is the Instrument Chassis?

## Slide 95: Instrument Chassis
Modules available:
  CPU Board
  Power Supply
  Environmental Monitoring Board
  Low Voltage Load Switcher (8 channels)
  Medium Voltage Load Switcher (4 channels)
  Ground Fault Detection Board (16 channels)
  Others

## Slide 96: Instrument Chassis
Advantages
Was designed specifically for use in the shallow water FOCE system
Modular; new boards can be designed.
Low Power design
Simple software interface
Disadvantages
Design complexity
Expensive to produce
Custom firmware needed
Currently, no serial expansion included

## Slide 97: Instrument Chassis
Function | Model # | Manuf | Notes | Watts | Cost | # | Tot Watt | Tot Cost
CPU |  | MBARI |  | 0.680 | 253 | 1 | 0.680 | 253
Power Supply |  | MBARI |  | 0.335 | 324 | 1 | 0.335 | 324
Backplane |  | MBARI |  | 0.000 | 193 | 1 | 0.000 | 193
Environmental Board |  | MBARI | 8-hum, 4-temp, pressure, X,Y,Z, H2O Sense | 0.200 | 316 | 1 | 0.200 | 316
Low Voltage Load Switcher |  | MBARI | 8-channels, 0-24V | 0.250 | 550 | 3 | 0.750 | 1650
Medium Voltage Load Switcher |  | MBARI | 4-channels 24V-48V | 0.250 | 425 | 1 | 0.250 | 425
Ground Fault Detection Board |  | MBARI | 16-Channels (with 4 HV) | 0.200 | 325 | 1 | 0.200 | 325
 |  |  |  |  |  | Q | 2.4 | 
 |  |  |  |  |  | Act | 10 | $3,486

## Slide 98: Device Appliance Controller
What is the Device Appliance Controller?
Pluggable
CPU
Module
BeagleBone?
Arduino?
Microchip PIC?
UART
Serial Transceiver
Load Switching
Ground Fault Detection
Over/Under
Curr/Volt
Det / Mon
Inrush
Limiting
Circuit
Breaker
DC Power from Bus
Ethernet Comms from Switch
DC Power to Instrument
Serial comms to Instrument
Notes: ----- Meeting Notes (4/26/12 11:22) -----
smart sensor, android

## Slide 99: Device Appliance Controller
Modules available?
  None, it is a fully functional standalone unit
  One instrument per DAC card
Functions available:
  CPU, storage
    Device driver could be stored locally
  Serial interface (uart + transceiver)
  Load switching
    Over/under curr/voltage detection
    Ground fault monitoring
    Current/Voltage monitoring
Notes: ----- Meeting Notes (4/26/12 11:22) -----
one per sensor node? limited number
device driver could run locally

## Slide 100: Device Appliance Controller
Advantages
All functions on one board
CPU simple to program
Single board design can handle a large variety of instruments
Open source HW and SW
Disadvantages
Custom design
Cost?
Distribution

## Slide 101: Architecture Comparison
 | PC/104 | Wago | Instrument Chassis | Appliance Controller
Central CPU | Yes | No | No | No
Local CPU | No | Yes | Yes | Yes
Local Storage | Hard Drive | No | SD Card | ?
Ethernet Interface | Yes | Yes | Yes | ?
Serial Expansion | Yes | No | No | One per
Load Control Relays | Yes | Yes | Yes | Yes
Circuit Breaker Protection | No | No | Yes | Yes
Inrush Limiting | No | No | Yes | Yes
Ground Fault Detection | No | No | Yes | Yes
Thermal Inputs | Yes | Yes | Yes | Yes
Humidity Inputs | Yes | No | Yes | Yes
H2O Sensor Inputs | Yes | Yes | Yes | Yes
Pressure Sensor Input | Yes | Yes | Yes | Yes
3-Axis Orientation | No | No | Yes | ?
Power Usage (Watts) | 45 | 70 | 10 | 
Cost per System ($) | 3500 |  | 3486 | 

## Slide 102
Mechanical Components Comprising xFOCE / swFOCE Farley F. Shane

## Slide 103: xFOCE Mechanical Sub-Systems
        Seafloor System
          Experiment Chamber
          Ancillary Support Equipment
        Surface Support Systems
          Seawater Enrichment System
            Generation
            Delivery
          Power
Notes: ----- Meeting Notes (4/26/12 11:22) -----
move before chad
order:
architecture, me, sw (ui,data), ee?
architecture, me, ee, sw (ui,data)?
put surface above seafloor

## Slide 104: Typical Seafloor System Comprising an xFOCE
Delay Path Section
Delay Path Section
Experiment Chamber
Seawater Inlet
Seawater Inlet
Conformal Sealing Mat(s)
Chamber Anchors (at 4 corners)
Enriched Seawater Delivery Line
From Surface
Scour Protection Elements
As needed
Scour Protection Elements
Perimeter Weights
Fan
Fan
Notes: ----- Meeting Notes (4/26/12 11:22) -----
larger, brighter
hard to make out what's there
elim one hose?

## Slide 105
Experiment Chamber
Requirements
  Diver Accessible
    40 meters or less
  Design focus on modularity
    Addition, Removal, or maintenance of equipment and instrumentation
  Sized for desired site and area of experimentation.
  Capable of accommodating all required instrumentation and ancillary equipment.
  At least one seawater entrance and one exit.
    Permits local current access.
    Permits active simulation of local current.
      Fan or Pump
  Access Hatch(es)
    Internal observation subject access.
    Access for maintenance of chamber, internal instrumentation, and ancillary equipment.
  Delay Path Connections
    Inlet to the Chamber for the mixed Enriched Seawater.
    Permits attachment of the duct
    Inlet for nutrients
  Anchoring points
  Site Interface Seal
    Mitigate enriched seawater leakage/ intrusion.
    Inhibit undesired local critter incursion.
  Optional
    Local surge internally translated by mechanical or other method.
    Detachable baseplate for securing to the site for ease of replacing/cleaning chamber.
Notes: ----- Meeting Notes (4/26/12 11:22) -----
elim slide, use pictures on next slide
[
reduce text
elim diver stuff, design focus...,
highlight size number
Permits local...
many sub bullets
]

## Slide 106: Sample Experiment Chambers
MBARI Deep FOCE
Trapezoidal
Hemi- Cylindrical
SWFOCE Prototype
Modular Fan Section
Surge Translation Paddle
Access Hatches
Side Access Opening
(Hatch Not Shown)
Handle
Conformal Seal
Surface Available for Instrumentation
Perimeter Shear Skirt
Fitting for Time
Delay Section
Anchors
Experiment Chamber
Subsea CO2 Reservoir
Delay Path
Enriched SW
Control System in
Pressure Housing
Fans to
Control Current
Buoyancy Blocks
Delay Path
Exo-Frame
Fan
Fan
Notes: ----- Meeting Notes (4/26/12 11:22) -----
make this section (me) earlier in order
use swfoce test chamber upgrades
talk modularity, shape choices

## Slide 107
Integral Delay Path
Sample Experiment Chambers
(Cont.)
Exhaust
Fan
Guggenheim Museum/Stadium Concept
Inlet vents
Experiment Chamber
Exhaust Vents
Transparent Cover
Polyethylene film
Frame made of plastic or metal tubing.
Requires a fairly benign environment.
Translates surge.
Isolates waterborne nutrients.
Requires creative instrument attachment.
Submersible Habitat for Analyzing Reef Quality (SHARQ)
Compliant Chamber
(Not a FOCE as shown)
Enriched SW
Inlet
Notes: ----- Meeting Notes (4/26/12 11:22) -----
eliminate

## Slide 108: Chamber Shear Skirt and Interface Seal
Chamber Shear Skirt
  Extend into the seafloor 8-10 cm.
    Resists lateral movement
    Seals perimeter of chamber at seafloor
    Assists in preventing critter intrusion
Chamber Interface Seal
  Extend 30 – 40 cm on seafloor surface from perimeter of Chamber
  Assists in sealing chamber at uneven seafloor surface
  Can assist in scour prevention and erosion from currents
  Variety of applicable materials
    Canvas
    Reinforced Plastic Sheet
    Rubber/Nitrile/ sheet
  Should be weighted
    Lead
    Concrete blocks
    Grout Bags
Notes: ----- Meeting Notes (4/26/12 11:22) -----
use pictures of real unit w/ arrows, main bullets

## Slide 109: Time Delay Mixing Section
Duct that provides the necessary time for the CO2
and seawater to chemically react and establish
a stabilized pH.
Reference the Zeebe-Wolf Gladrow CO2 Kinetic
Model to determine Tau (shown previously and
here).
Duct length is determined by using a 2 Tau time delay and the desired maximum current speed.
The cross-sectional area and the current speed
(volume/time) will approximate the rate of change
of the enriched seawater in the Experiment Chamber.
Tau = 67.8 secs
Tau = 51.3 secs
Tau = 31.1 secs
Offset pH = -0.7
Offset pH = -0.3
Bkgrd pH ~ 8.1
*
*
*
*
Offset pH = -0.5
Curves from the Zeebe-Wolf Gladrow CO2 kinetic model
showing e-folding time at various temperatures as a function of pH.
Flexible Duct
Commonly used for air handling
Integrated coil to maintain flow (use plastic instead of metals)
Use all plastic.
2 “ - 12” diameter commonly available
Low cost
Notes: ----- Meeting Notes (4/26/12 11:22) -----
reduce text
use pictures
elim Referenct to Zeeb....
combine bullets on Ducts

## Slide 110
Trolling Motors
  Compatible with shallow depths
  Reasonably predictable reliability (MTBF)
  Easy maintenance/replacement
  Compatible with available power (AC/DC, etc.)
  Controllable according to requirements
  Capable of reasonable volume/rate delivery
Commercial Thrusters
  Technadyne Model 520 DC Brushless - $3700, 520 Watts, various voltages available, analog or digital control, magnetically coupled prop
  CrustCrawler 400 HFL - $600, 0-50 VDC, 400 watts, lip seals, 300 ft
Submersible Bilge Pumps
  Compatible with shallow depths
  Large range of flow rates
  Large range of DC voltages
  Readily available/replaceable
  Very inexpensive
  Brand Names: Rule, Attwood, Lovett, Johnson, Jabsco,…
  May need replacing more often
  Not designed to run continuously
Components to Simulate Current
Submersible Bilge Pump
Commercial Thruster
Trolling Motor
Notes: ----- Meeting Notes (4/26/12 11:22) -----
use trade table
keep pictures

## Slide 111
Disk Theory for Moving Water
Ppropellor x RPM x Areapropellor / 100 = Volumewater / minute
Where:
* Ppropellor = Propellor Pitch (cm.)
RPM = Revolutions per minute
Areapropellor = Area of the diameter projected by rotated propellor (cm. sq.)
Volumewater = volume of water moved by propellor (liters)
*NOTE: Pitch is defined as "the distance a propellor would move in one revolution
if it were moving through a soft solid, like a screw through wood." For example,
a 21-pitch propellor would move forward 21 inches (53.3 cm) in one revolution.
Custom Thruster using Propellor and Motor
Components to Simulate Current
Equation for motor H.P. Requirement
HP = (psi x GPM) / (1714 x efficiencyMotor)
(Cont.)
Notes: ----- Meeting Notes (4/26/12 11:22) -----
use for reference material (elim slide)

## Slide 112
Anchors
  Related to type of seafloor, longevity, access, etc.
    Semi, Consolidated, and Unconsolidated Sand, Silt, and Clay
      Deadweight
        Concrete Block
        Other
      Direct Embedment
        Helix
        Keyed Plate
      Drag Embedment (Primarily for buoy moorings)
        Danforth, CQR, Delta, Bruce, etc.
      Self –Burying (Better for loose sand, silt)
        Dor-Mor
        Mushroom
    Rock and Coral
      Deadweight
        Concrete Block
        Other
      Direct Embedment
        Powder Actuated Stud Gun (down to 46 meter (150’) depth)
        Epoxied Stud (Drilled hole)
        Expansion Bolt (Drilled hole)
Anchoring
Notes: ----- Meeting Notes (4/26/12 11:22) -----
use picture slide, trade table

## Slide 113
Examples of Anchors
Single or
Multiple Helix
CQR
Danforth
Installation of
Anchor Pins
Powder Actuated Stud Gun
Dor-Mor
Claw or Bruce
Self Embedment Anchors
Drag Embedment Anchors for Mooring Buoy
Epoxied Anchor Pins in Coral
Deadweight Block
Helix Anchor

## Slide 114
Helix type easy to install by diver
  Screw-It Beach anchor, removable handle, Corrosion resistant - $70
  Ironwood Pacific – 21”, 4” helix, powder coated steel, $40 each
  MilSpec Anchors -- set of 4 for $23
Keyed Plate type requires digging out for retrieval
  Triangular earth anchors with galvanized cables, set of 4. ~$40
Drag embedment anchors require setting by boat.
Installation of anchor pins require drilling holes in coral or rock.
Anchor Notes
SWFOCE method of securing anchor to frame
Notes: ----- Meeting Notes (4/26/12 11:22) -----
matl for trade table

## Slide 115
  This system mixes CO2 with seawater and delivers the enriched seawater to each Seafloor Experiment System.
  The Delivery System is comprised of at least the following components:
    Mixing Tank
      Contains CO2 and seawater at 2 atmospheres.
      Designed for the creation and buffered storage of
      enriched seawater.
      Adequate volume to supply the requirements for all Experiment Systems
      Vaporizing Nozzle(s) to create enriched seawater
      Instrumentation to assure adequate monitoring and mixing of enriched seawater.
    Pump and Motor
      Provides recirculating seawater to mixing tank
      Provides enriched seawater to experiment systems
    Seawater Delivery Source
    CO2 Delivery Source
    Ancillary equipment and instrumentation
      Valves
      Gauges
      Filters
      Sensors
Enriched Seawater Generation and Delivery
Notes: ----- Meeting Notes (4/26/12 11:22) -----
use simple picture slide

## Slide 116
(SWFOCE shown)
Enriched Seawater Generation and Delivery
(Cont.)
Notes: ----- Meeting Notes (4/26/12 11:22) -----
do cartoon style
explain why we rain down instead of bubble up, etc.
partial pressures (2 atm)

## Slide 117
Supporting Information
Source: U.S. Environmental Protection Agency, "Emission Facts: Average Carbon Dioxide Emissions Resulting from Gasoline and Diesel Fuel," February 2009. | 
Carbon Dioxide Emissions from 1 gallon of fuel
Optional CO2 Use from Exhaust
Notes: ----- Meeting Notes (4/26/12 11:22) -----
shrink epa , enlarge others

## Slide 118: Power for XFOCE
Onshore Power
  Power supply Unit
  UPS
Diesel Generator
3500 Watt Output
0.3 Gallon per Hr.
Remote Location Power
Onshore or Offshore
  Diesel Generator
    Bonus of CO2 generation
  Wind Powered Generator
    Batteries
  Solar Cells
    Batteries
Wind Generator
400 Watt Output
240 Watt Panel
Notes: ----- Meeting Notes (4/26/12 11:22) -----
mention fuel cell (cost, mostly mil backup, made to run at one power, hard to regulate)
wind, solar inconsistent,
even diesel needs batteries
we can produce 50 W continuous solar wind
put this before diesel picture: advantage: combine CO2 and energy

## Slide 119
Power from Solar Cells on Buoy
Option for Power to Remote xFoce
Notes: ----- Meeting Notes (4/26/12 11:22) -----
shrink and combine

## Slide 120
Estimation of Shallow-FOCE CO2 enriched seawater release rate: |  |  |  |  |  |  |  |  |  | 
Assumptions: |  |  |  |  |  |  |  |  |  | 
 | 1. Shallow FOCE is smaller than FOCE at MARS by 1/2: 0.5m X 0.5m. |  |  |  |  |  |  |  |  | 
 | 2. Water velocity thru flume set as "on average" a 1 cm/s flow through chamber. |  |  |  |  |  |  |  |  | 
 |  | - residence time for a 1 meter length chamber is 100 secs. |  |  |  |  |  |  |  | 
 |  | - internal cyclic flow indiced by a paddle. |  |  |  |  |  |  |  | 
 |  | cm/sec | ht (m) | w (m) |  |  |  |  |  | 
 |  | 10 | 0.5 | 0.5 | 25 | L/s |  |  |  | 
 | 3. Concentration of CO2-ESW: |  |  | 40 | mM | pH: | 4.75 |  |  | 
 | 4. FOCE uses different amounts of CO2 depending upon pH offset: |  |  |  |  |  |  |  |  | 
 |  |  |  |  | Vol CO2-ESW |  |  |  | Amt CO2 | 
 |  | pH offset | +TCO2 | Amt CO2 | mL/s | L/min | L/day |  | kg/day | lb/day
 |  |  | μmol/kg | µmole/s |  |  |  |  |  | 
 |  | 0.2 | 74.5 | 1862.5 | 46.563 | 2.794 | 4023 |  | 7.082 | 15.61
 |  | 0.4 | 136.1 | 3402.5 | 85.062 | 5.104 | 7349 |  | 12.938 | 28.52
 |  | 0.8 | 257.3 | 6432.5 | 160.813 | 9.649 | 13894 |  | 24.459 | 53.92
 |  | 1.5 | 767.7 | 19192.5 | 479.813 | 28.789 | 41456 |  | 72.978 | 160.89
XFOCE Website Reference Material
Spreadsheet
Notes: ----- Meeting Notes (4/26/12 11:22) -----
reference matl

## Slide 121
 |  | FOCE Delay Section Lengths and Flow(Q) |  |  |  |  |  |  | 
Assumption for this version - pH delta of - 0.3, 10 deg. C, so 2 Tau ~ 135 seconds |  |  |  |  |  |  |  |  | 4/2/2012
 |  | -Ambient pH ~8.1 |  |  |  |  |  |  | 
 |  | -Mixing Section is Round tubing or pipe |  |  |  |  |  |  | 
 |  | -Flow thru Test Section is the bulk (average) flow |  |  |  |  |  |  | 
INPUTS | 47.0 | cm, Height of Test Section |  |  |  | Note: swFOCE dim's Ht, W, L |  |  | 
 |  |  |  |  |  |  | 47cm,49cm, 2m |  | 
 | 49.0 | cm, Width of Test Section |  |  |  |  |  |  | 
 | 2.0 | meters, Length of Test Section |  |  |  |  |  |  | 
 | 2 | cm/second, Flow velocity in Test Section |  |  |  |  |  |  | 
 | 30.5 | cm, Diameter of Mixing Section tubing |  |  |  | 12.0 | inches |  | 
RESULTS | 2303.0 | cm sqd, Cross Sectional Area of Test Section |  |  |  |  |  |  | 
 | 730.2 | cm sqd, Cross Sectional Area of Mixing Section |  |  |  |  |  |  | 
 | 6.3 | cm/sec, Flow vel in mixing section |  |  |  |  |  |  | 
 | 8.5 | meters, Length of mixing section req'd for 2 Tau |  |  |  |  |  |  | 
 | 4.6 | Liters/sec, Quantity of S.W. req'd |  |  |  |  |  |  | 
 | 16582 | Liters/hr |  |  |  |  |  |  | 
 | 4381 | Gallons/hr |  |  |  |  |  |  | 
 | 100 | seconds, Residence Time in Test Section |  |  |  |  |  |  | 
XFOCE Website Reference Material
Spreadsheet
Notes: ----- Meeting Notes (4/26/12 11:22) -----
reference

## Slide 122: Flow Rate of Stabilized Enriched Seawater Relative to Chamber Cross-Section and Internal Current Speed
Cross Section of Experiment Chamber | 2 cm/sec | 4 cm/sec | 6 cm /sec | 8 cm/sec | 10 cm/sec
.5 m x .5 m | 602 (159) | 1200 (317) | 1802 (476) | 2400 (634) | 3001 (793)
.25 m x .25 m | 299 (79) | 450 (119) | 901 (238) | 1200 (317) | 1503 (397)
.13 m x .13 m | 151 (40) | 299 (79) | 450 (119) | 598 (158) | 749 (198)
*Liters/minute (Gallons/minute)
NOTE: The relative cross-sectional areas of the time delay mixing section (provides
delivery of stabilized enriched seawater) and the experiment chamber must
be considered when desiring to minimize the time for stabilizing pH in the
chamber.
*3.785 liters = 1 gallon
Current Speed
XFOCE Website Reference Material
Notes: ----- Meeting Notes (4/26/12 11:22) -----
reference matl not in talk

## Slide 123
Polycarbonate-colored or clear
Nearly unbreakable
Scratch resistant
Relatively easy to fabricate
Excellent corrosion resistance
High notch sensitivity (crack propagation)
Difficult to saw
Visible light transmission good ~86%
Yellows when exposed to UV
Acrylic- colored or clear
Fair impact resistance
Excellent corrosion resistance
High notch sensitivity (crack propagation)
Difficult to work with
Requires non-solvent based cutting fluid during fabrication
Visible light transmission is very good, 92%
UV transmission falls off rapidly at ~350 nm
  G UVT formulation available with 275 nm cut-off
Less yellowing from UV
Easily bonded with methyl chloride, or Weld-On #16
Potential Polymer Materials for Large Panels
PVC – pale blue or clear
Fair impact resistance
Fair notch sensitivity (crack propagation)
Good UV resistance
  Thicker materials retain resistance longer
  Starts to yellow over long term > 20 months
Good chemical resistance
Excellent corrosion resistance
XFOCE Website Reference Material

## Slide 124: Potential Materials and Components
p.2
If using an External Frame to support Panels:
FRP-fiber reinforced plastic (fiberglass)
  Easy to work with
  Available in many structural shapes
  Excellent for long term immersion
  Can dull cutting/boring tools quickly
  Does not hold threads well
  Sheet metal screws can be used in >.25“ thick materials.
6061 Aluminum
  Easy to work with
  Available in many structural shapes
  Corrosion issues when in contact with SS fasteners
    Insulating washers may be used
  Excellent for long term immersion
    Cathodic protection may be used
PVC - polyvinyl chloride
  Easy to work with
    Drilled and tapped easily
    Bonds well with adhesives
  Available in many structural shapes
  Clear version is UV resistant
    Angles used for reinforcing edges allow good passage of light
UHMW- ultra-high molecular weight polyethylene
  Easy to work with
  Common shapes are sheets, bars, rods
  Lower specific gravity than seawater
  Black formulation precludes light but is UV resistant
(Cont.)
XFOCE Website Reference Material
LATCHES
  Must be sturdy
  Corrosion resistant
  Easily operated by diver with gloves on
  Commercially available
    Cabinet type, SS
    Block and pin, plastic or SS
  Custom Design
    Cam lock, single or paired
    Other
HINGES
Must be sturdy, corrosion resistant
-piano type, SS
-solid rubber, 1/8-1/4” thick, screwed in with facing plate
FASTENERS
Use stainless steel
  316 is preferable, 18-8 is acceptable
COMPONENTS

## Slide 125: Proven Fabrication Methods
Fastening Angles for Stiffness
Inner Angle
Outer Angle
Use of appropriate materials will maximize light
transmission into the test chamber.
-1/4” Clear Acrylic Panels
-3/16” x 1.5” x 1.5” clear PVC angle used as outside support structure.
-3/16” x1.25” x1.25” clear PVC used inside.
-8-32 x 5/8” screws tapped into inner PVC pieces, 6” Center to Center.
Outer Angle
Wall
Wall
Inner Angle
Clearance
Threaded
XFOCE Website Reference Material
FABRICATION Note: Drilling holes in plastics, polycarbonate and especially acrylic can be difficult because the drill tends to grab and “dig” into the material. Modify the cutting edge of the drill’s flutes by filing or sanding the cutting edge to a more vertical “scraping” edge (i.e. perpendicular to the surface being cut). Keep it sharp and a very nice hole without breakout on the back surface will result.

## Slide 126
Light Transmission through
Polycarbonate and Acrylic
XFOCE Website Reference Material

## Slide 127: 400nm through 700 nm
Photosynthetically Active Radiation (PAR)
(0 Meters)
(4.6 Meters)
(9.1 Meters)
(18.3 Meters)
(22.9 Meters)
XFOCE Website Reference Material

## Slide 128
PVC |  | 
Nominal Pipe Size (inches) | Schedule 40 | Schedule 80
1/2 | 358 | 509
3/4 | 289 | 413
1 | 270 | 378
1 1/4 | 221 | 312
1 1/2 | 198 | 282
2 | 166 | 243
2 1/2 | 182 | 255
3 | 158 | 225
4 | 133 | 194
5 | 117 | 173
6 | 106 | 167
8 | 93 | 148
10 | 84 | 140
12 | 79 | 137
Operating Temp (°F) | De-Rating Factor
73 | 1.00
80 | 0.88
90 | 0.75
100 | 0.62
110 | 0.51
120 | 0.40
130 | 0.31
140 | 0.22
PVC - Polyvinyl Chloride
strong and rigid
resistant to a variety of acids and bases
maximum usable temperature 140oF (60oC)
Operating Depth = 40 Meters (~131 ft.)
Maximum Pressure = .444 x Depth (ft.) +14.7 psi  73 psi
Factor of Safety = 2 Therefore 2 x 73 psi = ~146 psi
Low Cost Shallow Water Pressure Housing Case Fabrication
XFOCE Website Reference Material
Notes: ----- Meeting Notes (4/26/12 11:22) -----
need version in talk for xFOCE: can use PVC
how can scientists make low cost housings
length limits (otherwise get help), depth limits, what machining required, thermal issues
torpedo locks
what other seal options: flanged bolts
consistent units in meters, deg C
safety factor
handling safety (vents): if you're unsure, don't do it