## Slide 1: Computing side of xFOCE
(Computing system trades)
FIXIT

## Slide 2: Computing Architectures User Concerns
Performance: valid scientific approach, data quality
Flexibility: wide range of environments, scenarios
Ease:
  Build
  Test
  Use, maintain
  Extend
Cost
Notes: ----- Meeting Notes (4/19/12 09:27) -----
power constrained slide 2

## Slide 3: A few assumptions
Implementer profile | Researchers plus 2-4 post docs, grad students 0-1 engineer
Technical | Access to modest manufacturing facilities Software is harder than hardware, mechanical Strong preference for familiar COTS solutions
Implementation schedule | A few months to build
Experiments | Campaign-style deployments 12 month service life Remote and/or restricted sites
Lifecycle | Prefer to extend capability, rather than re-spin from scratch for successive funding rounds

## Slide 4
Controller
Enriched
Seawater
Power
Data
CO2
H2O
FOCE Essentials
Flow
Flow
CTD
pH
CTD
pH
DO
DO2
Flow
ESW
Notes: ----- Meeting Notes (4/19/12 09:27) -----
pump hard to recognize
workstation graphic
remo
----- Meeting Notes (4/19/12 09:36) -----
expand DO2?

## Slide 5: Computing Architectures Elements
Instruments
Software
Housings
Electronics
Computers
Cabling
For each, many options
Many ways to arrange them
In a FOCE experiment
Notes: ----- Meeting Notes (4/19/12 09:36) -----
computer heads in periodic table

## Slide 6: Computing Architectures Shrinking the Universe of Trades
Look at decisions that have greatest impact on user concerns
  Build vs Buy
  Location matters: Shore vs Surface vs Seafloor
  Topology: how the pieces are connected

## Slide 7: Build vs Buy General Principles
Buy what you can’t/shouldn’t build
  Processors, instruments, cabling
  Software
Build (or borrow) as needed
  Chambers, housings
  Use COTS components if possible
  Get help on tough key builds
    contract, open source
Beware Frankensystem
  Patchwork integration of COTS parts
  Power consumption
  Rube Goldberg-ness of mechanical/electrical interfaces

## Slide 8: Location Matters General Principles
Connected vs Disconnected
  Generally easier to generate and store power, ESW on shore
  Telemetry bandwidth
Trades for off-shore elements
  Accessibility (to you, the elements, others)
  Reliability
Keep what’s offshore/sub-surface as simple and robust as possible
  Basics: Enriched seawater, power
  HW: Cables, connectors, housings
  SW: Applications, protocols, processes
Play to your application, tech strengths and budget
  Permits, environment
  Experiment duration, depth
  Data access requirements
  Maintenance schedule, spares
  Available design/fabrication resources

## Slide 9
Controller
Enriched
Seawater
Power
Data
What’s inside?
Build or Buy?
Where to put the pieces?
How are pieces connected?
CO2
H2O
Flow
Flow
CTD
pH
CTD
pH
DO
DO2
The software developer sees…
The user needs to consider
Flow
ESW
Notes: ----- Meeting Notes (4/19/12 09:45) -----
not clear about thought bubbles

## Slide 10
Some things must be on the seafloor
  Chamber, instruments
  Actuators (pumps, fans, etc.)
But location of everything else is flexible…
  Power, ESW
  Controller
  Data storage, user interfaces
And, there are many ways to implement all of it…

## Slide 11
Our goal is to narrow the choices
Choices depend on experiment and constraints
  Budget, schedule
  Environment
  Technical resources
xFOCE community may draw from different approaches

## Slide 12
A study of some approaches
  Grand Centralized Workstation
  Industrial Computers
  Sensor Node
3 views to evaluate key features and trades
  Build/buy what and why: hardware, software
  Location: shore, surface, seafloor
  Connections: topology and infrastructure

## Slide 13
Next stop: Grand Centralized Workstation…
  Workstation computing
  Mixed COTS/custom hardware
  Shown using cabled configuration (it’s not the only way)

## Slide 14
Controller
Power
Data
Grand Centralized Workstation
Location View
Data
Flow
Flow
CTD
pH
CTD
pH
DO
DO2
Flow
Component | Location | Why
Controller HW | Seafloor | Experiment continues if comms fails
Controller Software | Seafloor | ‘’
UI Software | Shore | Easier maintenance
Power | Seafloor | Need fine-grained power management at site
Data | Seafloor And Shore | Experiment continues if comms fails
Seafloor
Shore
Surface
ESW
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow

## Slide 15
Controller
Power
Data
Flow
Flow
CTD
pH
CTD
pH
DO
DO2
Grand Centralized Workstation
Data
Build/Buy
View
Seafloor
Shore
Surface
Flow
ESW
Component | Build/Buy | Implementation
Controller HW | Buy | PC104 16 serial ports
Controller Software | Build Open Source | Linux/Java SIAM Open Source Dataturbine
Archive, UI | Build | PC Workstation MacOS, Windows, Linux, Java SSDS Custom FOCE GUI
Power | Build | Custom chassis
Data | Build | SIAM SSDS Open Source
ESW | Build | Custom electronics, Software, chassis COTS pumps, controllers

## Slide 16
ESW
Flow
Flow
Flow
CTD
pH
CTD
pH
DO
DO2
Controller
Power
Data
Data
100 MBps
Ethernet
RS232
1 kW Cable
Grand Centralized Workstation
Ethernet-Serial
Ethernet
Connection
View
Seafloor
Shore
Surface

## Slide 17: Summary Grand Centralized Workstation
Benefits
  One software platform
  COTS computers
  COTS serial I/O solutions
Costs
  Extensibility in packaging and housings…have to put a lot of holes in housings
    Can use junction boxes
  Less modular, extensible
  Need lots of serial ports
    Custom serial IO
  Power consumption
  Specialized for cabled observatory
    Ship, ROV service
  Custom HW/SW
Bottom Line for xFOCE
  Central computing w/ workstation computing environment

## Slide 18
Next up: Industrial Computers…
  COTS Industrial automation computers
  Heavy use of COTS hardware and software
  Shown using stand-alone configuration (it’s not the only way)

## Slide 19
ESW
Controller
Power
Data
Data
Flow
Flow
CTD
pH
CTD
pH
DO
DO2
Component | Location | Why
Controller HW | Surface and/or Shore | Easier access Large housings
Controller Software | Surface And Shore | Co-located w/ HW
UI Software | Shore | Easier maintenance
Power | Surface or Shore | Lots Needed! Easier access
Data | Surface and/or Shore | Co-located w/ control
ESW | Shore Or Surface | Permitting, depth, distance from shore
Controller
UI
Seafloor
Shore
Surface
Junction
Flow
Industrial Computers
Location View

## Slide 20
ESW
Controller
Power
Data
Data
Flow
Flow
CTD
pH
CTD
pH
DO
DO2
Controller
UI
Seafloor
Shore
Surface
Junction
Flow
Industrial Computers
Location View
Component | Build/Buy | Implementation
Controller HW | Build/Buy | WAGO, National Instruments C-Rio Serial Mux, Video Mux Custom serial expansion
Controller Software | Build/Buy COTS Open Source | LabView Open Source Dataturbine?...
Archive, UI | Build/Buy COTS | PC Workstation MacOS, Windows, Linux LabView
Power | Buy Build | WAGO, National Instruments C-Rio Custom GF monitoring
Data | Build/Buy | Matlab SIAM, SSDS Open Source
ESW | Build/Buy | WAGO, National Instruments C-Rio LabView COTS pumps, controllers

## Slide 21
ESW
Flow
Flow
CTD
pH
CTD
pH
DO
DO2
Flow
Controller
Power
Data
Data
Controller
UI
Seafloor
Shore
Surface
Junction
Industrial Computers
Location View
RS422
RF Wireless
WiFi
Wired Ethernet
Controller

## Slide 22: Summary Industrial Computers
Benefits
  Mostly COTS components
  Vendor and user community support
  Easier to build
  COTS software provides much infrastructure
Costs
  High cost of software and hardware
  High power consumption
  Cable may be very technical, especially from surface expression in active environment
  Large form factors mean larger housings
The Bottom Line
  Expensive, more straightforward design pattern
  min custom HW/SW
  Best suited to cabled system

## Slide 23
Next up: Sensor Node…
  Focus on small COTS embedded PCs and microprocessors
  Modularize and aggregate instrument drivers/data acquisition
  Reduce power consumption
  Shown using stand-alone configuration (it’s not the only way)

## Slide 24
Controller
Gateway
Power
Data
Sensor Node
Location View
Data
Flow
Flow
CTD
pH
CTD
pH
DO
DO2
Flow
Component | Location | Why
Controller HW | Surface/Seafloor | Surface: telemetry, UI Seafloor: experiment control
Controller Software | Seafloor | Gateway: control, telemetry Node: data acquisition
UI Software | Shore/Surface | Easier maintenance
Power | Surface | Stand-alone option
Data | Seafloor And Shore | Local data needed for control Central archive for redundancy, easier access
Seafloor
Shore
Surface
ESW
Controller
Gateway
Node
Node
Node
Node
Data
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow

## Slide 25
Controller
Gateway
Power
Data
Sensor Node
Location View
Data
Flow
Flow
CTD
pH
CTD
pH
DO
DO2
Flow
Seafloor
Shore
Surface
ESW
Controller
Gateway
Node
Node
Node
Node
Data
Component | Build/Buy | Implementation
Controller HW | Buy | Gateway: BeagleBoard, Android Node: Arduino, MSP430
Controller Software | Build | Gateway: Linux, Java, C++/Java Node: C/C++, Wiring, e.g.
Archive, UI | Build/Buy | Custom backend Front end options TBD
Power | Build | Custom load switch, GF/iso
Data | Build | Mix of open source, custom Open source data turbine, C++/Java (OSDataTurbine+custom)
ESW | Build/Buy | 
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow

## Slide 26
Node
Node
Node
Node
Controller
Gateway
Power
Data
Sensor Node
Location View
Data
Flow
Flow
CTD
pH
CTD
pH
DO
DO2
Flow
Seafloor
Shore
Surface
ESW
Controller
Gateway
Data
RS422
RS422
RS232
RF Wireless
Cell/Sat
WiFi
Wired Ethernet
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow

## Slide 27: Summary Sensor Node
Benefits
  Reduce power
  No custom serial IO expansion
  Modularizes data acquisition
  Many variations possible
    COTS processors, languages
    Topologies
    Connection backbone (cost: power)
    Component upgrades
    Drivers on Gateway
Costs
  Two software development platforms
  More custom hardware to build, configure, maintain
  More cables, connectors, housings
  Video expansion path unclear
  Multiple system clocks
The Bottom Line
  It’s a good design pattern, with balance of build/buy
  flexible, extensible, moderate cost
  Variants trade complexity, power, modularity

## Slide 28: Approach Tradeoffs
Approach | Performance | Flexibility | Ease |  |  | Cost
 |  |  | Build | Use | Extend | 
Deep Cabled |  |  |  |  |  | 
WAGO Lego |  |  |  |  |  | 
Sensor Node |  |  |  | … |  | 

Benefit
Cost

## Slide 29: Other technologies and approaches
Options | Why not here
CAN bus | 
Inductive cables | 
OASIS, BRS | 
Pachube | 
MatLab | 
Acoustic comms | 

## Slide 30: We’d like to hear from you
Requirements and priorities
Range of resources and capabilities
Likeliest application configurations, constraints
  Stand- alone vs connected
What you’d re-use, re-invent (and why)
When you have to open the hood: processors and programming languages

## Slide 32: UI
Could organize technology options by connection bandwidth, power, platform capability
  Serial
  Satellite
  WiFi
  Ethernet
  Embedded, Industrial PC, Workstation
Sketch out a couple of concepts at either end of the spectrum

## Slide 33: Computing Architectures Considered Approaches
Location Matters  Build vs Buy  | Connected | Semi-Connected | Stand-alone
Custom |  |  | 
Consumer COTS |  |  | 
High grade COTS |  |  | 
xFOCE
CP FOCE
SW FOCE
eFOCE
Deep FOCE
Sensor Node
IPC
SIAM+Digi
SensorPod
?
Slide order? later?
What are Sensor Node etc?

## Slide 34: The Options
What to look for:
mixed
custom
cots/os
Build vs Buy:
by subsystem, color
Location Matters:
More stuff @...
Shore 
Surface 
Seafloor 
Remember to breathe :o)
10 kW
1000 MBps
Eth, Serial
Star
Topology, Resources:
Power, Bandwidth
Backbone
Topology

## Slide 35: Computing Architectures Deep Cabled Approach
Description
  1 year experiment
  1000m Operation
  High Power, Bandwidth cable
Features
  Central computing w/ many serial ports
  Custom electronics & housings
  Custom/open software
  Ethernet, serial
  In situ ESW gen
  ROV CO2 handling
  Video
Examples
  Deep FOCE
ESW
mixer
CO2
FOCE Control
Flow
ESW dist
Power
Dist
video
instruments
mixed
custom
cots/os
SIAM
PC104
Sci/Control
SSDS
RDV
OSDT
Browser
(video)
SIAM
10 kW
1000 MBps
Eth, Serial
Star
terminal
Mac/Win/Lin
DFOCE GUI
Power
Shore

## Slide 36: Computing Architectures WAGO Lego Approach
Description
  1 year experiment
  40-? m Operation
  Med Power, Bandwidth cable
  Not stand-alone (power)
Features
  Custom electronics & housings
  COTS/custom software
  Ethernet, serial, modbus
  On shore ESW gen
  Video
Examples
  Deep FOCE
ESW
mixer
CO2
FOCE Control
flow
ESW dist
Power
Dist
video
instruments
mixed
custom
cots/os
WAGO
Serial MUX
Sci/Control
Browser
(video)
LabView
0.2 kW
2-10 MBps
Eth, RS422
Star/Bus
terminal
National
Inst
Mac/Win/Lin
Serial MUX
WAGO
LV GUI
GF ISO
video
MUX
Shore
Power

## Slide 37: Computing Architectures Sensor Node Approach
Description
  0.5-1 year experiment
  40 m Operation
  stand-alone (shown) or cable
Features
  Custom electronics & housings
  COTS/custom software
  Mixed topology
  Ethernet, serial, modbus
  Off shore ESW gen
Examples
  eFOCe
ESW
mixer
CO2
FOCE Control
Flow
ESW dist
Power
instruments
mixed
custom
cots/os
Beagle e.g. Gateway
Power Dist
Sci/Control
Browser
2 kW
0.1-2 MBps
Eth/DSL?
RS422
Star
terminal
Mac/Win/Lin
Serial MUX
GUI
GF ISO
Diesel Gen
Electronics
FOCE Control
Beagle
Android
Telem
Custom SW
Custom SW
Cell
RF
WiFi
FOCE Control
Sensor Node
Custom SW
Arduino, e.g.