## Slide 1: Computing elements of xFOCE
(Architecture and system trades)

## Slide 2: Computing Architectures User Concerns
Performance: valid scientific approach, data quality
Flexibility: wide range of environments, scenarios
Ease:
  Build
  Test
  Use, maintain
  Extend
Cost
Notes: ----- Meeting Notes (4/19/12 09:27) -----
power constrained slide 2

## Slide 3: A few assumptions
Implementer profile | Researchers plus 2-4 post docs, grad students 0-1 engineer
Technical | Access to modest manufacturing facilities Software is harder than hardware, mechanical Strong preference for familiar COTS solutions
Implementation schedule | ~6 months
Experiments | Campaign-style deployments 12 month service life Remote and/or restricted sites
Lifecycle | Prefer to extend capability, rather than re-spin from scratch for successive funding rounds

## Slide 4
Controller
Enriched
Seawater
Power
Data
CO2
H2O
FOCE Essentials
Flow
Flow
CTD
pH
CTD
pH
DO
DO2
Flow
ESW
Chamber
External
Notes: ----- Meeting Notes (4/19/12 09:27) -----
pump hard to recognize
workstation graphic
remo
----- Meeting Notes (4/19/12 09:36) -----
expand DO2?

## Slide 5: Computing Architectures Elements
Instruments
Software
Housings
Electronics
Computers
Cabling
For each, many options
Many ways to arrange them
In a FOCE experiment
Notes: ----- Meeting Notes (4/19/12 09:36) -----
computer heads in periodic table

## Slide 6: Computing Architectures Shrinking the Universe of Trades
Look at decisions that have greatest impact on user concerns
  Build vs Buy
  Location matters: Shore vs Surface vs Seafloor
  Topology: how the pieces are connected

## Slide 7: Build vs Buy General Principles
Buy what you can’t/shouldn’t build
  Processors, instruments, cabling
  Software
Build (or borrow) as needed
  Chambers, housings
  Use COTS components if possible
  Get help on tough key builds
    contract, open source
Beware Frankensystem
  Patchwork integration of COTS parts
  Power consumption
  Rube Goldberg-ness of mechanical/electrical interfaces

## Slide 8: Location Matters General Principles
Connected vs Disconnected
  Generally easier to generate and store power, ESW on shore
  Telemetry bandwidth
Trades for off-shore elements
  Accessibility (to you, the elements, others)
  Reliability
Keep what’s offshore/sub-surface as simple and robust as possible
  Basics: Enriched seawater, power
  HW: Cables, connectors, housings
  SW: Applications, protocols, processes
Play to your application, tech strengths and budget
  Permits, environment
  Experiment duration, depth
  Data access requirements
  Maintenance schedule, spares
  Available design/fabrication resources

## Slide 9
Controller
Enriched
Seawater
Power
Data
What’s inside?
Build or Buy?
Where to put the pieces?
How are pieces connected?
CO2
H2O
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
The software developer sees…
The user needs to consider
Flow
ESW
DO2
Chamber
External
Notes: ----- Meeting Notes (4/19/12 09:45) -----
not clear about thought bubbles

## Slide 10
Some things must be on the seafloor
  Chamber, instruments
  Actuators (pumps, fans, etc.)
But location of everything else is flexible…
  Power, ESW
  Controller
  Data storage, user interfaces
And, there are many ways to implement all of it…

## Slide 11
Our goal is to simplify the choices
Choices depend on experiment and constraints
  Budget, schedule
  Environment
  Technical resources
xFOCE community may draw from different approaches

## Slide 12
A study of some approaches
  Centralized Workstation
  Industrial Computers
  Sensor Node
3 views to evaluate key features and trades
  Build/buy what and why: hardware, software
  Location: shore, surface, seafloor
  Connections: topology and infrastructure

## Slide 13
Next up: Centralized Workstation…
  Workstation computing
  Mixed Common Off The Shelf (COTS) /custom hardware
  Shown here using cabled configuration

## Slide 14
Controller
Power
Data
Grand Centralized Workstation
Location View
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Flow
Component | Location | Why
Controller HW | Seafloor | Experiment continues if comms fails
Controller Software | Seafloor | ‘’
UI Software | Shore | Easier maintenance
Power | Seafloor | Need fine-grained power management at site
Data | Seafloor And Shore | Experiment continues if comms fails
Seafloor
Shore
Surface
ESW
Chamber
External
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow

## Slide 15
Controller
Power
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Grand Centralized Workstation
Data
Build/Buy
View
Seafloor
Shore
Surface
Flow
ESW
Component | Build/Buy | Implementation
Controller HW | Buy | PC104 Serial port cards (16 total)
Controller Software | Build Open Source | Linux, Java Custom: SIAM Data Acquisition software Open Source: DataTurbine, e.g.
Archive, UI | Build | PC Workstation MacOS, Windows, Linux, Java Custom: Shore Side Data System (SSDS), FOCE GUI
Power | Build | Custom: chassis
ESW | Build | Custom: electronics, software, chassis COTS: pumps, controllers
Chamber
External

## Slide 16
ESW
Flow
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Controller
Power
Data
Data
100 MBps
Ethernet
Serial
1 kW Cable
Grand Centralized Workstation
Ethernet-Serial
Connection
View
Seafloor
Shore
Surface
Ethernet
Chamber
External

## Slide 17: Summary Centralized Workstation
Pros
  One software platform
  COTS computers
  COTS serial I/O solutions
Cons
  Extensibility in packaging and housings…have to put a lot of holes in housings
    Can use junction boxes
  Power consumption
  Less modular
  Need lots of serial ports
    Custom serial IO
  Custom HW/SW

## Slide 18
Next up: Industrial Computers…
  Industrial automation computers (WAGO, Compact Rio, e.g.)
  Heavy use of COTS hardware and software
  Shown here using moored configuration

## Slide 19
Controller
ESW
Controller
Power
Data
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Component | Location | Why
Controller HW | Surface and/or Shore | Easier access Large housings
Controller Software | Surface And Shore | Co-located w/ HW
UI Software | Shore | Easier maintenance
Power | Surface or Shore | Easier access
Data | Surface and/or Shore | Co-located w/ control
ESW | Shore Or Surface | Permitting, depth, distance from shore
Controller
UI
Seafloor
Shore
Surface
Junction
Flow
Industrial Computers
Location View
Mooring pic
Wireless
Chamber
External
Controller

## Slide 20
ESW
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Controller
UI
Seafloor
Shore
Surface
Junction
Flow
Industrial Computers
Build/Buy
View
Chamber
External
Wireless
Controller
Controller
Power
Data
Controller
Component | Build/Buy | Implementation
Controller HW | Build/Buy | COTS: WAGO, National Instruments Compact-Rio (NI-CRIO), Serial Multiplexer (MUX), Video MUX
Controller Software | Build/Buy COTS Open Source | COTS/Custom: LabView Open Source: DataTurbine
Archive, UI | Build/Buy COTS Open Source | PC Workstation MacOS, Windows, Linux Open Source: DataTurbine, RDV, Pachube... COTS/Custom: LabView
Power | Buy Build | COTS: WAGO, NI-CRIO Custom: GF, isolation
ESW | Build/Buy | COTS: WAGO, NI-CRIO, LabView, pumps, motor controllers

## Slide 21
Controller
ESW
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Flow
Controller
Power
Data
Data
Controller
UI
Seafloor
Shore
Surface
Junction
Industrial Computers
ConnectionView
Serial
Ethernet
RF Wireless
WiFi
Cell
Satellite
Controller
Chamber
External

## Slide 22: Summary Industrial Computers
Pros
  Mostly COTS components
  Vendor and user community support
  Easier to build
  COTS software provides much infrastructure
Cons
  High cost of software and hardware
  High power consumption
  Cable may be somewhat technical, especially from surface expression in active environment
  Large electronics form factors require larger housings

## Slide 23
Next up: Sensor Node…
  Focus on small COTS embedded PCs and microprocessors
  Modularize and aggregate power switching and/or data acquisition
  Reduce power consumption
  Shown here using moored configuration

## Slide 24
Controller/
Gateway
Power
Data
Sensor Node
Location View
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Flow
Component | Location | Why
Controller HW | Surface/Seafloor | Surface: telemetry, UI Seafloor: experiment control
Controller Software | Seafloor | Gateway: control, telemetry Node: data acquisition
UI Software | Shore/Surface | Easier maintenance
Power | Surface | Probably use generator, solar, wind on surface
Data | Seafloor And Shore | Local data needed for control Central archive for redundancy, easier access
Seafloor
Shore
Surface
ESW
Controller
/Gateway
Node
Node
Node
Node
Data
Load switching,
Data Acquisition for
1-4 Devices
Chamber
External
Wireless
Experiment Control for 1 chamber
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow

## Slide 25
Wireless
Controller
Gateway
Power
Data
Sensor Node
Build/Buy View
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Flow
Seafloor
Shore
Surface
ESW
Controller
Gateway
Node
Node
Node
Node
Data
Open source:
options./examples vs required
Component | Build/Buy | Implementation
Controller HW | Buy | Gateway: BeagleBoard, Android Node: Arduino, MSP430
Controller Software | Build | Gateway: Linux, Java, C++/Java Node: C/C++, Wiring, e.g.
Archive, UI | Build/Buy | Custom: back end interface Open Source: web server on gateway
Power | Build | Custom: load switch, GF/iso
ESW | Build/Buy | 
Chamber
External
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow

## Slide 26
Node
Node
Node
Node
Controller
Gateway
Power
Data
Sensor Node
Connection
View
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Flow
Seafloor
Shore
Surface
ESW
Controller
Gateway
Data
Ethernet
(Serial?)
Serial
Serial
RF Wireless
Cell
Satellite
WiFi
Chamber
External
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow

## Slide 27: Summary Sensor Node
Pros
  Reduce power
  No custom serial IO expansion
  Modularizes data acquisition
  Many variations possible
    COTS processors, languages
    Topologies
    Connection backbone (cost: power)
    Component upgrades
    Drivers on Gateway
Cons
  Two software development platforms
  More custom hardware to build, configure, maintain
  More cables, connectors, housings
  Video expansion path unclear
  Multiple system clocks
Notes: The Bottom Line
  It’s a good design pattern, with balance of build/buy
  flexible, extensible, moderate cost
  Variants trade complexity, power, modularity

## Slide 28: Approach Tradeoffs
Approach | Performance | Flexibility | Ease |  |  | Cost
 |  |  | Build | Use | Extend | 
Centralized Workstation |  |  |  |  |  | 
Industrial Computer |  |  |  |  |  | 
Sensor Node |  |  |  |  |  | 

Pro
Con

## Slide 29: UI
Help users to understand and simplify key choices
What UI choices will the user make related to UI
  Network, interfaces, security
How do those choices affect concerns (performance, flexibility, ease, cost)
What are pros/cons of various choices
  Cost, power, bandwidth, software skill, processing capability, software/system dependencies
Modularity
  Interfaces that support flexibility in UI choices
  Expansion path: what’s needed up front to start simply and build capability
Sketch out a couple of concepts at either end of the spectrum
Specific choice/detail more important for SWFOCE

## Slide 30: Tethers?

## Slide 31
Questions?