## Slide 1: Computing elements of xFOCE
(Architecture and system trades)

## Slide 2: Computing Architectures User Concerns
Performance: valid scientific approach, data quality
Flexibility: wide range of environments, scenarios
Ease:
  Build
  Test
  Use, maintain
  Extend
Cost
Notes: ----- Meeting Notes (4/19/12 09:27) -----
power constrained slide 2

## Slide 3: A few assumptions
Implementer profile | Researchers plus 2-4 post docs, grad students 0-1 engineer
Technical | Access to modest manufacturing facilities Software is harder than hardware, mechanical Strong preference for familiar COTS solutions
Implementation schedule | ~6 months
Experiments | Campaign-style deployments 12 month service life Remote and/or restricted sites
Lifecycle | Prefer to extend capability, rather than re-spin from scratch for successive funding rounds

## Slide 4
Controller
Enriched
Seawater
Power
Data
CO2
H2O
FOCE Essentials
Flow
Flow
CTD
pH
CTD
pH
DO
DO2
Flow
ESW
Chamber
External
Data, Control
Power
Notes: ----- Meeting Notes (4/19/12 09:27) -----
pump hard to recognize
workstation graphic
remo
----- Meeting Notes (4/19/12 09:36) -----
expand DO2?

## Slide 5: Computing Architectures Elements
Instruments
Software
Housings
Electronics
Computers
Cabling
For each, many options
Many ways to arrange them
In a FOCE experiment
Notes: ----- Meeting Notes (4/19/12 09:36) -----
computer heads in periodic table

## Slide 6: Computing Architectures Shrinking the Universe of Trades
Look at decisions that have greatest impact on user concerns
  Build vs Buy
  Location matters: Shore vs Surface vs Seafloor
  Topology: how the pieces are connected

## Slide 7: Build vs Buy General Principles
Buy what you can’t/shouldn’t build
  Processors, instruments, cabling
  Software
Build (or borrow) as needed
  Chambers, housings
  Use COTS components if possible
  Get help on tough key builds
    contract, open source
Beware Frankensystem
  Patchwork integration of COTS parts
  Power consumption
  Rube Goldberg-ness of mechanical/electrical interfaces

## Slide 8: Location Matters General Principles
Connected vs Disconnected
  Generally easier to generate and store power, ESW on shore
  Telemetry bandwidth
Trades for off-shore elements
  Accessibility (to you, the elements, others)
  Reliability
Keep what’s offshore/sub-surface as simple and robust as possible
  Basics: Enriched seawater, power
  HW: Cables, connectors, housings
  SW: Applications, protocols, processes
Play to your application, tech strengths and budget
  Permits, environment
  Experiment duration, depth
  Data access requirements
  Maintenance schedule, spares
  Available design/fabrication resources

## Slide 9
Controller
Enriched
Seawater
Power
Data
What’s inside?
Build or Buy?
Where to put the pieces?
How are pieces connected?
CO2
H2O
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
The software developer sees…
The user needs to consider
Flow
ESW
Chamber
External
Notes: ----- Meeting Notes (4/19/12 09:45) -----
not clear about thought bubbles

## Slide 10
Some things must be on the seafloor
  Chamber, instruments
  Actuators (pumps, fans, etc.)
But location of everything else is flexible…
  Power, ESW
  Controller
  Data storage, user interfaces
And, there are many ways to implement all of it…

## Slide 11
xFOCE helps to simplify the choices
  Experience, Designs, Community
Choices depend on experiment and constraints
  Budget, schedule
  Environment
  Technical resources
xFOCE community may draw from different approaches

## Slide 12
A study of some approaches
  Centralized Workstation
  Industrial Computers
  Sensor Node
3 views to evaluate key features and trades
  Location: shore, surface, seafloor
  Build/buy: hardware, software
  Connections: topology and infrastructure

## Slide 13
Next up: Centralized Workstation…
  Workstation computing
  Similar to dpFOCE implementation
  Mixed Common Off The Shelf (COTS) /custom hardware
  Shown here using cabled configuration

## Slide 14
Controller
Power
Distribution
Data
Archive
Centralized Workstation
Location View
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Flow
Component | Location | Why
Controller HW | Seafloor | Could run on shore Experiment continues if comms fails
Controller Software | Seafloor | ‘’
UI Software | Shore | Easier maintenance
Power | Seafloor | Need fine-grained power management at site
Data | Seafloor And Shore | Experiment continues if comms fails
Seafloor
Shore
Surface
ESW
Chamber
External
Power
Source
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow

## Slide 15
Centralized Workstation
Build/Buy
View
SIAM: Software Infrastructure and Applications for MOOS
SSDS: Shore Side Data System
Component | Build/Buy | Implementation
Controller HW | Buy | PC104 Pentium Serial port cards (16 total)
Controller Software | Build Open Source | Linux, Java Custom: SIAM Data Acquisition software Open Source: DataTurbine, e.g.
Archive, UI | Build | PC Workstation MacOS, Windows, Linux, Java Custom: SSDS, FOCE GUI
Power | Build | Custom: load switching and monitoring chassis
ESW | Build | Custom: electronics, software, chassis COTS: pumps, controllers

## Slide 16
Power
Distribution
Power
Source
ESW
Flow
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Controller
Data
Data
Serial
Fiber Optic
Power and Data Cable
Centralized Workstation
Ethernet-Serial
Connection
View
Seafloor
Shore
Surface
Ethernet
Chamber
External
1 kW
100 MBps
Ethernet

## Slide 17: Summary Centralized Workstation
Pros
  One software platform
  COTS computers
  COTS serial I/O solutions
Cons
  Extensibility in packaging and housings…have to put a lot of holes in housings
    Can use junction boxes
  Need lots of serial ports
    Custom serial IO Power consumption
  Less modular
  Custom HW/SW

## Slide 18
Next up: Industrial Computers…
  Industrial automation computers (WAGO, Compact Rio, e.g.)
  Similar to CP-FOCE implementation
  Uses primarily COTS hardware and software
  Shown here using moored configuration

## Slide 19
Controller
ESW
Controller
Power
Data
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Component | Location | Why
Controller HW | Surface and/or Shore | Easier access Large housings
Controller Software | Surface And Shore | Co-located w/ HW
UI Software | Shore | Easier maintenance
Power | Surface or Shore | Easier access
Data | Surface and/or Shore | Co-located w/ control
ESW | Shore Or Surface | Permitting, depth, distance from shore
Controller
UI
Seafloor
Shore
Surface
Junction
Flow
Industrial Computers
Location View
Wireless
Chamber
External
Controller

## Slide 20
Industrial Computers
Build/Buy
View
Component | Build/Buy | Implementation
Controller HW | Buy | COTS: WAGO, National Instruments Compact-Rio (NI-CRIO), Serial MUX, Video MUX
Controller Software | Buy | COTS: LabView (custom drivers) Open Source: DataTurbine
Archive, UI | Buy | PC Workstation MacOS, Windows, Linux Open Source: DataTurbine, RDV, Pachube... COTS: LabView (custom archive), MATLAB
Power | Build/Buy | COTS: WAGO, NI-CRIO Custom: Ground fault detection, isolation
ESW | Build/Buy | Custom: pump and valve drivers COTS: WAGO, NI-CRIO, LabView, pumps, motor controllers
COTS: Common Off The Shelf
OSDT: Open Source Data Turbine
RDV: Real-time Data Viewer OSDT client
WAGO, CRIO: Industrial computer implementations
MUX: multiplexer

## Slide 21
Controller
ESW
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Flow
Controller
Power
Data
Data
Controller
UI
Seafloor
Shore
Surface
Junction
Industrial Computers
ConnectionView
Serial
Ethernet
RF Wireless
WiFi
Cell
Satellite
Controller
Chamber
External
Serial
Ethernet

## Slide 22: Summary Industrial Computers
Pros
  Mostly COTS components
  Vendor and user community support
  Easier to build
  COTS software provides much infrastructure
Cons
  High cost of software and hardware
  High power consumption
  Large electronics form factors require larger housings

## Slide 23
Next up: Sensor Node…
  Small COTS embedded PCs and microprocessors
  Modularize and aggregate power switching and/or data acquisition
  Similar to eFOCE implementation
  Reduce power consumption
  Shown here using moored configuration

## Slide 24
Controller/
Gateway
Power
Data
Sensor Node
Location View
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Flow
Component | Location | Why
Controller HW | Surface/Seafloor | Surface: telemetry, UI Seafloor: experiment control
Controller Software | Seafloor | Gateway: control, telemetry Node: data acquisition
UI Software | Shore/Surface | Easier maintenance
Power | Surface | Probably use generator, solar, wind on surface
Data | Seafloor And Shore | Local data needed for control Central archive for redundancy, easier access
Seafloor
Shore
Surface
ESW
Controller
/Gateway
Node
Node
Node
Node
Data
Load switching,
Data Acquisition for
1-4 Devices
Chamber
External
Wireless
Experiment Control for 1 chamber
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow

## Slide 25
Sensor Node
Build/Buy View
Component | Build/Buy | Implementation
Controller HW | Buy | Gateway: BeagleBoard, Android, Gumstix Node: Arduino, MSP430, SmartSensor
Controller Software | Build | Gateway: Linux, Java, C++/Java Node: C/C++, Wiring, e.g. Instrument drivers
Archive, UI | Build/Buy | Custom: back end interface Open Source: web server on gateway
Power | Build | Custom: load switch, ground fault detection, isolation
ESW | Build/Buy | Custom: pump and valve drivers COTS: pumps, motor controllers
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow

## Slide 26
Node
Node
Node
Node
Controller
Gateway
Power
Data
Sensor Node
Connection
View
Data
Flow
Flow
CTD
pH
CTD
pH
DO2
DO2
Flow
Seafloor
Shore
Surface
ESW
Controller
Gateway
Data
Ethernet
(Serial?)
Serial
Serial
RF Wireless
Cell
Satellite
WiFi
Chamber
External
Notes: ----- Meeting Notes (4/19/12 09:50) -----
purpose of flow

## Slide 27: Summary Sensor Node
Pros
  Reduce power
  No custom serial IO expansion
  Modularizes data acquisition
  Many variations possible
    COTS processors, languages
    Topologies
    Connection backbone (cost: power)
    Component upgrades
    Drivers on Gateway
Cons
  Two software development platforms
  More custom hardware to build, configure, maintain
  More cables, connectors, housings
  Video expansion path unclear
  Multiple system clocks
Notes: The Bottom Line
  It’s a good design pattern, with balance of build/buy
  flexible, extensible, moderate cost
  Variants trade complexity, power, modularity

## Slide 28: Approach Tradeoffs
Approach | Performance | Flexibility | Ease |  |  | Cost
 |  |  | Build | Use | Extend | 
Centralized Workstation |  |  |  |  |  | 
Industrial Computer |  |  |  |  |  | 
Sensor Node |  |  |  |  |  | 

Pro
Con

## Slide 29
Questions?

## Slide 30: UI
Help users to understand and simplify key choices
What UI choices will the user make related to UI
  Network, interfaces, security
How do those choices affect concerns (performance, flexibility, ease, cost)
What are pros/cons of various choices
  Cost, power, bandwidth, software skill, processing capability, software/system dependencies
Modularity
  Interfaces that support flexibility in UI choices
  Expansion path: what’s needed up front to start simply and build capability
Sketch out a couple of concepts at either end of the spectrum
Specific choice/detail more important for SWFOCE