## Slide 1
xFOCE / swFOCE
Review

## Slide 2: FOCE and OA Research

## Slide 3: xFOCE
European FOCE (eFOCE) is currently under construction and scheduled for deployment in May 2012. This system uses a cable but the CO2 is delivered in bottles to a surface expression.
Deep FOCE (dpFOCE) is the original FOCE built for multi-science users on a cabled observatory.
Coral Prototype FOCE (cpFOCE) is the first tech transfer of FOCE built for multi-science users on the Great Barrier Reef. Solar and wind powered except for the creation of the enriched CO2 water.
Antarctic FOCE (antFOCE) proposal submitted and partially funded. Proposal for other 50% of funding underway.

## Slide 4
Why xFOCE?
The problem is some folks are reading our papers and starting out on their own. That is fine but they are calling systems FOCE that are 1) not actually doing the functions of FOCE but more over 2) the chemistry is incorrect and publications using the FOCE acronym pull other work into question.
MBARI was contacted and we gave feedback about how to use the existing hardware and reconfigure it to become a functional FOCE.
The scientist did some of it but still didn’t grasp what FOCE is an how to properly set up a system to get meaningful science results.
For the good of the OA research community and MBARI’s reputation we needed to create a way of preventing these errors!

## Slide 5: xFOCE
xFOCE shall support 6 test chambers (3 active and 3 control)
xFOCE shall maintain a desired pH offset from ambient within +/- .2 pH
xFOCE shall be capable of pH offsets of between .2 and .8 pH units
xFOCE shall hold a selected pH offset for a minimum of 2 weeks
xFOCE shall be capable of deployments greater than 6 months in duration
xFOCE shall be fully functional in external currents of 50 cm/sec
xFOCE shall mimic surge to the extent possible based on chamber scale
xFOCE shall maximize the allowance of full spectrum natural light
xFOCE shall include pH, CTD, O2, flow rate or calculated flow using velocity with data reported at currently accepted standards for science publication

## Slide 6: xFOCE
xFOCE shall provide internal environmental data for all instruments on the required list from each active chamber
xFOCE shall provide internal environmental data for
xFOCE shall be diver maintainable
xFOCE shall not use materials that are toxic to the marine environment
xFOCE shall not be dangerous to maintenance divers
xFOCE shall minimized impacts on local marine life
xFOCE shall be capable of being fully recovered and leave no components behind
xFOCE shall be capable of being built, installed and maintained by a typical university oceanographic research lab with a minimum of 1 scientist and 2 graduate students

## Slide 7: xFOCE
xFOCE shall maximize use of commercially “off-the-shelf” or readily available technology to the fullest extent possible
xFOCE shall be capable of working in waters anyplace in the ocean or other alkaline waters where the water velocity does not exceed 75 cm/sec.

## Slide 8: xFOCE
xFOCE may support more than 6 total chambers
xFOCE may control pH to tighter than +/- .2 pH units
xFOCE may operate continuously
xFOCE may include photosynthetic active radiation (PAR) sensing
xFOCE may allow alternative maintenance
xFOCE may allow use of any ship of opportunity
xFOCE may modify flow rates internally to maximize CO2 use
xFOCE may operate in waters in any water velocities up to 150 cm/sec

## Slide 9: swFOCE
swFOCE shall meet all xFOCE requirements
swFOCE shall not require a support ship greater than 50’ for deployment and recovery
swFOCE shall include a camera system capable of variable time lapse digital data collection suitable for publication, the camera (and light source if included) shall also be adjustable within the swFOCE structure
swFOCE shall use the Stanford Hopkins
Marine Station’s submarine cable
swFOCE shall provide a separate power and communications links form the planned Hopkins science use and will not interfere with other science operations.

## Slide 10: xFOCE Concept of Ops cable
Science interface on shore
CO2 and Enriching process on shore
Air / sea interface managed using buried cable
Capable of supporting 6 to 8 xFOCE units
(4 active pH chg and 4 control)
Depth rating
min - XX
max - XX
Anchored to bottom
Uses ??? to prevent erosion

## Slide 11: xFOCE Concept of Ops no cable
Science interface on shore
CO2 and Enriching process off shore
Air / sea interface managed using surface expression (buoy ?)
Capable of supporting 6 xFOCE units (?? Maybe less)
(3 active pH chg and 3 control)
Depth rating
min - XX
max - XX
Anchored to bottom
Uses ??? to prevent erosion
Comms by telemetry

## Slide 12
xFOCE/swFOCE Concept of Ops
This still needs modification By Bill
Flow Vel

## Slide 13: xFOCE Functional Interfaces
CO2
SW Pump
ESW
ESW Distributor
Data Archive
Data Acquisition
Data
Distribution
Console
Instruments
ESW injector(s)
Flow effector(s)
Camera(s)
Control System
Generation
Storage
Distribution/Protection
GUI
Configuration & Control
Monitoring/
Health/Status
Comms
ESW injector(s)
Flow effector(s)
Mixer
Subsea Electronics
Surface
Subsea
Power
House Power
Science / Control System
Internet
xFOCE Control
Enriched
Seawater
System

## Slide 14: xFOCE Mooring Concept
CO2 Mix Electronics
System Control Electronics
Diesel Fuel
Exhaust used for CO2
Particle Scrubber

## Slide 15
xFOCE Systems concept
What is the minimum requirement of elements for xFOCE?
Proposed minimum instrumentation for an active pH controlled chamber. The blue elements are options and controls would only have CTD and pH. Not shown is the other option of a motor and fan to control flow.

## Slide 16
Shallow Water Corals
Benthic Biology
Multi-Site
Multi- Discipline
Multi-Year
swFOCE Basic Concept
Shallow Water
Off-Shore
Schematic View of the Hopkins Site

## Slide 17
pH Sensor
Thruster
CTDO Sensor
Camera and Light
FOCE Controller
Power and Comm
Cabling
Animal
Restrictor
Anchors
CO2 Enriched Water
swFOCE Concept
Flow meter
Ducting
(Time delay)
Bottomside FOCE chamber for swFOCE

## Slide 18
Sea Level
Intake Filter
Existing Drain at
Hopkins
Barrier End Cap
Sea Water
Low pH Sea Water
Power and Comms
xFOCE/swFOCE Cable Concept

## Slide 19
Humidity Sensor
Flash Storage
CPU
Battery Charger
Voltage Regulator
Deep Cycle Batteries
Wireless Comm
Instrument Interface
Wind ??
xFOCE /swFOCE Components

## Slide 20
CPU
Voltage Regulator
Deep Cycle Batteries
Level Sensor
Small Water Pump
Motor Controller
xFOCE /swFOCE Components

## Slide 21: Trade Elements Mechanical
Chamber size, shape, materials, anchor, mounts
ESW generation, storage, distributor, effectors
Flow effectors

## Slide 22: Trade Elements Software
UI console, GUI, data access SW
Data acquisition, distribution SW
  HW requirements: IO, memory
  Language(s), tools, OS/none, 3rd Party
Communications protocols SW
Control system software

## Slide 23: Trade Elements Electrical
Power generation, storage, distribution
Load/Bus switching, GF detection, isolation, monitoring
Environmental monitoring HW
Data acquisition, archive HW
Communications backbone HW

## Slide 24: swFOCE Systems concept
Divide sub-systems out, major blocks and define what will traded starting with xFOCE base.
Define system / sub-system interfaces
Assign each trade to a

## Slide 25: Legal and Permitting

## Slide 26: Mechanical
Basic xFOCE Structure
swFOCE if anything is modified
Anchoring (environmental data)
Flow control
Light management
Bio-fouling

## Slide 27: Electrical
Power
Budgets
Management
Communications
Ground Fault ??
Control Circuits

## Slide 28: Software
Basic Architectural Structure
xFOCE (minimum needs)
swFOCE (extensible elements as needed)
Open Source
Controller / algorithm development
Science/User interfaces
most basic
options
Realtime vs. ??

## Slide 29: Data
Collection
Storage
Processing (??)
Quality
How does design handle modularity of xFOCE

## Slide 30: Technology Transfer of FOCE
William J. Kirkwood
Heron Island FOCE Site