## Slide 1: Free Ocean CO2 Enrichment
An illustration of the atmospheric CO2 increase and the change in ocean pH

## Slide 2: FOCE and OA Research
Free Ocean CO2 Enrichment experiments are based on an existing base of scientific work that started in the early 1990’s. The Free Air CO2 Enrichment (FACE) experiments.
Dr. Peter Brewer first proposed this type of experiment to MBARI engineering in 2003 as part of his greenhouse gases research. The drawing to the right is the initial concept from engineering and presented to NOAA’s Dr. Dick Feely later that year.
Concept using the MARS cable in Monterey Bay, later deployed as deep FOCE (dpFOCE)

## Slide 3
Why xFOCE?
The problem: Some scientists are misinterpreting our publications and what is required to make a FOCE system work.
MBARI was contacted and we gave feedback about how to use the existing hardware and reconfigure it to become a functional FOCE.
The scientist did some of it but still didn’t grasp what FOCE is an how to properly set up a system to get meaningful science results.
It became apparent that a resource clearly outlining FOCE and how to get started would be useful.

## Slide 4: xFOCE
European FOCE (eFOCE) is currently under construction and scheduled for deployment in May 2012. This system uses a cable but the CO2 is delivered in bottles to a surface expression.
Deep FOCE (dpFOCE) is the original FOCE built for multi-science users on a cabled observatory.
Coral Prototype FOCE (cpFOCE) is the first tech transfer of FOCE built for multi-science users on the Great Barrier Reef. Solar and wind powered except for the creation of the enriched CO2 water.
Antarctic FOCE (antFOCE) proposal submitted and partially funded. Proposal for other 50% of funding underway.

## Slide 5: xFOCE
xFOCE shall support 2 test chambers (1 active and 1 control)
xFOCE shall maintain a desired pH offset from ambient within +/- .2 pH
xFOCE shall be capable of pH offsets of between .2 and .8 pH units
xFOCE shall hold a selected pH offset for a minimum of 2 weeks
xFOCE shall be capable of deployments greater than 6 months in duration
xFOCE shall be fully functional in external currents of 50 cm/sec
xFOCE shall mimic surge to the extent possible based on chamber scale
xFOCE shall maximize the allowance of full spectrum natural light
xFOCE shall include pH, CTD, O2, flow rate or calculated flow using velocity

## Slide 6: xFOCE
xFOCE shall provide internal environmental data for all instruments on the required list from each active chamber
xFOCE shall provide internal environmental data for
xFOCE shall be diver maintainable
xFOCE shall not use materials that are toxic to the marine environment
xFOCE shall not be dangerous to maintenance divers
xFOCE shall minimized impacts on local marine life
xFOCE shall be capable of being fully recovered and leave no components behind
xFOCE shall be capable of being built, installed and maintained by a typical university oceanographic research lab with a minimum of 1 scientist and 2 graduate students

## Slide 7: xFOCE
xFOCE shall maximize use of commercially “off-the-shelf” or readily available technology to the fullest extent possible
xFOCE shall be capable of working in ocean waters where the velocity does not exceed 75 cm/sec.

## Slide 8: swFOCE
swFOCE shall meet all xFOCE requirements
swFOCE shall not require a support ship greater than 50’ for deployment and recovery
swFOCE shall include a camera system capable of variable time lapse digital data collection suitable for publication, the camera (and light source if included) shall also be adjustable within the swFOCE structure
swFOCE shall use the Stanford Hopkins
Marine Station’s submarine cable
swFOCE shall provide a separate power and communications links form the planned Hopkins science use and will not interfere with other science operations.

## Slide 9: xFOCE Concept of Ops cable
Science interface on shore
CO2 and Enriching process on shore
Air / sea interface managed using buried cable
Capable of supporting 6 to 8 xFOCE units
(4 active pH chg and 4 control)
Depth rating
min - XX
max - XX
Anchored to bottom
Uses ??? to prevent erosion

## Slide 10: xFOCE Concept of Ops no cable
Science interface on shore
CO2 and Enriching process off shore
Air / sea interface managed using surface expression
Capable of supporting 2 xFOCE units minimum
1 active pH chg and 1 control, 3 active and 3 control desired
Depth rating
max – 40m
Anchored to bottom
Comms by telemetry
Buoy or Platform

## Slide 11: xFOCE Functional Requirements
Max depth: 40m (130 ft)
pH Range: 0.0 to -0.6 continuous based on CO2 available. Brief excursions to -0.8 or -1.0 offset potentially
pH resolution: resolution: 0.05 pH units, 0.1 unit may be OK (prefer best resolution possible)
Temp range: -2 to 30 degrees C
Max ext. velocity: 50 cm/sec
Max int. velocity: 10 cm/sec
Full spectrum light: Max transmission of sunlight at depth
Number of Units: System support for 1 active and 1 control chamber

## Slide 12: swFOCE Additional Requirements
Surge: Imitate surge to extent possible
Temp range: -2 to 30 degrees C
Number of Units: System support for 3 active and 3 control chamber

## Slide 13
xFOCE/swFOCE Concept of Ops
Flow Vel
Science selected velocity

## Slide 14: xFOCE Functional Interfaces
CO2
SW Pump
ESW
ESW Distributor
Data Archive
Data Acquisition
Data
Distribution
Console
Instruments
ESW injector(s)
Flow effector(s)
Camera(s)
Control System
Generation
Storage
Distribution/Protection
GUI
Configuration & Control
Monitoring/
Health/Status
Comms
ESW injector(s)
Flow effector(s)
Mixer
Subsea Electronics
Surface
Subsea
Power
House Power
Science / Control System
Internet
xFOCE Control
Enriched
Seawater
System

## Slide 15: xFOCE Mooring Concept
CO2 Mix Electronics
System Control Electronics
Diesel Fuel
Exhaust used for CO2
Particle Scrubber

## Slide 16
xFOCE Systems concept
Blue circles are included for swFOCE
Proposed minimum instrumentation for an active pH controlled chamber. The blue elements are options and controls would only have CTD and pH. Not shown is the other option of a motor and fan to control flow.

## Slide 17
Shallow Water Corals
Benthic Biology
Multi-Site
Multi- Discipline
Multi-Year
swFOCE Basic Concept
Shallow Water
Off-Shore
Schematic View of the Hopkins Site

## Slide 18
pH Sensor
Thruster
CTDO Sensor
Camera and Light
FOCE Controller
Power and Comm
Cabling
Animal
Restrictor
Anchors
CO2 Enriched Water
swFOCE Concept
Flow meter
Ducting
(Time delay)
Bottomside FOCE chamber for swFOCE

## Slide 19
Sea Level
Intake Filter
Existing Drain at
Hopkins
Barrier End Cap
Sea Water
Low pH Sea Water
Power and Comms
swFOCE Cable Concept

## Slide 20: xFOCE Core Instrument Suite
pH : +/- .01 pH unit or better and suitable for
control loop applications
CTD: Comparable to current units at MBARI, unit is
FastCAT SBE49 (oxygen can be included)
Flow sensor: TBD, likely electromagnetic to get smooth
flow numbers and volumetric data. From dpFOCE acoustic velocity sensors are not suitable.
Suggested architecture allows for expansion of additional instrumentation
PAR* - Photosynthetically Active Radiation

## Slide 21: swFOCE Core Instrument Suite
pH : +/- .01 pH unit or better and suitable for control loop applications
CTD: Comparable to current units at MBARI, baseline unit is FastCAT SBE49 (oxygen can be included)
Flow sensor: TBD, likely electromagnetic to get smooth
flow numbers and volumetric data. From dpFOCE acoustic velocity sensors are not suitable.
PAR* Sensor: 400 – 700 nm / calibrated t0 0 – 5000 μmol photons•m -2 •s -1
Camera/Lights: 1080p - 16:9 ratio format – light source either natural and/or color balanced LED
PAR* - Photosynthetically Active Radiation

## Slide 22
Humidity Sensor
Flash Storage
CPU
Battery Charger
Voltage Regulator
Deep Cycle Batteries
Wireless Comm
Instrument Interface
Wind ??
xFOCE /swFOCE Components

## Slide 23
CPU
Voltage Regulator
Deep Cycle Batteries
Level Sensor
Small Water Pump
Motor Controller
xFOCE /swFOCE Components

## Slide 24: xFOCE /swFOCE Data Reqs.
Health and Status: Ability to query system status from web page (data dependent on sensors included)
Timing Accuracy: Network Time Protocol (NTP) protocol for synchronizing computers
Sample Rates: System will support 10 Hz standard operation
Basic Data Format: Comma delimited string, time stamped
swFOCE: Compatible with the current dpFOCE data streams and SSDS (Shore Side Data System*)
Near real time ground fault monitoring
*SSDS – Open source from MBARI

## Slide 25: xFOCE Engineering Trades
Color Frequency Wavelength
violet 668–789 THz 380–450 nm
blue 631–668 THz 450–475 nm
cyan 606–630 THz 476–495 nm
green 526–606 THz 495–570 nm
yellow 508–526 THz 570–590 nm
orange 484–508 THz 590–620 nm
red 400–484 THz 620–750 nm
infrared longer than 750 nm
Since these wavelengths penetrate water easier but most plastic materials respond poorly to high freq light the materials selections will focus on this end of the spectrum
The selection of materials will likely transmit this end of the spectrum fairly well but in selection, if required, we would trade attenuation here to maximize shorter frequencies.
Acrylic (vs Polycarbonate) has less attenuation overall and carries much further into the ultraviolet when comparing the blue lines.

## Slide 26: FOCE: A tool to understand local impacts of Ocean Acidification
Funding Provided by The David and Lucile Packard Foundation