## Slide 1: SIAM-based xFOCE design concept
Tom O’Reilly

## Slide 2
SIAM: device drivers, resource management
OSDT
HTML5 GUI pages
ARM processor
Serial instruments
Pump controller
Prop controller
These controllers might be Arduino
Radio
Serial breakout,
isolation
Serial breakout via Digi/Lantronix or “native” serial

## Slide 3: ARM processor
Main controller, data acquisition node
Hosts Linux or Android operating system
Hosts Java Virtual Machine (Oracle Embedded JavaSE)
Smaller, lower power than PC-104
Network connection to boat and/or shore
  Ethernet
  802.11 or Freewave radio
  Bluetooth
  Iridium
Breakout for serial instrument comms, isolation
USB for camera (common COTS camera interface)

## Slide 4: SIAM xFOCE approach
Reduce user need to modify code
  Provide “Universal” Instrument Driver (applicable to many instruments)
  Simplify driver code framework
Simplify configuration procedures with GUIs and automation
Accept that Java programming skills are needed to modify SIAM internals

## Slide 5: SIAM advantages
Extensively tested, many deployments
Satisfies most xFOCE software requirements
Many existing drivers; extensible via SIAM framework
Suitable for cabled-to-shore as well as moored
Java: object-oriented, portable to many processors

## Slide 6: SIAM drawbacks
Complex configuration files, many commands/options to remember
  Develop GUIs to simplify configuration, monitor, control
Need a virtual machine
  JVMs now widely available on embedded platforms (Oracle embedded JVM, Dalvik/Android)
Need a Java programmer to extend functionality
  Universal instrument driver reduces need for software development
  Embedded Java skills are increasingly common (e.g. many Android programmers)
  Graphical IDEs available (Eclipse, NetBeans)

## Slide 7: What new SIAM features are needed?
Serial drivers for pump, prop, other “custom” devices
“Universal” instrument driver: Reduce need for device-specific driver development
  Leverage SID, Sensor Pod approaches; extend BaseInstrumentService
  ‘Wizard’ GUI to define instrument protocol
GUIs to configure, monitor and control the system
  Leverage configt, Salamy GUI experiences
Easy conversion to MatLab-compatible format
If Android, need RMI replacement
USB instrument port for camera driver?
Digital I/O port for other sensors?
Bluetooth instrument port?

## Slide 8: SIAM GUI functions
Configure SIAM node (similar to configt)
Driver configuration wizard, XML authoring (builds on Schlining’s prototype)
  Replaces manual edit of jar Makefile
System status; ports, instruments, resources, etc (builds on Headley and O’Reilly prototypes)
FOCE-specific functions (ala Salamy GUI)

## Slide 9: Oracle JavaSE Embedded Virtual Machine
Supported on ARMv5 and higher

## Slide 10: ARM processor candidates (Oracle JVM runs on these)
BeagleBone
GumStix Water
TS-7800

## Slide 11: Serial comms

## Slide 12: Power
GumStix: ~2 W running SIAM
What is total xFOCE power budget?