## Slide 1: Modified design idea #1865
Tom O’Reilly

## Slide 2: Option A: Drivers on sensor node (aka ultra-low power option)
Advantages
  Low power consumption; gateway sleeps most of the time
  Real-time scheduling
Potential drawbacks
  Harder to debug/modify code in the field? (Non-trivial drivers may require this)
  Must track which sensor node is associated with exactly which instrument(s)
  Code reuse-portability issues
  Need to develop gateway-to-sensor node protocol
  Separate tool-chains, procedures needed for sensor node and gateway node

## Slide 3: Option B: Drivers on gateway node
Advantages
  Easier to debug/modify code in field?
  Gateway speaks to instruments in their native protocols (no need to develop additional protocol)
  Option for Python or Java implementation; potentially very portable (e.g. to other MBARI projects)
  More resources for “complex” drivers
  Single development tool-chain
  Fewer at-sea processors
Potential drawbacks
  Gateway must be “on” when acquiring data
  Gateway OS/language may not be hard real-time; sampling jitter (what are RT requirements?)

## Slide 4: Option B concept: Android gateway
Android-capable gateway node
  Phone on surface gateway (provides screen/console)
  BeagleBone on underwater gateway
xFOCE app for data acquisition
  Instrument drivers run as Android “services” in the background
  CO2 injection loop
  GUIs for configuration, monitoring, data quick-look
  DataTurbine provides data streams and logging

## Slide 5: xFOCE Gateway Android app
Implemented in Java (perhaps with native ‘C’ components for performance)
Provides driver framework, extended to implement specific drivers
Includes “Universal” driver, which may be applicable to many instruments
Standard Android development environment
  Eclipse plug-in
  Symbolic debugger
  Device emulator

## Slide 6: xFOCE app is simpler than SIAM
No RMI (and no need for Node classes?)
No custom power management (provided by Android)
No custom comms management (provided by Android)
Simpler logging (provided by DataTurbine)
Simpler “portal” functionality (provided by DataTurbine)
PROTOTYPE DEMO