## Slide 1: xFOCE/swFOCE Data System

## Slide 2: xFOCE Data
Controller
Controller
Distribution
Distribution
Basic requirements
  Sample rates, Timestamp accuracy (1 s)
  Time-stamped archive of experiment data
  Flexible data archive format (time-stamped CSV)
  Health and status monitoring
Users will prefer different ways to access data
  MATLAB, Excel, LabView, custom utilities…
Well defined (and standard) interfaces are key
  Configuration and control interfaces
  Data access interfaces:
    Services, clients, applications
    Simple, efficient, support low-bandwidth links
  Data archive formats
Metadata
  Science and system contextual data
    Changes to instruments, sampling, calibrations
    Ground faults, leaks and other system faults
  Enables understanding of what is (or did) happen
  Provides insight into anomalies, troubleshooting
Driver
Device
Controller
Archive
Distribution
Driver
Device
Transformation
Archive
Query
Configuration
& Control
Clients
Presentation
Links

## Slide 3: swFOCE Data
Added requirements
  Remote access
    Multi-user
    Separate administrative access
  Metadata management
  Compatibility w/ dpFOCE data
  Ground fault monitoring
  Still/video image data

## Slide 4
Access
Server
Controller
Controller
OSDT Server
Controller
Controller Software
swFOCE Data
OSDT?
Data ACQ
Services
Control Service
Data ACQ
Services
Data ACQ
Services
Instrument Data
Archive
Instrument Data
Archive
Local Data
Archive
Open Source
DataTurbine
Flow
CTD
pH
DO
OSDT Data
Archive
SSDS Server
SSDS
SSDS Data
Archive
Data
ACQ
Data
ACQ

Seafloor
Hopkins
Remote
FOCE GUI
Control, monitor
Real-time Data Viewer (RDV) OSDT client
Live, post-experiment
data playback
Shore Side Data System (SSDS)
Primary data archive
MBARI internal standard
Access
Service
HTTPS
TCP, UDP
HTTPS
Java RMI
ESW
Flow
User
Tools
TCP, UDP

## Slide 5: UI
Help users to understand and simplify key choices
What UI choices will the user make related to UI
  Network, interfaces, security
How do those choices affect concerns (performance, flexibility, ease, cost)
What are pros/cons of various choices
  Cost, power, bandwidth, software skill, processing capability, software/system dependencies
Modularity
  Interfaces that support flexibility in UI choices
  Expansion path: what’s needed up front to start simply and build capability
Sketch out a couple of concepts at either end of the spectrum
Specific choice/detail more important for SWFOCE

## Slide 6: UI System Requirements
Network Connectivity (Ethernet, Serial, Wireless)
Health and Status (heartbeat on connection)
Control Application Programming Interfaces (APIs) – System and Instruments
Data Collection APIs
Security:
  User Authentication/Authorization
  Enforce Maintenance or Lockout of System (unless mechanical)
Node/Instrument List (registry)
Metadata access / management
Data Format and Parsing (or pick data format)
System Change Notification (push notification for low bandwidth)
Scaling and Extensibility (all the above for additional instruments)
Data repository for historical data

## Slide 7
REQUIREMENTS | xFOCE | SWFOCE
1. Network Connectivity |  | 
2. Health and Status |  | 
3. Control APIs for both System & Instruments |  | 
4. Data Collection APIs |  | 
5. Security |  | 
6. Node/Instrument List (Registry) |  | 
7. Metadata Access Management |  | 
8. Data format and parsing |  | 
9. System Change Notification |  | 
10. Scaling and Extensibility |  | 
11. Data repository |  | 

## Slide 8: UI Functions

## Slide 9: One end of the spectrum

## Slide 10: The other end (swFOCE)

## Slide 11: The other end (swFOCE)
COMMS

## Slide 12: The other end (swFOCE)
Comms
Transport

## Slide 13: The other end (swFOCE)
Comms
Transport
Security

## Slide 14: The other end (swFOCE)
Comms
Transport
Security

## Slide 15: The take home
Take a controlled, layered approach architecture
Define options for comms
Design transport for system concerns and comms
  RPC
  Messaging
  ?
Design security/safety
Explicit, well document and controlled interfaces/APIs
These core system APIs can be used by any type of client
  Command line
  Direct client application
  Remote Client