## Slide 1: Desktop testbed: goals
Gain familiarity with object and methods
  Fluidics
  Optics
Find out what is possible
  Scaling of performance to deployable prototype
  Direction to design optimization
Test ideas
  Cell phone cytometer
  Automated fluorescent microscope

## Slide 2: Approach – what do we need?
Technology evaluation criteria
Draft adaptation requirements (LRAUV)

## Slide 3: Key criteria
Adaptability to autonomous platform
Science “performance”
Maintenance stability
Actionable data
Size, power
Shock
Tilt
Population diversity
Throughput
Maintenance
Alignment
Biofouling
Trigger sampling
Telemetry
Screening/sorting
Temporal spatial resolution

## Slide 4: Key criteria
Adaptability to autonomous platform
Science “performance”
Maintenance stability
Actionable data
Size, power
Shock
Tilt
Population diversity
Throughput
Maintenance
Alignment
Biofouling
Trigger sampling
Telemetry
Screening/sorting
Limiting use on many platforms
Population statistics in real time is challenging
Length of deployment
Unattended operation
Configurability
Temporal spatial resolution

## Slide 5: Benchmark: fluorescent imaging
Filtering 25 ml on 0.2um black polycarbonate filter
Sampling, 125 ml
Fixing with Glutaraldehyde
Visual identification, counting
Translating stage
Change objective: 10x, 40x, 100x
Entering spreadsheet

## Slide 6: Benchmark: fluorescent imaging
Ciliate with sequestered chloroplasts, at 100x
Zeiss Axioplan fluorescence microscope
Courtesy of Lisa Ziccarelli

## Slide 7: Benchmark: fluorescent imaging
Pseudo-nitzschia, at 100x
Courtesy of Lisa Ziccarelli
Zeiss Axioplan fluorescence microscope
Chaetoceros, at 100x

## Slide 8: Optics: excitation and fluorescence
(1) http://www.oceanopticsbook.info/view/optical_constituents_of_the_ocean/_phytoplankton
(2) http://mhl.nsw.gov.au/projects/berowra/chloro.php
Chlorophyll absorption (1)
Pigments absorption (2)
(3) http://www.photobiology.com/photobiology99/contrib/danuta/
Chlorophyll fluorescence (3)
Light source + excitation filter
Detector + emission filter

## Slide 9: Cell phone test stand
X-Y-Z stage
Optical base plate
Cell phone
Sample on a slide
Optical filter film (for fluorescence)
Micro lens

## Slide 10: Cell phone: Kyocera C5155
2048x1536
1.6 um / pixel
1 mm grid
85 um line
45 um, 27 pixel

## Slide 11: Cell phone: HTC Nexus One
2592x1944
1.3 um / pixel
1 mm grid
85 um line
With red film filter
Cross-talk!!!

## Slide 12: Optics: Filters
LED Luxeon Royal Blue 455 nm
Roscolux #19 red film
Cross-talk regions
Problem!!!

## Slide 13: Optics: Filters
LED Luxeon Royal Blue 455 nm
+
Roscolux #19
Blue is still visible
Problem!!!
LED Luxeon Royal Blue 455 nm
+
Blue filter (Intor 450-40)
+
Red filter (Roscolux #19)

## Slide 14: Optics: Filters
LED Luxeon Royal Blue 455 nm
540 Long Pass Filter (Intor)
Cross-talk region
Problem!!!

## Slide 15: Optics: Filters
Filter search
Film
Plastic
Interference filters

## Slide 16: Optics: Filters
LED Luxeon Royal Blue 455 nm
+
Intor 450-40 filter
Delvie 2422 plastic filter
Isolation region
Cross-talk removed!

## Slide 17: Testbed
X-Y-Z stage
Base plate
Imaging Source camera
Blue LED
White LED
Microscope objective
Lens tube

## Slide 18: Testbed: imaging scale
4x objective
1600x1200 pixel
1600 um wide = > 1 um / pixel
10x objective
1600x1200 pixel
650um wide = > 0.4 um / pixel
100 um optical glass target

## Slide 19: Testbed: imaging scale
4x objective
1600x1200 pixel, 1 um / pixel
RG630 filter
BW camera
Fluorescence
White light

## Slide 20: Optics: optimization

## Slide 21: Some open questions, issues
How best to compare AUV integration candidates?
  So far have compared “marketing” specifications
  What are current top candidates?
Deployment duration, particle size range? (affects design significantly)
Need close science engagement during prototype development