## Slide 1: Testbed: goals
Gain familiarity with object and methods
  Fluidics
  Optics
Find out what if possible
  Scaling of performance to prototype
  Direction to design optimization
Test ideas
  Cell phone Cytometer
  Automated fluorescent microscope

## Slide 2: Cytometer technology for autonomous platforms 2014 Kickoff
Tom O’Reilly and Denis Klimov
Jim Bellingham
Francisco Chavez
Alex Worden

## Slide 3: Project focus
Cytometry (fr. Greek “cell measurement”): General name for methods that measure parameters of individual cells
  Flow cytometers
  Microscopes (including fluorescent microscopes)
  Coulter counters
No “one size fits all” solution

## Slide 4: Project allocation and budget
O’Reilly (project manager) – 23 days
Klimov - 40 days
Budget: $6,800 (travel, test-bed components)

## Slide 5: Schedule and milestones
Discuss SeaFlow during Swalwell visit to MBARI | 2/5
Demonstrate fluorescent microscope test-bed, version 1 | 6/1
Evaluate loaner instrument in fall CANON (e.g. Submersible Microscope) | 9/15
Annual project report, including test-bed results | 12/15

## Slide 6: Methods comparison
Optical methods of detection
Proxy to population composition
  Size
  Pigment
Fluorescence can be used with most methods by adding appropriate channel
Trade-off method advantages/drawbacks for applications

## Slide 7: Bulk scattering
Min ~10E3- 10E4 cells / scatter scan for repeatability
High throughput at relatively low processing cost
Harder to interpret larger / complex morphology cells
Sensitive to cell (random) orientation
High–res detector
Signature decomposition

## Slide 8: Flow cytometry
Limited dynamic range vs. wide natural range population composition
If detection volume is set to be able to resolve pulses from small particles, then statistics on larger cells with low concentration is becoming unacceptably slow
Hard to interpret data for larger / complex morphology organisms
Flow
Resolution
Concentration
Statistics
Optimization
Narrow range of parameters
Detection volume
Light
Signal on detector

## Slide 9: Imaging cytometry
Wider dynamic range on cell size vs. statistics
Works better for larger/ complex morphology organisms
Does not work well for smaller (< 5um) organisms
Flow
Detection volumes
Space domain
Resolution of morphology
Wider range of parameters
Detection volumes

## Slide 10: Scale comparison
Different detection methods have different optimum size range
There is certain overlap
Combination methods help overcome limitations and expand application range
1 um
10 um
100 um
1000 um
particle size
0.1 um
Flow cytometry
Imaging
Bulk scattering

## Slide 11: Hardware
Imaging cytometer, 2 channels:
  Imaging and fluorescence imaging
  Synchronous or asynchronous acquisition?
Ability to package into compact instrument
Maintenance/ longevity
Camera and imaging vs. processing platform
Same image or different images?
organic vs. inorganic
Flow cell configuration
Could decouple for larger system
Or integrated (cell phone?)

## Slide 12: Hardware
Optics:
  1 or 2 cameras?
  Tunable filter?
  Still images vs. video?
Light source:
  Triggering, optical resolution
Size, complexity
Attractive, but problem of contrast
Could orientation be tracked at the cost or resolution?

## Slide 13: Hardware
Orientation seems to be common theme
  Can it be controlled?
Bulk vs. hydro focusing
Pressure, velocity gradient
Acoustics
Electric field?
Recirculation helps keep clean = > longevity
Larger cells sizes possible

## Slide 14: Software
Simplified imaging processing algorithm
  Particle length and width
  Fluorescent vs non-fluorescent
  Area, integral signal => proxy to biomass
Triggered image logging, other actions
Prototype runs on laptop, should be embedded in the future
Explore hardware acceleration, e.g. with FPGA or GPU

## Slide 15: Example processing chain, implemented in GPU/FPGA
From “A hardware accelerated approach for imaging flow cytometry”, Lee, Meng et al (2013)

## Slide 16: Some open questions, issues
How best to compare AUV integration candidates?
  So far have compared “marketing” specifications
  What are current top candidates?
Deployment duration, particle size range? (affects design significantly)
Need close science engagement during prototype development