## Slide 1: Cytometer technology for autonomous platforms 2014 Kickoff
Tom O’Reilly and Denis Klimov
Jim Bellingham
Francisco Chavez
Alex Worden

## Slide 2: Project focus
Cytometry (fr. Greek “cell measurement”): General name for methods that measure parameters of individual cells
  Flow cytometers
  Microscopes (including fluorescent microscopes)
  Coulter counters
No “one size fits all” solution

## Slide 3: Project goals
Investigate cytometers that could be integrated with LRAUV or Dorado
Build lab test-bed to study approaches (hardware and software)
Evaluate available cytometers
Facilitate collaboration with external cytometer developers (commercial, academic)

## Slide 4: Project allocation and budget
O’Reilly (project manager) – 23 days
Klimov - 40 days
Budget: $6,800 (travel, test-bed components)

## Slide 5: Schedule and milestones
Discuss SeaFlow during Swalwell visit to MBARI | 2/5
Demonstrate fluorescent microscope test-bed, version 1 | 6/1
Evaluate loaner instrument in fall CANON (e.g. Submersible Microscope) | 9/15
Annual project report, including test-bed results | 12/15

## Slide 6: Methods comparison
Optical methods of detection
Proxy to population composition
  Size
  Pigment
Fluorescence can be used with most methods by adding appropriate channel
Trade-off method advantages/drawbacks for applications

## Slide 7: Bulk scattering
High throughput al low processing cost
Harder to interpret larger / complex morphology cells
Sensitive to cell orientation
High–res detector
Signature decomposition

## Slide 8: Flow cytometry
Limited dynamic range vs. wide natural range population composition
If detection volume is set to be able to resolve pulses from small particles, then statistics on larger cells with low concentration is becoming unacceptably slow
Hard to interpret data for larger / complex morphology organisms
Flow
Resolution
Concentration
Statistics
Optimization
Narrow range of parameters
Detection volume
Light
Signal on detector

## Slide 9: Imaging cytometry
Wider dynamic range on cell size vs. statistics
Works better for larger/ complex morphology organisms
Does not work well for smaller (< 5um) organisms
Flow
Detection volumes
Space domain
Resolution of morphology
Wider range of parameters
Detection volumes

## Slide 10: Scale comparison
Different detection methods have different optimum size range
There is certain overlap
Combination methods help overcome limitations and expand application range
1 um
10 um
100 um
1000 um
particle size
0.1 um
Flow cytometry
Imaging
Bulk scattering

## Slide 11: Test bed hardware details
Imaging cytometer, 2 channels:
  Imaging and fluorescence imaging
  Synchronous or asynchronous acquisition?
Ability to package into compact instrument
Maintenance/ longevity (flow cell configuration)
Camera and imaging vs. processing platform
Simplified imaging processing algorithm
  Length/ width
  Area, integral signal => proxy to biomass
Ability for unattended operation

## Slide 12: Test bed software details
Simplified imaging processing algorithm
  Particle length and width
  Fluorescent vs non-fluorescent
  Area, integral signal => proxy to biomass
Triggered image logging, other actions
Prototype runs on laptop, should be embedded in the future
Explore hardware acceleration, e.g. with FPGA or GPU

## Slide 13: Example processing chain, implemented in GPU/FPGA
From “A hardware accelerated approach for imaging flow cytometry”, Lee, Meng et al (2013)

## Slide 14: Some open questions
How best to compare AUV integration candidates?
  So far have compared “marketing” specifications
  What are current top candidates?
Deployment duration? (affects design significantly)