## Slide 1
Wind speeds (10 m) from NDBC buoy 42040 used when anemometer on Wave Glider failed.
pH2O computed from temperature and salinity following Weiss and Price (1980)
pCO2 is the computed water-saturated partial pressure from measured xCO2 and, barometric pressure and pH2O following Sabine et al.,(2000);
Flux of CO2 to atmosphere (F) computed via
  The piston velocity k (Wanninkhof, 1992)
  where Sc is the Schmidt # computed via a temperature dependence following Wanninkhof (1992) using empirical relationships determined by , Jähne et al., (1987)
  s is the solubility of CO2 as a function of temperature and salinity (Weiss, 1974)
  The
Chlorophyll a concentrations from MODIS on the Aqua satellite were obtained from the OceanColor website of NASA/GSFC (http://oceancolor.gsfc.nasa.gov/cgi/l3) at 4 km resolution.
A Pilot Project for Autonomous Ocean Acidification Surveys in the Northern Gulf with the Liquid Robotics Wave Glider. #033
Stephan Howden1, Jamie Griffin2, Rik Wanninkhof3, Gernot Friederich4, Kjell Gundersen5 and Kevin Martin1
1University of Southern Mississippi, 2Liquid Robotics, 3NOAA/AOML, 4MBARI,5Institute for Marine Research (Havforskningsinstituttet) Bergen, Norway.
Summary
Acknowledgements
This project was funded by a NOAA grant, through the Northern Gulf Institute, to member institution the University of Southern Mississippi, and from a NOAA grant to the Gulf of Mexico Coastal Ocean Observing System to Liquid Robotics. Wai-jun Cai of UGA provided analysis of TA and DIC from wet samples. The Liquid Robotics deployment, recovery, and operations teams were essential to the project.
Wave Glider Instruments
Deployment 01/23/2013-02/27/2013
Lon
The CO2 flux over the course of the mission varied between -55.72 and 3.56 mmol m-2 d-1 with an average of -8.33.
Dividing the mission into prior and after the glider sat in a watch circle around CenGOOS buoy the average fluxes were -5.63 and -14.33 mmol m-2 d-1 , respectively.
Waveglider could adaptively sample regions where uncertainty in remote retrievals of pCO2 is high
In this application the Wave Glider with the MBARI OA package has been shown to be useful in monitoring a spatially and temporally heterogeneous region for air-sea carbon flux and seawater pH. These platforms will help achieve the goal of developing the monitoring capacity to quantify and track ocean acidification, called for in the NOAA Ocean and Great Lakes Acidification Research Implementation Plan.
MODIS Image February 17, 2013
MODIS Image January 23, 2013
Deployment and Recovery Location
Methods
Wave Glider back at buoy station
References
USGS Mississippi River Gauge at Baton Rouge, Louisiana
River was below the 5 year average from October 2012 through most of January 2013 but at or above average for most of the Jan-Feb deployment
Braatz, A. (2011) M.S. Thesis, The University of Southern Mississippi, Hattiesburg, MS, pp86.
Jähne, B., K. O. Münnich, R. Bösinger, A. Dutzi, W. Huber and P. Libner (1987), On the parameters influencing air-water gas exchange, J. Geo.phys. Res., 92, 1937-1949
Lohrenz, S. E. and W.-J. Cai (2006), Satellite ocean color assessment of air-sea fluxes of CO2 in a river-dominated coastal margin, G. Res. Let. 33, L01601, doi:10.1029/2005GL023942.
Lohrenz, S. E., W.-J. Cai, F. Chen, X. Chen, and M. Tuel (2010) , Seasonal variability in air-sea fluxes of CO2 in a river-influenced coastal margin, J. Geophys. Res. 115, doi:10.1029/2009JC005608.
Wanninkhof, R. (1992), Relationship between wind speed and gas exchange over the ocean, J. Geophys. Res. 97, 7373-7382.
Weiss, R. F. (1974). Carbon dioxide in water and seawater: The solubility of a non-ideal gas, Mar. Chem. 2, 203-215.
Weiss, R. F. and B. A. Price (1980), Nitrous Oxide solubility in water and seawater, Mar. Chem., 8, 347-359.
+
This study
Lohrenz et al., 2010
Braatz, 2011
Lohrenz and Cai 2006
Drought conditions
Average CO2 Flux
Mississippi River Outflow
<2005-2009>
actual
Chlorophyll a [mg m-3]
Latitude
Longitude
pCO2 air
pCO2 seawater
NDBC Buoy 42040
U10 [m/s]
S [psu]
T seawater [oC]
dO [mg/l]
pH
MODIS Chl_a 01/23
MODIS Cha_a 02/17
CO2 Flux to atmosphere
Airmar PB200 Weather Station | Airmar CS4500 Water Speed Sensor
Seabird GPTCTD 90688 CTD w/high speed pump | Seabird SBE43F DO
Honeywell Durafet pH | Li-cor 820 pCO2
Means and Standard Deviations of Data Binned in 2 m/s Winds
All data Binned into 2 m/s wind speed bins. Fluxes change due to both temporal and sparial variations
Only data collected while Wave Glider was at CenGOOS buoy location. Flux changes driven mostly by time variation of winds
Real-time Data
In collaboration with the Gulf of Mexico Coastal Ocean Observing Center (GCOOS) the data were served in real-time on its Products website with an ESRI server application.
CenGOOS Buoy and Wave Glider launch and recovery site
Stations for the GOMECC cruises
Wave Glider track