## Slide 1: MBARI Wave Glider “Hot Spot” applications
Tom O’Reilly and Brian Kieft

## Slide 2: Hot Spot payload
Relay data between autonomous sensor platforms, shore; geolocate/track assets, features
Acoustic modem, directional acoustic transponder
Cellular, satellite, WiFi, 900 MHz, antennas – distinct from Wave Glider “core” radios
Application software on SMC
Inspired by work of Rajan, Borges de Sousa, Pinto, Martins et al (University of Porto LSTS)

## Slide 3: Hot Spot Acoustics
Acoustic modem – range, data exchange
Directional Acoustic Transponder (DAT) – bearing/range/elev
Target (e.g. AUV) carries acoustic modem or DAT

## Slide 4: Hot Spot radios
Line-of-sight to AUV
  802.11 Wifi (Ubiquiti)
  900 MHz (Freewave)
Link to shore
  Cell modem (coastal regions)
  Globalstar satellite (coastal, some open ocean)
  Iridium satellite (world-wide)
Notes: Console capaibilty; through ssh (cell, Globalstar) or Iridium console

## Slide 5: Cell signal strength at Hot Spot

## Slide 6: Hot Spot applications
Gateway console applications
  User ssh/dial-in to Hot Spot via satellite or cell, then connect to asset via RF or acoustic
  Data retrieval, trouble-shooting, reconfiguration...
Autonomous applications
  Acoustic geolocation
  AUV navigation, target tracking/stalking
  AUV command/telemetry relay

## Slide 7: Hot Spot gateway console
AUV on surface
AUV, benthic instruments
Notes: User logs into Hot Spot via cell or satellite, then accesses onboard RF or acoustic interfaces to connect with vehicles/instruments, get status, other data. Real-time interaction with assets anywhere on Earth. No ship needed

## Slide 8: Autonomous navigation apps
Offboard (from shore)
  Invoke LR wcs script to send WG commands
Onboard (from SMC)
  Send commands to CCU through LR interface
Applications:
  Geolocate, follow vehicles/instruments
  Adaptive sampling, front detection
Notes: Autonomous navigation apps eliminate need for continuous human control through WGMS. Offboard commanding is subject to WGMS latency.

## Slide 9: Autonomous onboard navigation apps
Requires Regulus, Python, Java on SMC
Issue gotoWatch() command to CCU through CORBA interface
  CCU ship avoidance supercedes navigation commands
Issue alarms/events, any other WG command to CCU as appropriate
Commands reflected in wgms ‘commands history’
Notes: Can issue ANY wave glider command to the CCU

## Slide 10: Hot Spot “stalking” algorithm
Get target bearing/range/elev from DAT
Compute target lat/lon, depth
If target location is “safe”, command vehicle to circle target
Repeat every n seconds
Main vehicle
computer
Hot Spot SMC
rudder
DAT
GPS
Nav cmd
GPS loc
“Black box”
application
Notes: Compute target lat/lon from bearing/range (DAT) and Wave Glider lat/lon (GPS)

## Slide 11: Chase application: Lagrangian drift sampling
Drifter
Wave Glider
Profiler
R/V Rachel Carson
Notes: Drifter LRAUV moves with current, servos to thermocline or other depth surface using variable buoyancy system. Wave Glider and profiler LRAUV acoustically determine drifter LRAUV location and circle it. All three vehicles carry science sensors (CTD, fluorescence, backscatter, dissolved oxygen). Crewed ship periodically visits to take water samples for genomic/microscopic/isotopic analysis, uses Wave Glider surface location to easily locate the volume to be sampled.

## Slide 12: Lagrangian drift sampling: October 2014
profiling AUV
WG, following drifting AUV
drifting AUV at thermocline
Wave Glider autonomously chased drifter for 48 hours
1000 m
Notes: RV Rachel Carson able to easily locate Wave Glider. Acoustic track shows small wiggles which are artifacts – note that we don’t yet account for offsets between DAT, compass, GPS
Autonomous navigation saved operational cost – no need for operator to continually issue commands through WGMS interface
Last Fall navigation commands were issued automatically from on shore following receipt of target location from WG cell; now they issued directly from the Hot Spot payload to the main vehicle computer.

## Slide 13: Range-only geolocation
Advantages
  Acoustic modem; relatively cheap, simple gear
Limitations
  Multiple range measurements, energy, time needed
  Best accuracy for stationary/slow targets
Notes: In collaboration with Ivan Masmitja, Joaquin del Rio at Polytecnic University of Catalunya

## Slide 14
Test1
Test2
Benthic Rover
Station M, 4000 m depth
Crawl speed: ~3 m/day
Acoustic modem
WG Hot Spot application
Navigates WG in specified pattern centered on specified point
Acquires acoustic target range at specified interval
Computes target location (x, y, z)
Masmitja, Kieft, Gomariz, del Rio, O’Reilly
Session 212
Marriot Santa Barbara room
Tuesday 3:30-5:00 pm
Notes: Need to periodically check Rover status, position via acoustic modem link.
Previously used crewed ship – costing several days
Now using Wave Glider Hot Spot

## Slide 15: Disruption tolerant ‘data mule’
Hot Spot automatic store-and-forward data between vehicles, shore
rsync file-transfer protocol
  It’s everywhere; very robust implementations
  Very efficient “delta-transfer” algorithm
  Disruption-tolerant; transfer resumes where it left off
  Requires TCP/IP link
Notes: Rsync is included with most Linux distributions – no need to install

## Slide 16
Cellular
802.11
cache
incoming
outgoing
incoming
outgoing
Hot Spot store-and-forward exchange using rsync
Pull outgoing files from AUV into cache
HOT SPOT
SHORE

## Slide 17
HOT SPOT
SHORE
Cellular
cache
incoming
outgoing
802.11
incoming
outgoing
Push cached files destined for AUV
Pull outgoing files from shore into cache
Hot Spot store-and-forward exchange using rsync

## Slide 18
Cellular
cache
incoming
outgoing
Push cached files destined for shore
HOT SPOT
SHORE
Hot Spot store-and-forward exchange using rsync
Notes: If RF link breaks mid-transfer, rsync will pick up where it left off on next attempt. If destination link not available, rsync will try later; Hot Spot is store-and-forward/data-mule.
Only differences between source and destination are transferred; so if ‘n’ bytes are added to an N-byte file between retrievals, only ‘n’ bytes are transferred

## Slide 19: Collision
WG running tests for several days, 3 km from harbor mouth
Light, radar target enhancer on
Ship AIS avoidance enabled
Hit by object not carrying AIS
  15:00 local time – daylight
  Cracked solar panels, broken antennas/masts, float damage

## Slide 20: Collision
Smoke from Big Sur fire limited visibility to few hundred meters
Hot Spot onboard autonomous navigation was running, but ship avoidance was enabled, no AIS signal detected
Repairs cost $14K, 33 days – but collision occurred after 380 sea days, 20,000 km
Lessons:
  Spending time near harbor mouth may increase risk
  Significant risk from non-AIS vessels

## Slide 21: Questions?