## Slide 1: Mobile Hotspot Preliminary* Design Review Tom O’Reilly / Mark Chaffey
* “The aim of the preliminary design review is that from now on the team is working on a single ‘point’ design…”

## Slide 2: Wave Glider (WG) HotSpot Functional Requirements
Support 2013 Autonomy field trials and the 2013 CANON fall experiment.
  Provide data transfer from mobile platforms to MBARI servers with minimum latency.
Provide bidirectional data transfer with:
  Significantly higher resolution than the current capability using AUV based Iridium satellite modems.*
  Minimum platform surface time.
Provide these capabilities anywhere along the California coast where MBARI may conduct field operations.
Simple configuration and operation.
Don’t restrict HotSpot platform to WG.
  Loose coupling to WG infrastructure
Allow future expansion to acoustic communications.
Don’t re-invent existing solutions.
* An AUV generates ~ 10MB of data per hour and the current feasible data return during the mission is several hundreds of bytes per hour.

## Slide 3: WG HotSpot Design Requirements
Communicate to mobile platforms via line-of-sight (LOS) radio link.
  For Dorado must use a 900 mHz FGRplus-RE ethernet radio.*
  802.11 WiFi link for Porto group Seacon AUVs.
Communicate to MBARI servers by linking using:
  via public wireless phone network
  via Over-the-Horizon satellite communications link
      Initially Iridium RUDICS
      Future migration to a less expensive, higher bandwidth option.
Use leased WG platform
  Available energy limited by stock capability and other users (~10W).
  Minimal or no customization of WG possible.
* Pending hardware confirmation from Hans T.

## Slide 4: WG HotSpot Design Requirements cont…
Minimize shadowing of solar panels.
Minimize antenna weight aloft.
Maximize antenna heights.
Minimize interference with lifting bail.
Do not create RF interference between 900 MHz radios, Iridium and wireless phone modems*.
  Maximize vertical antenna separation.
  Minimum 20cm horizontal antenna separation.
*Also unknown interference potential from radar Racon.

## Slide 5: Fall 2013 CANON Near Shore (<10nm) Gateway Relay to MBARI Scenario
MBARI intranet
ODSS, etc.
Firewall
FreeWave 900 MHz
<1nm range
Land Based 3G GSM/GPRS/EDG Cellular modem 1000/500kbs downlink/uplink
Wave Glider
802.11G
FreeWave 900 MHz
Drifter
Dorado AUV
Seacon AUV

## Slide 6: Fall 2013 CANON Offshore Gateway Relay to MBARI Scenario
MBARI intranet
ODSS, etc.
Firewall
IP WAN
Iridium Rudics – 2.4kbs
Globalstar – 9.6kbs
FreeWave 900 MHz
<1nm range
802.11G
Dorado AUV
Drifter
Seacon AUV
FreeWave 900 MHz
Wave Glider

## Slide 7: Software topics
Proposed approach
DTN compared with rsync
Bent pipe vs store-and-forward
Link management
Rsync-based algorithm
Required interfaces

## Slide 8: Proposed HotSpot approach for 2013
Store-and-forward files using rsync
  No DTN
  Bent pipe not supported
  Files only, not “remote procedure calls”
HotSpot acts as TCP/IP gateway in “console” mode
Link management
  Some links always-on
  Scheduled links (e.g. satellite, cellular)
  Auto link select between satellite/cellular

## Slide 9
shore endpoint
dorado endpoint
seacon endpoint
HotSpot
tethys endpoint
HotSpot stores and forwards files between “endpoints”
3g
Freewave
Freewave
802.11

## Slide 10: DTN compared with rsync
 | DTN | rsync
Bent pipe support | yes | no
Dynamic endpoint | yes | yes
Non-IP support | Integrated CLA interface, some existing CLA drivers | Design/implement non-IP driver interface
Multi-hop routing | yes | no
Tolerant to link disconnect | yes | yes (‘-partial’ option)
Reliability | DTN daemon issues | very reliable
Configuration | Complex, poorly documented | Straightforward; well-documented
Documentation | poorly organized | extensive
Development effort | Debug existing DTN C++ code, develop scripts | Develop rsync scripts, configuration
Wider adoption | Experimental; No known operational applications | Pervasive

## Slide 11: Bent pipe vs store-and-forward
Bent pipe
  HS relays each message to destination as it receives it from source
  Source and destination links are simultaneously active
Store and forward
  HS gets messages from source, stores them in a file, later sends file to destination
  One link active at a time
NOTE: Store and forward is REQUIRED, in case a link segment is down!

## Slide 12: File transfer airtime
Assume radios on AUV and HS with bit rates Rfast and Rslow
Assume transfer file of size Vfile from AUV to HS to shore
File transfer airtime T
  Store and forward: T = Vfile * (Rfast + Rslow)
  Bent pipe: T = Rslow* Vfile

## Slide 13: File transfer airtime
Assuming Vfile = 500 KB:
 | Freewave + RUDICS | Freewave + 3G | Freewave + Globalstar
Rfast | 96 kbit/s | 200 kbit/s | 96 kbit/s
Rslow | 2.4 kbit/s | 96 kbit/sec | 7.8 kbit/s
T (bent pipe) | 1667 s | 42 s | 513 s
T (store-fwd) | 1709 s | 62 s | 554 s
The additional store-fwd time is incurred over the faster link
The additional store-fwd cost is 10s of seconds in this example
Store-and-fwd incurs additional latency due to link scheduling

## Slide 14: Link management
Always-on link - e.g. Freewave listens for AUV
Scheduled link - e.g. periodically connect satellite modem to shore
  Control radio power when possible
  Adjustable schedule
  But must coordinate with AUV schedules (radio, surfacing)
Auto-selected link – e.g. use either cellular or satellite, depending on signal strength

## Slide 15: Link scheduling
On-demand: connect link in response to asynchronous event
  Requires connection “rules”, e.g. “Connect to shore immediately after data received from Dorado”
  Minimizes store-and-fwd latency
  Not required for 2013

## Slide 16: HS-AUV link management: HS radio always on
Endpoint turns on radio, negotiates with HS to establish link
Endpoint turns radio off after n minutes
  Unaware of data retrieval process; no need for “closing handshake”
  Partially-transferred file will be resumed on next comms session (“rsync –partial” option)
  Specify ‘n’ to balance on-surface time against average file size

## Slide 17: rsync store-and-fwd
Every endpoint has this structure in its file system:
  /outgoing/endpoint1
  /outgoing/endpoint2
  ...
  /incoming/endpoint1
  /incoming/endpoint2
  ...
  “endpoint1”, “endpoint2”, ... represent mnemonically useful host names, e.g. “dorado-gulper”, “tethys”, etc.
HotSpot file system has this structure:
  /endpoint1/outgoing/endpoint2
  /endpoint2/outgoing/endpoint1
  ...
Destination endpoint specified by subdirectory name
Shore treated like any other endpoint

## Slide 18: rsync store-and-fwd algorithm
When connection established with endpoint “eConnected”
# Pull outgoing from eConnected
rsync eConnected:/outgoing to local:/eConnected/outgoing
# Push incoming to eConnected
for each endpoint other than eConnected:
rsync local:/endpoint[i]/outgoing/eConnected
eConnected:/incoming/endpoint[i]
if (success) remove local:/endpoint[i]/outgoing/eConnected
Run periodically for always-on links, or when intermittent link connects
Use rsync “-partial” option to resume file transfer after network disruption – transfers single file over multiple sessions

## Slide 19: rsync store-and-fwd algorithm
Endpoint can detect new files with periodic scan of /incoming subdirectories, or via inotify
Interpretation of files is beyond HotSpot scope
  Could use file-naming naming convention, subdirectory structure, etc

## Slide 20: rsync store-and-fwd
Endpoint must have TCP/IP stack
Endpoint must run rsync daemon
Endpoint must provide account for HS access
All endpoints must agree on valid endpoint names; each endpoint must provide its name to HotSpot (e.g. via ZeroConf or during ppp link negotiation)

## Slide 21
WaveGlider SMC
802.11
Free
wave
Endpoint file cache
802.11
rsync
HotSpot app
Free
wave
/outgoing
/incoming
rsyncd
shore
ppp/SLIP
/outgoing
/incoming
rsyncd
Dorado
/outgoing
/incoming
rsyncd
Seacon-1
/outgoing
/incoming
rsyncd
Seacon-2
802.11
LAN
cell or sat
Internet
Fall 2013 CANON scenario

## Slide 22: Non-IP links
Non-IP “bridge” on HS - e.g. acoustic - transfers files between cache and non-IP link
Specify link as “acoustic” in HS configuration file
WaveGlider SMC
802.11
Free
wave
Endpoint file cache
rsync
HotSpot app
LAN
cell or sat
acoustic
Acoustic
bridge
Tethys

## Slide 23: Endpoint console function
Set HS as TCP/IP gateway to individual endpoints
E.g. - User can ssh from shore/ship endpoint to AUV endpoint
  RUDICS for shore-to-HS segment
  Freewave for HS-to-AUV segment

## Slide 24: How does HotSpot know...
Endpoint addresses?
  Could specify in HS configuration file, but auto-discovery is simpler for users
  Endpoints can advertise themselves via ZeroConf
When endpoint connected and ready for push-pull?
  Some links are scheduled, some are always-on, some may break
  HS could use ZeroConf, ppp ip-up script, and/or ping

## Slide 25: Standard endpoint names
Endpoint users must use subdirectory names that HS can map to IP address of another endpoint
  HS logs error when it can’t map directory name

## Slide 26: Interfaces accessed by HotSpot
Serial radio ports
Ethernet radio sockets
Radio power switches
Radio signal strength

## Slide 27: HotSpot-provided interfaces
Remote interfaces:
  /incoming and /outgoing directories on endpoints
Local interfaces (e.g. on WG SMC):
  List of available links
  Link status (bitrate, connected?, signal strength, etc)
  List of known endpoints
  Event log (e.g. files transferred, latest connection time, errors/warnings, etc)
  FUTURE: Assert connection on specified link
  FUTURE: Link quality index (includes %success rate, waves, etc)

## Slide 28: Open questions
How to schedule HS and endpoint radios to maximize connection probability?
  First experiments; HS radio always on? How does U Porto handle this?
Cell radio interface
  IP or serial?
  Need to set up ppp?
Wave Glider issues
  How does WG power management affect HotSpot?
  May want capability to manage HotSpot (e.g. modify radio schedules) via Wave Glider Iridium SBD

## Slide 29: WG HotSpot Electrical Interface A

## Slide 30: WG HotSpot Detail Interface A

## Slide 31: Wave Glider Mechanical Interface

## Slide 32: WG Preliminary Power Budget
HotSpot Power Budget |  |  | 
 | Power Use in Watts |  | 
Device | Sleep | Standby | Transmit
SMC Overhead* | 0.5 | 0.5 | 0.5
900MHz Modem |  | 0.14 | 4.4
802.11 Modem |  | 4 | 4
Iridium Modem |  | 0.4 | 1.25
Cellular Modem | 0.53 | 1.29 | 2.47
Totals | 1.03 | 6.33 | 12.62
Example 1 | 1.65 |  | 
Example 2 | 2.25 |  | 
Example 3 | 3.42 |  | 
Example 1 = 900MHz modem at 15% and Cellular at 20% |  |  | 
Example 2 = 900MHz, 802.11 modems at 15% and Cellular at 20% |  |  | 
Example 2 = 900MHz, 802.11 modems at 20% and Cellular at 50% |  |  | 
* Estimate |  |  | 

## Slide 33: Project Management
Detailed budget TBD.
  Estimate ~$20k
Schedule
  Have tested hardware ready for June Dorado cruises.
  Detailed milestones to June TBD.
    In a reversal, need to negotiate WG test time from Thom.
    Get radios and Wave Glider Sensor Management Computer (SMC) into Tom’s hands ASAP.
Resources remaining.
  Tom has about 320 hours
  Mark has about 294 hours

## Slide 34: Open Questions
Cell radio interface
  IP or serial?
  Need to set up PPP?
Wave Glider issues
  How does WG power management affect HotSpot?
  May want capability to manage HotSpot (e.g. modify radio schedules) via Wave Glider Iridium SBD
  Use Front or rear payload bay for electronics?
    Depends on Iridium modem sharing.
    Space considerations.
    Front housing more $.
  Use WG housing or our own?
    Recommend WG housing.
  Details of antenna mounting.

## Slide 35: END

## Slide 36: Public Cell Service Options
T-MOBILE: GSM 1700/2100 MHz, 1900 MHz (3G) or EDGE 1900 MHz (2G). SIM card system.
AT&T: GSM 850 MHz, 1900 MHz (3G). SIM. LTE 700MHz (4G), SIM.
Verizon: CDMA 850 MHz, 1900 MHz (3G) . No SIM. LTE 700MHz (4G), SIM.

## Slide 37: WG HotSpot Electrical Interface B