## Slide 1: Wave Glider Hot Spot
901411
(formerly 901224 DTN feasibility)

## Slide 2: Growing Data
Persistent presence + multiple assets = large datasets
Large data sources (Mb to Gb)
  Imaging
  Genomic
  ADCP
Background image: video taken by Tethys LRAUV, 12/2011

## Slide 3: Science Applications
Patch and organism tracking, minimize surface time
Acoustic navigation / localization
Informed decision making (e.g. through ODSS)

## Slide 4: Relevance to MBARI Strategic plan
“…adapt innovative technologies…”
  Exploration and discovery
  Ocean visualization
  Ecosystem dynamics
  Ocean biogeochemistry

## Slide 5: Specific Applications
Improve effectiveness and coordination of assets
    Distributed Autonomy
      University of Porto SeaCon AUV collaboration fall CANON 2013
    CANON / LRAUV
      LST tracking
      LRAUVs
    Aerostat
    Benthic Event Detectors

## Slide 6: The Cost of Data
Financial (ship time, data transfer)
  WG: $800/day, Ship: $12K/day
Opportunity cost

## Slide 7: The Cost of Data
Informed Decision Making
  EcoHAB spring 2013: decimated versus complete data

## Slide 8: Current Work
Radio and antenna integration
  Freewave (2)
  GSM Modem (Multitech 3G)
Dorado-WG link characterization sea trials
Initial Wave Glider Acoustic Work

## Slide 9: Current Work
1.34 Mbyte file-set:
Mean transfer time: 4.8 minutes
Mean transfer time within 200 meters: 3.6 minutes
Farthest successful transfer range: 450 meters, transferred in 8.0 minutes

## Slide 10: Current Work
Modem mounted here
Daphne iUSBL used to home
to Wave Glider
Initial acoustic work focused on homing to the Wave Glider.

## Slide 11: Future Work
Addition of Acoustic modem and interface
  iUSBL add on possibility
Add endpoints
  Refine protocols to demonstrate use with LRAUV, LST, BEDs
Globalstar/Iridium Integration*
802.11 Wifi*
GSM Modem Integration*
Power Management
Aerostat data transfer demonstration
Investigate Georgia Tech Agile Aperture Antenna (http://www.unmannedsystemstechnology.com/2013/06/gtri-agile-aperture-antenna-tested-on-autonomous-ocean-vehicle/)
* Work begins 2013, in Distributed Autonomy

## Slide 12: Equipment
Waveglider
Wave Glider Towbody*
Acoustic modem (LF)*
Acoustic modem (MF)*?
802.11 radio*
Satellite modems*
iUSBL (DAT MF)*?
* Proposing to share inventory from other programs

## Slide 14: SV3 Benefits
Extensible power bus
More energy available below the float (including the towbody)
Higher performance computing
Parallel integration/development with LRI (i.e. better support)
More payloads
Back seat driver
Propulsion
L&R from Paragon as usual