## Slide 1: Wave Glider Hot Spot 2016
901411
Brian Kieft, Tom O’Reilly

## Slide 2: Hot Spot on SV3
802.11
Iridium/GlobalStar
Cell
Acoustic
modem /usbl

## Slide 3: Antenna Height Matters
Antennas high above water line

## Slide 4: Where We’ve Been
12 Hotspot deployments over past two years
  Sea Tests (Dorado)
  Porto AUV/Dorado joint ops
  Station M (Benthic Rover x3)
  EcoHAB (LRAUV x2)
  Benthic Event Detectors
  Smooth Ridge (Rover)
  CANON (x3)
Transitioned SV2 payload box to SV3 Vehicle
Existing Capabilities / Payloads
  Autonomous following of AUV (DAT)
  Slant range geolocation (acoustic modem)
  Underwater Data Transfer (acoustic modem)
  Surface Data Transfer (wifi, 900 MHz)

## Slide 5: Lagrangian drift survey: October 2014
profiling AUV
WG, following drifting AUV
drifting AUV at thermocline
Wave Glider autonomously followed submerged LRAUV for 48 hours
1000 m
Notes: RV Rachel Carson able to easily locate Wave Glider. Acoustic track shows small wiggles which are artifacts – note that we don’t yet account for offsets between DAT, compass, GPS
Autonomous navigation saved operational cost – no need for operator to continually issue commands through WGMS interface
Last Fall navigation commands were issued automatically from on shore following receipt of target location from WG cell; now they issued directly from the Hot Spot payload to the main vehicle computer.

## Slide 6: Cost to transfer 13.4 MB AUV data per day
 | AUV-Iridium | AUV-HotSpot-cell | AUV-Hotspot-Globalstar
Total AUV surface time | 5.0 hours | 46 minutes | 46 minutes
Hot Spot operational cost | N.A. | $100 | $100
Airtime cost | $380 | $1 | $13
Total cost | $380 | $101 | $113
Notes: AUV - Hot Spot link: 900MHz radio AUV – Hot Spot range: < 400 meters
Iridium bandwidth: 2400 bits/sec
Compression: 2.7 AUV antenna wash-over: 10%
Iridium cost: $1.25/minute GlobalStar cost: $2.58/MB

## Slide 7: Cell signal strength at Hot Spot

## Slide 8: Where We’re Going
    Leverage Initial Investment
    Standard Payload
    USBL Improvements
    Further Automation
    Onboard Sensor Data Transfer
    LRAUV acoustic command/control/nav working with Jordan’s project

## Slide 9: Existing USBL Error
Mean bearing error:
26.2 deg
100 m
50 m
Tan 26.2= .492
R= 100m
~50m error

## Slide 10: Range Only Geolocation

## Slide 11: Collaboration
    Improve USBL Accuracy
    Automate Range Only Geolocation
    Collaboration Ivan Masmitja (SARTI UPC, Spain)
    Collaboration agreement in effect

## Slide 12: Onboard Sensor Data Gateway
Existing SV3 Sensor Architecture is:
  Power Hungry – 3W overhead for .25W sensor
  Poorly Documented:
      “Hi Tom,
      Unfortunately, our software architecture isn’t well documented or explained, even internally.”
    Ryan Carlon – Business Development, LRI
    04/27/2015
-Data feeds into existing paths

## Slide 13: Cooperative Work
    Wave Glider Sensor Payload Box and Towbody Engineering
    Integrated Acoustic Tracking proposal
        Localization software toolkit

## Slide 14: Previously Shared Inventory
Additional Hotspot for SV2
Acoustic modem (LF)
iUSBL (DAT MF)