Pilot Station
Pilot Right Pedestal

Fore/aft cmd	Joystick	ADC 0-5vdc	1
Turns cmd	Joystick	ADC 0-5vdc	2
Lateral cmd	Joystick	ADC 0-5vdc	3
Main Camera Pan cmd	Joystick	ADC 0-5vdc	4
Main Camera Tilt cmd	Joystick	ADC 0-5vdc	5
Main Camera Shoulder cmd	Joystick	ADC 0-5vdc	6
Trigger open (push)	M SPDT	DI low	1
Trigger close (pull)	M SPDT	DI low	2
Rocker deploy (up)	M SPDT	DI low	3
Rocker retract (down)	M SPDT	DI Low	4
Still trigger	M SPST	DI low	5
Pilot Left Pedestal
Vertical cmd	Slider	ADC 0-5vdc	7
VB Pump Control	Pot #1	ADC 0-5vdc	8
Spare Servo Valve cmd	Pot #2	ADC 0-5vdc	9
Spare Analog Input cmd	Pot #3	ADC 0-5vdc	10
Upper Camera Pan Left	M SPDT	DI low	6
Upper Camera Pan Right		DI low	7
Upper Camera Tilt Up	M SPDT	DI low	8
Upper Camera Tilt Down		DI low	9
Auto Heading	L SPST	DI low	10
Auto Depth	L SPST	DI low	11
Auto Altitude	L SPST	DI low	12
Cruise	L SPST	DI low	13
Bypass	L SPST	DI low	14
Bellypack Enable	L SPST	DI low	15
Depth Jog Up	M SPST	DI low	16
Depth Jog Down	M SPST	DI low	17
Aux Cam Zoom In	M SPDT	DI low	18
Aux Cam Zoom out		DI low	19
Aux Cam Focus Near	M SPDT	DI low	20
Aux Cam Focus Far		DI low	21
Aux Cam Select 0	Rot 8Pos	DI low	22
Aux Cam Select 1		DI low	23
Aux Cam Select 2		DI low	24
Aux Cam Select 3		DI low	25
Aux Cam Select 4		DI low	26
Aux Cam Select 5		DI low	27
Aux Cam Select 6		DI low	28
Aux Cam Select 7		DI low	29
Tlsld Tilt Up	M SPDT	DI low	30
Tlsld Tilt Down		DI low	31
Tlsld Pan Left	M SPDT	DI low	32
Tlsld Pan Right		DI low	33
Spare Digital Input 34	L SPST	DI low	34
Spare Digital Input 35	L SPST	DI low	35

Belly Pack Micro
Starboard cmd	Bellypack	ADC 0-5vdc	1
Lateral cmd	Bellypack	ADC 0-5vdc	2
Vertical cmd	Bellypack	ADC 0-5vdc	3
Port cmd	Bellypack	ADC 0-5vdc	4
Auto Heading On/Off	Bellypack	DI low	1
System Kill	Bellypack	DI low	2
Heading Serial Data (output)	Control Sys	LCD input

Toolsled Remote
HFSS Speed Control	Remote	ADC 0-5vdc	1
Index Rev		DI low	1		Toolsled
Index Fwd		DI low	2
Index Stop		DI low	3
Spare Digital Input 4		DI low	4

Port Thruster	Sub Ana Out	DAC +/- 5vdc @10mA
Lateral Thruster	Sub Ana Out
Spare Servo 1	Sub Ana Out
Stbd Thruster	Sub Ana Out
Vertical Thruster	Sub Ana Out
Sony Cam Pan	Sub Ana Out
Sony Cam Tilt	Sub Ana Out
Sony Cam Shoulder	Sub Ana Out

Spare 3000psi Servo	Sub Ana Out
Spare 3000psi Servo	Sub Ana Out
Spare LP Servo	Sub Ana Out

Bellypack Enable	Software	Software enable
Depth Jog Up	Software	Logic only if
Depth Jog Down	Software
Auto Depth	Software	Logic
Auto Heading	Software
Auto Altitude	Software
Auto Cruise	Software

Toolsled enable 240VAC	Switch	Touch
Toolsled enable 120VAC	Switch	Touch
FOG Gyro Power	Switch	Touch
Altimeter #1 Power	Switch	Touch
Altimeter #2 Power	Switch	Touch
Science 120 VAC	Switch	Touch
Core 120 VAC	Switch	Touch
DVL Power	Switch	Touch
Main Camera Power	Switch	Touch
Upper Zoom Camera Power	Switch	Touch
Upper Insite Camera Power	Switch	Touch

Aux Camera 1 Power	FO Menu	Touch
Aux Camera 2 Power	FO Menu	Touch
Still Camera Trigger	FO Menu	Touch
Schilling Power	FO Menu	Touch
Lasers Power	FO Menu	Touch
CTD Power	FO Menu	Touch
CTD Pump Power	FO Menu	Touch
Homer Power	FO Menu	Touch
Sonar Power	FO Menu	Touch
ACM Power	FO Menu	Touch
FO science 24 Power	FO Menu	Touch
Stbd Science 24 Power	FO Menu	Touch
Port Science 24 Power	FO Menu	Touch
FO Science 12 Power	FO Menu	Touch
Stbd Science 12 Power	FO Menu	Touch
Port Science 12 Power	FO Menu	Touch

Upper Camera Pan Left	Switch	PIO96	PA0	25	TB2-47	MPL4205-3	33	P2-1,2,3	2,3,1
Upper Camera Pan Right	Switch	PIO96	PA1	26	TB2-45	MPL4205-3	34	P2-4,5,6	5,6,4
Upper Camera Tilt Up	Switch	PIO96	PA2	27	TB2-43	MPL4205-3	35	P2-7,8,9	8,9,7
Upper Camera Tilt Down	Switch	PIO96	PA3	28	TB2-41	MPL4205-3	36	P2-10,11,12	11,12,10
Still Camera #2 Trigger	Switch	PIO96	PA3	29	TB2-39	MPL4205-3	37	P2-13,14,15	14,15,13
Spare Dry Contact From Pilot Tray	Switch	PIO96	PA5	30	TB2-37	MPL4205-3	38	P2-16,17,18	17,18,16
Spare Dry Contact	Switch	PIO96	PA6	31	TB2-35	MPL4205-3	39	P2-19,20,21	20,21,19
Spare Dry Contact	Switch	PIO96	PA7	32	TB2-33	MPL4205-3	40	P2-22,23,24	23,24,22
GFI A Bit 1	BCD Select	Softwar				MPL4205-3	41	P2-25,26,27	28,29,27
GFI A Bit 2	BCD Select	Softwar				MPL4205-3	42	P2-28,29,30	31,32,30
GFI A Bit 3	BCD Select	Softwar				MPL4205-3	43	P2-31,32,33	34,35,33
Aux Heading Power	Button	Touch				MPL4205-3	44	P2-34,35,36	37,38,36
GFI B Bit 1	BCD Select	Auto				MPL4205-3	45	P2-37,38,39	40,41,39
GFI B Bit 2	BCD Select	Auto				MPL4205-3	46	P2-40,41,42	43,44,42
GFI B Bit 3	BCD Select	Auto				MPL4205-3	47	P2-43,44,45	46,47,45
GFI B Bit 4	BCD Select	Auto				MPL4205-3	48	P2-46,47,49	49,50,48

Spare Valve S2A	Switch	PIO96	PB0	33	TB2-31	GESOUT-1	1	P2-8	TB1-1
Spare Valve S2B	Switch	PIO96	PB1	34	TB2-29	GESOUT-1	2	P2-9	TB1-2
Port Manip Rotate CW	Master	PIO96	PB2	35	TB2-27	GESOUT-1	3	P2-10	TB1-3
Port Manip Rotate CCW	Master	PIO96	PB3	36	TB2-25	GESOUT-1	4	P2-11	TB1-4
Port Jaw Open	Master	PIO96	PB4	37	TB2-23	GESOUT-1	5	P2-12	TB1-5
Port Jaw Close	Master	PIO96	PB5	38	TB2-21	GESOUT-1	6	P2-13	TB1-6
Bypass	Switch	PIO96	PB6	39	TB2-19	GESOUT-1	7	P2-14	TB1-7
Port Manip Enable	Switch	PIO96	PB7	40	TB2-17	GESOUT-1	8	P2-15	TB1-8
Detritus 1A	Selected	PIO96	PC0	41	TB2-15	GESOUT-1	9	P2-16	TB1-19
Detritus 1B	Selected	PIO96	PC1	42	TB2-13	GESOUT-1	10	P2-17	TB1-20
Detritus 2A	Selected	PIO96	PC2	43	TB2-11	GESOUT-1	11	P2-18	TB1-21
Detritus 2B	Selected	PIO96	PC3	44	TB2-9	GESOUT-1	12	P2-19	TB1-22
Detritus 5A	Selected	PIO96	PC4	45	TB2-7	GESOUT-1	13	P2-20	TB1-23
Detritus 5B	Selected	PIO96	PC5	46	TB2-5	GESOUT-1	14	P2-21	TB1-24
Detritus 6A	Selected	PIO96	PC6	47	TB2-3	GESOUT-1	15	P2-22	TB1-25
Detritus 6B	Selected	PIO96	PC7	48	TB2-1	GESOUT-1	16	P2-23	TB1-26

Detritus Selected Input	Joystick	PIO96	PA0	49	TB3-47
Mapped to any Detritus Funct	Finger Sw	PIO96	PA1	50	TB3-45

Detritus 3A	Selected	PIO96	PB0	57	TB3-31	GESOUT-1	17	P3-8	TB1-27
Detritus 3B	Selected	PIO96	PB1	58	TB3-29	GESOUT-1	18	P3-9	TB1-28
Detritus 4A	Selected	PIO96	PB2	59	TB3-27	GESOUT-1	19	P3-10	TB1-29
Detritus 4B	Selected	PIO96	PB3	60	TB3-25	GESOUT-1	20	P3-11	TB1-30
Detritus 7A	Selected	PIO96	PB4	61	TB3-23	GESOUT-1	21	P3-12	TB1-31
Detritus 7B	Selected	PIO96	PB5	62	TB3-21	GESOUT-1	22	P3-13	TB1-32
Detritus 8A	Selected	PIO96	PB6	63	TB3-19	GESOUT-1	23	P3-14	TB1-33
Detritus 8B	Selected	PIO96	PB7	64	TB3-17	GESOUT-1	24	P3-15	TB1-34
Stbd Swing Arm Brake On	Selected	PIO96	PC0	65	TB3-15	GESOUT-1	25	P3-16	TB1-45
Stbd Swing Arm Brake Off	Selected	PIO96	PC1	66	TB3-13	GESOUT-1	26	P3-17	TB1-46
Stbd Swing Arm In	Selected	PIO96	PC2	67	TB3-11	GESOUT-1	27	P3-18	TB1-47
Stbd Swing Arm Out	Selected	PIO96	PC3	68	TB3-9	GESOUT-1	28	P3-19	TB1-48
Drawer Open	Selected	PIO96	PC4	69	TB3-7	GESOUT-1	29	P3-20	TB1-49
Drawer Close	Selected	PIO96	PC5	70	TB3-5	GESOUT-1	30	P3-21	TB1-50
Spare Valve S1A	Selected	PIO96	PC6	71	TB3-3	GESOUT-1	31	P3-22	TB1-51
Spare Valve S1B	Selected	PIO96	PC7	72	TB3-1	GESOUT-1	32	P3-23	TB1-52

Switch mapped to any of the	Rocker	PIO96	PA2	51	TB3-43
Eight above Functions	Switch	PIO96	PA3	52	TB3-41

Toolsled Valve In	Rocker Arm	PIO96	PA4	53	TB3-39
Toolsled Valve Out	Switch	PIO96	PA5	54	TB3-37
Spare Switch Input	Switch	PIO96	PA6	55	TB3-35
Spare Switch Input	Switch	PIO96	PA7	56	TB3-33

Toolsled Valve 1a	Selected					GESOUT-2	1	P2-8	TB2-1
Toolsled Valve 1b	Selected					GESOUT-2	2	P2-9	TB2-2
Toolsled Valve 2a	Selected					GESOUT-2	3	P2-10	TB2-3
Toolsled Valve 2b	Selected					GESOUT-2	4	P2-11	TB2-4
Toolsled Valve 3a	Selected					GESOUT-2	5	P2-12	TB2-5
Toolsled Valve 3b	Selected					GESOUT-2	6	P2-13	TB2-6
Toolsled Valve 4a	Selected					GESOUT-2	7	P2-14	TB2-7
Toolsled Valve 4b	Selected					GESOUT-2	8	P2-15	TB2-8
Toolsled Valve 5a	Selected					GESOUT-2	9	P2-16	TB2-19
Toolsled Valve 5b	Selected					GESOUT-2	10	P2-17	TB2-20
Toolsled Valve 6a	Selected					GESOUT-2	11	P2-18	TB2-21
Toolsled Valve 6b	Selected					GESOUT-2	12	P2-19	TB2-22
Toolsled Valve 7a	Selected					GESOUT-2	13	P2-20	TB2-23
Toolsled Valve 7b	Selected					GESOUT-2	14	P2-21	TB2-24
Toolsled Valve 8a	Selected					GESOUT-2	15	P2-22	TB2-25
Toolsled Valve 8b	Selected					GESOUT-2	16	P2-23	TB2-26

Port lower HID lamp	Light Menu	Touch				GESOUT-2	17	P3-8	TB2-27
Port upper HID lamp	Light Menu	Touch				GESOUT-2	18	P3-9	TB2-28
Port Toolsled HID lamp	Light Menu	Touch				GESOUT-2	19	P3-10	TB2-29
Camera incandescent lamp	Light Menu	Touch				GESOUT-2	20	P3-11	TB2-30
Aft incandescent lamp	Light Menu	Touch				GESOUT-2	21	P3-12	TB2-31
Stbd Toolsled HID lamp	Light Menu	Touch				GESOUT-2	22	P3-13	TB2-32
Stbd lower HID lamp	Light Menu	Touch				GESOUT-2	23	P3-14	TB2-33
Stbd upper HID lamp	Light Menu	Touch				GESOUT-2	24	P3-15	TB2-34
Port lower HID lamp Isolate	Light Menu	Touch				GESOUT-2	25	P3-16	TB2-45
Port upper HID lamp Isolate	Light Menu	Touch				GESOUT-2	26	P3-17	TB2-46
Port Toolsled HID lamp Isolate	Light Menu	Touch				GESOUT-2	27	P3-18	TB2-47
Camera incandescent lamp Isolate	Light Menu	Touch				GESOUT-2	28	P3-19	TB2-48
Aft incandescent lamp Isolate	Light Menu	Touch				GESOUT-2	29	P3-20	TB2-49
Stbd Toolsled HID lamp Isolate	Light Menu	Touch				GESOUT-2	30	P3-21	TB2-50
Stbd lower HID lamp Isolate	Light Menu	Touch				GESOUT-2	31	P3-22	TB2-51
Stbd upper HID lamp Isolate	Light Menu	Touch				GESOUT-2	32	P3-23	TB2-52

Arm Fb Power Supply GFI	Software	Alarm				GFIWATER	1	35	TB12-35
Cam FB Power Supply GFI	Software	Alarm				GFIWATER	2	36	TB12-36
Depth Power Supply GFI	Software	Alarm				GFIWATER	3	37	TB12-37
Doppler Power Supply GFI	Software	Alarm				GFIWATER	4	38	TB12-38
Altimeter Power GFI	Software	Alarm				GFIWATER	5	39	TB12-39
Oil Press Power GFI	Software	Alarm				GFIWATER	6	40	TB12-40
ISIT Power GFI	Software	Alarm				GFIWATER	7	41	TB12-41
Spare GFI	Software	Alarm				GFIWATER	8	42	TB12-42
Spare GFI	Software	Alarm				GFIWATER	9	43	TB12-43
Spare GFI	Software	Alarm				GFIWATER	10	44	TB12-44
Spare GFI	Software	Alarm				GFIWATER	11	45	TB12-45
Spare GFI	Software	Alarm				GFIWATER	12	46	TB12-46
Spare GFI	Software	Alarm				GFIWATER	13	47	TB12-47
Spare GFI	Software	Alarm				GFIWATER	14	48	TB12-48
Spare GFI	Software	Alarm				GFIWATER	15	49	TB12-49
Spare GFI	Software	Alarm				GFIWATER	16	50	TB12-50
					GFM3
FOG Gyro GFI	Sub Dig In	Alarm			12	GESINP	1	P2-8	TB3-1
Valves GFI	Sub Dig In	Alarm			11	GESINP	2	P2-9	TB3-2
Instrument Bus GFI	Sub Dig In	Alarm			10	GESINP	3	P2-10	TB3-3
Logic Bus GFI	Sub Dig In	Alarm			9	GESINP	4	P2-11	TB3-4
Lights GFI	Sub Dig In	Alarm			8	GESINP	5	P2-12	TB3-5
Toolsled 120VAC GFI	Sub Dig In	Alarm			7	GESINP	6	P2-13	TB3-6
Core 120VAC GFI	Sub Dig In	Alarm			6	GESINP	7	P2-14	TB3-7
Main 120VAC GFI	Sub Dig In	Alarm			5	GESINP	8	P2-15	TB3-8
					Gfiwater
Port Manip FB Water	Sub Dig In	Alarm			19,17,18	GESINP	9	P2-16	TB3-9
Aux Heading Sensor Water	Sub Dig In	Alarm			20,15,16	GESINP	10	P2-17	TB3-10
Servo Pack Water	Sub Dig In	Alarm			21,13,14	GESINP	11	P2-18	TB3-11
Thruster Servo Water	Sub Dig In	Alarm			22,11,12	GESINP	12	P2-19	TB3-12
DVL Water Alarm	Sub Dig In	Alarm			23,9,10	GESINP	13	P2-20	TB3-13
Altimeter #1 Water	Sub Dig In	Alarm			24,7,8	GESINP	14	P2-21	TB3-14
Altimeter #2 Water	Sub Dig In	Alarm			25,5,6	GESINP	15	P2-22	TB3-15
Spare Water Alarm	Sub Dig In	Alarm			26,3,4	GESINP	16	P2-23	TB3-16

Control Can Water Alarm	Sub Dig In	Alarm			5,27,28	GESINP	17	P3-8	TB3-42
Fibre-Optic Can Water Alarm	Sub Dig In	Alarm			6,25,26	GESINP	18	P3-9	TB3-41
Gyro Water Alarm	Sub Dig In	Alarm			7,23,24	GESINP	19	P3-10	TB3-40
Transformer Can Water Alarm	Sub Dig In	Alarm			8,21,22	GESINP	20	P3-11	TB3-39
Core/Power Water Alarm	Sub Dig In	Alarm			9,19,20	GESINP	21	P3-12	TB3-38
DVL Can Water Alarm	Sub Dig In	Alarm			10,17,18	GESINP	22	P3-13	TB3-37
Term Can Water Alarm	Sub Dig In	Alarm			11,15,16	GESINP	23	P3-14	TB3-36
Spare Water Alarm	Sub Dig In	Alarm			12,13,14	GESINP	24	P3-15	TB3-35
RPM counter	Sub Dig In	For	The	RPM		GESINP	30	P3-21	TB3-29
Spare Digital In	Sub Dig In					GESINP	31	P3-22	TB3-28
Spare Digital In	Sub Dig In					GESINP	32	P3-23	TB3-27

Sony Pan Sine	Sub Ana Iso	Soft			ANAISO	GESADC-1	11	P2-24	AI1-9
Sony Pan Cosine	Sub Ana Iso	Soft			ANAISO	GESADC-1	12	P2-20	AI1-12
Sony Tilt Sine	Sub Ana Iso	Soft			ANAISO	GESADC-1	13	P2-16	AI1-15
Sony Tilt Cosine	Sub Ana Iso	Soft			ANAISO	GESADC-1	14	P2-12	AI1-18
Sony Shoulder Sine	Sub Ana Iso	Soft			ANAISO	GESADC-1	15	P2-8	AI1-21
Sony Shoulder Cosine	Sub Ana Iso	Soft			ANAISO	GESADC-1	16	P2-4	AI1-24

Altimeter #1	Sub Ana Iso	Soft			Anaiso	GESADC-2	1	P2-31	AI2-29
Hydraulic Oil Level	Sub Ana Iso	Soft			Anaiso	GESADC-2	2	P2-27	AI2-32
Sit Cam Pan FB	Sub Ana Iso	Soft			Anaiso	GESADC-2	3	P2-23	AI2-35
Sit Cam Tilt FB	Sub Ana Iso	Soft			Anaiso	GESADC-2	4	P2-19	AI2-38
HP Oil Press	Sub Ana Iso	Soft			Anaiso	GESADC-2	5	P2-15	AI2-41
LP Oil Press	Sub Ana Iso	Soft			Anaiso	GESADC-2	6	P2-11	AI2-44
Reservoir Pressure	Sub Ana Iso	Soft			Anaiso	GESADC-2	7	P2-7	AI2-47
Motor Comp Pressure	Sub Ana Iso	Soft			Anaiso	GESADC-2	8	P2-3	AI2-50
Tether Comp Pressure	Sub Ana Iso	Soft			Anaiso	GESADC-2	9	P2-32	AI2-3
Electrical Comp Pressure	Sub Ana Iso	Soft			Anaiso	GESADC-2	10	P2-28	AI2-6
Valves 24VDC Power FB	Sub Ana Iso	Soft			Anaiso	GESADC-2	11	P2-24	AI2-9
Isolated 24VDC Power FB	Sub Ana Iso	Soft			Anaiso	GESADC-2	12	P2-20	AI2-12
FOG Analog #1	Sub Ana Iso	Soft			Anaiso	GESADC-2	13	P2-16	AI2-15
FOG Analog #2	Sub Ana Iso	Soft			Anaiso	GESADC-2	14	P2-12	AI2-18
FOG Analog #3	Sub Ana Iso	Soft			Anaiso	GESADC-2	15	P2-8	AI2-21
FOG Analog #4	Sub Ana Iso	Soft			Anaiso	GESADC-2	16	P2-4	AI2-24

Logic 5VDC FB						GESADC-3	1	P2-31	TB6-1
Logic +12VDC FB						GESADC-3	2	P2-27	TB6-2
Can Humidity						GESADC-3	3	P2-23	TB6-3
Logic +15VDC FB						GESADC-3	4	P2-19	TB6-4
Main Ground Fault Analog						GESADC-3	5	P2-15	TB6-5
Aux Ground Fault Analog						GESADC-3	6	P2-11	TB6-6
Can Temperature (Power Supply)						GESADC-3	7	P2-7	TB6-7
Can Temperature (Processor)						GESADC-3	8	P2-3	TB6-8
Aux Head Sine						GESADC-3	9	P2-32	TB6-10
Aux Head Cosine						GESADC3	10	P2-28	TB6-11
Spare Analog Input						GESADC-3	11	P2-24	TB6-12
Spare Analog Input						GESADC-3	12	P2-20	TB6-13
Spare Analog Input						GESADC-3	13	P2-16	TB6-14
Spare Analog Input						GESADC-3	14	P2-12	TB6-15
Spare Analog Input						GESADC-3	15	P2-8	TB6-16
Spare Analog Input						GESADC-3	16	P2-4	TB6-17

Analog Sub Output FB Ch 1	GESDAC-1	P2-2			TB5-1	GESADC-4	1	P2-31	TB7-1
Analog Sub Output FB Ch 2	GESDAC-1	P2-4			TB5-2	GESADC-4	2	P2-27	TB7-2
Analog Sub Output FB Ch 3	GESDAC-1	P2-6			TB5-3	GESADC-4	3	P2-23	TB7-3
Analog Sub Output FB Ch 4	GESDAC-1	P2-8			TB5-4	GESADC-4	4	P2-19	TB7-4
Analog Sub Output FB Ch 5	GESDAC-1	P2-10			TB5-5	GESADC-4	5	P2-15	TB7-5
Analog Sub Output FB Ch 6	GESDAC-1	P2-12			TB5-6	GESADC-4	6	P2-11	TB7-6
Analog Sub Output FB Ch 7	GESDAC-1	P2-14			TB5-7	GESADC-4	7	P2-7	TB7-7
Analog Sub Output FB Ch 8	GESDAC-1	P2-16			TB5-8	GESADC-4	8	P2-3	TB7-8
Analog Sub Output FB Ch 9	GESDAC-2	P2-2			TB5-9	GESADC-4	9	P2-32	TB7-10
Analog Sub Output FB Ch 10	GESDAC-2	P2-4			TB5-10	GESADC-4	10	P2-28	TB7-11
Analog Sub Output FB Ch 11	GESDAC-2	P2-6			TB5-11	GESADC-4	11	P2-24	TB7-12
Analog Sub Output FB Ch 12	GESDAC-2	P2-8			TB5-12	GESADC-4	12	P2-20	TB7-13
Analog Sub Output FB Ch 13	GESDAC-2	P2-10			TB5-13	GESADC-4	13	P2-16	TB7-14
Analog Sub Output FB Ch 14	GESDAC-2	P2-12			TB5-14	GESADC-4	14	P2-12	TB7-15
Analog Sub Output FB Ch 15	GESDAC-2	P2-14			TB5-15	GESADC-4	15	P2-8	TB7-16
Analog Sub Output FB Ch 16	GESDAC-2	P2-16			TB5-16	GESADC-4	16	P2-4	TB7-17

Depth Analog Output	Surf Ana out	AIO16P	DA0		TB5-9
Spare Surf Analog Output	Surf Ana out	AIO16P	DA1		TB5-27
Spare Surf Analog Output	Surf Ana out	AIO16P	DA0		TB6-9
Spare Surf Analog Output	Surf Ana out	AIO16P	DA1		TB6-27

Enable Port Arm	Menu
Enable Port Camera	Menu
Enable	Menu
Enable	Menu
Enable	Menu
Enable	Menu
Enable	Menu
Teleos enable	Menu
Overlay on/off	Menu
Annotation on/off	Menu

Spare Digital Surf In	Switch	PIO96	PB0		TB3-31
Spare Digital Surf In	Switch	PIO96	PB1		TB3-29
Spare Digital Surf In	Switch	PIO96	PB2		TB3-27
Spare Digital Surf In	Switch	PIO96	PB3		TB3-25
Spare Digital Surf In	Switch	PIO96	PB4		TB3-23
Spare Digital Surf In	Switch	PIO96	PB5		TB3-21
Spare Digital Surf In	Switch	PIO96	PB6		TB3-19
Spare Digital Surf In	Switch	PIO96	PB7		TB3-17
Spare Digital Surf In	Switch	PIO96	PC0		TB3-15
Spare Digital Surf In	Switch	PIO96	PC1		TB3-13
Spare Digital Surf In	Switch	PIO96	PC2		TB3-11
Spare Digital Surf In	Switch	PIO96	PC3		TB3-9
Spare Digital Surf In	Switch	PIO96	PC4		TB3-7
Spare Digital Surf In	Switch	PIO96	PC5		TB3-5
Spare Digital Surf In	Switch	PIO96	PC6		TB3-3
Spare Digital Surf In	Switch	PIO96	PC7		TB3-1