## Slide 1: AUV Science Operations Using Terrain Relative Navigation #901500
Stanford TRN research
MBARI development project
MBARI Operations
MBARI development project bridging Stanford TRN research with MBARI Operations
Carried the 2016 Rockfish effort
NASA Iceberg AUV project
  Iceberg AUV
  Wall-following
  TRN

## Slide 2: Terrain-Relative Navigation (TRN)
Measurement
Likelihood Score
Terrain Map
Slide courtesy of Dr. Steve Rock
Low-cost, precision navigation tool
Uses existing acoustic instruments (altimeter, DVL, multi-beam sonar)
Compare the time history of the depth profile with an on-board map
The accuracy of other navigation techniques degrades over time. This makes it difficult to return to a site, e.g. a rock pile
TRN figures out where you are with respect to the terrain
Target boulder
Trajectory without TRN correction
Filter converges
Trajectory specified in map coordinates (before dive)

## Slide 3: 2016 Field Trials
Used Mapping AUV to generate a High resolution map of a suspected deep rockfish habitat
  in a Sanctuary Ecologically Significant Area (SESA)
Deployed MBARI’s “low-cost” MiniROV
  Improved maneuverability, imaging, navigation
  Employed TRN to determine map offset for precise navigation
  Imaged/counted fish in the water column followed by visual ID
    Low-cost swath sonar for fish detection

## Slide 4: Rockfish in the Water Column Low-cost Multi-beam Sonar

## Slide 5: MiniROV footage “Rare” and Rebuilding Species